LIGO Laboratory / LIGO Scientific Collaboration

LIGO-T040136-01-D	ADVANCED LIGO	20 May 2004

Seismic Isolation System (SEI)
Payload Mass Properties

Dennis Coyne

Distribution of this document:

LIGO Science Collaboration

This is an internal working note

of the LIGO Project.

| California Institute of Technology LIGO Project – MS 18-34 1200 E. California Blvd. Pasadena, CA 91125 Phone (626) 395-2129 Fax (626) 304-9834 E-mail: info@ligo.caltech.edu | Massachusetts Institute of Technology LIGO Project – NW17-161 175 Albany St Cambridge, MA 02139 Phone (617) 253-4824 Fax (617) 253-7014 E-mail: info@ligo.mit.edu |
| --- | --- |
| LIGO Hanford Observatory P.O. Box 1970 Mail Stop S9-02 Richland WA 99352 Phone 509-372-8106 Fax 509-372-8137 | LIGO Livingston Observatory P.O. Box 940 Livingston, LA 70754 Phone 225-686-3100 Fax 225-686-7189 |

http://www.ligo.caltech.edu/

Revision 00:	Mar 2004, Initial draft release

Revision 01:	Release in conjunction with E030179-A for the AdL SEI structural design requirements.

# Purpose

The purpose of this memo is to document the mass property limits for the payloads on the SEI platforms for advanced LIGO, which will be defined in the interface control document (ICD, which is to be written). This document provides the basis for establishing the requirements for the AdL SEI structural design requirements. Parameters had to be estimated for the purpose of establishing a set of interface requirements. As the designs mature, the interface requirements can be re-evaluated based upon better design information and the basic methodology and considerations given in this document.

A companion document, will be used to track the current estimates of payload mass properties and compare them to the ICD limits.

# Layouts

Layouts are depicted in the attached Figures.

# Assembly Mass Properties

The assemblies that comprise the AdL in-chamber payload are listed in the following Table, with their estimated masses. These mass estimates for the individual assembly/component items are used with the layouts to estimate the mass properties of the payload ensembles for each optics table (particularly the total mass and the first moments of mass about the table center).

# Optics Table Mass Properties

The mass properties for each chamber are listed in the following Tables. The payloads are separated into HAM Chamber and BSC chamber payloads.