LIGO Laboratory / LIGO Scientific Collaboration

LIGO-E080493-v2	LIGO	April 3, 2009

Output Mode Cleaner As-Built Description

D. Bridges, C. Echols, M. Meyer

Distribution of this document:

LIGO Science Collaboration

This is an internal working note

of the LIGO Project.

| California Institute of Technology LIGO Project – MS 18-34 1200 E. California Blvd. Pasadena, CA 91125 Phone (626) 395-2129 Fax (626) 304-9834 E-mail: info@ligo.caltech.edu | Massachusetts Institute of Technology LIGO Project – NW17-161 175 Albany St Cambridge, MA 02139 Phone (617) 253-4824 Fax (617) 253-7014 E-mail: info@ligo.mit.edu |
| --- | --- |
| LIGO Hanford Observatory P.O. Box 1970 Mail Stop S9-02 Richland WA 99352 Phone 509-372-8106 Fax 509-372-8137 | LIGO Livingston Observatory P.O. Box 940 Livingston, LA 70754 Phone 225-686-3100 Fax 225-686-7189 |

http://www.ligo.caltech.edu/

# Introduction

This note is intended to document the as-built configuration of the output mode cleaners (OMCs) installed at LLO and LHO.

# LLO Output Mode Cleaner

The figure and accompanying table below show the layout and serial numbers of the blades and OSEMs for the as-built output mode cleaner at the Hanford Observatory.

Figure 1: OMC Blade and OSEM Layout

Table 1: LLO OMC Blade and OSEM Part and Serial Numbers

| Blade | Part/Serial Number |  | OSEM | Part/Serial Number |
| --- | --- | --- | --- | --- |
| A | D020205-A S/N 1L 3.5 deg |  | Top 1 | D060108-B S/N 013 or 009? |
| B | D020205-A S/N 2L 3.5 deg |  | Top 2 | D060108-B S/N 010 |
| C | D020201-A S/N 13 or 3L 2.5 deg |  | Top 3 | D060108-B S/N 012 or 015 |
| D | D020201-A S/N 10S 3 deg |  | Left | D060108-B S/N 008 |
| E | D020201-A S/N ? 3.5 deg |  | Right | D060108-B S/N 006 |
| F | D020201-A S/N 0 or 3 3 deg |  | Side | D060108-B S/N 011 |

The upper blade clamps are part numbers D020690 (upper side) and D030466 (lower side), which have a 3.5 degree angle.  The lower blade clamps are part numbers X (upper side) and D020336 (lower side) (2.5 degree angle), X (upper side) and X (lower side) (3 degree angle), and X (upper side) and X (lower side) (3.5 degree angle).

The upper wire length is 249.95 mm and the lower wire length is 246.2 mm.

Additional masses totaled X grams on the upper mass and X grams on the fused silica bench.  Description of placement of masses – pictures?

# LHO Output Mode Cleaner

Figure 1 above and accompanying table below show the layout and serial numbers of the blades and OSEMs for the as-built output mode cleaner at the Hanford Observatory.

Table 2: LHO OMC Blade and OSEM Part and Serial Numbers

| Blade | Part/Serial Number |  | OSEM | Part/Serial Number |
| --- | --- | --- | --- | --- |
| A | D080018-A S/N 2 |  | Top 1 | D060108-B S/N 040 |
| B | D080018-A S/N 4 |  | Top 2 | D060108-B S/N 041 |
| C | D080019-A S/N 004 |  | Top 3 | D060108-B S/N 042 |
| D | D080019-A S/N 007 |  | Left | D060108-B S/N 043 |
| E | D080019-A S/N 002 |  | Right | D060108-B S/N 044 |
| F | D080019-A S/N 003 |  | Side | D060108-B S/N 045 |

The upper blade clamps are part numbers D020312 (upper side) and D030463 (lower side), which have a 2.0 degree angle.  The lower blade clamps are part numbers D070031 (upper side) and D020308 (lower side), which have a 0.0 degree angle, except for blade number 7 (labeled D in Figure 1) which are part numbers D020337 and D020333 (lower side), which have a 0.5 degree angle.

The upper wire length is 249.6 mm and the lower wire length is 251.8 mm.

Additional masses totaled 0 grams (no additional mass) on the upper mass and X grams on the fused silica bench.  X (more) grams was placed on the same corner as blade D and X (less) grams was place on the same corner as blade F (see Figures 2 and 3).

Figure 2: Illustration of Additional Mass on Glass Bench

Figure 3: Installation Picture Showing Orientation of Additional Mass

# Part Differences Between the LLO and LHO OMCs

The two output mode cleaner suspensions have some differences in the parts used in their construction.  Table 3 below outlines these differences:

Table 3: Differences Between LLO and LHO OMCs

| Part Number | Part Name | Description of Differences |
| --- | --- | --- |
| D060296 | Structural Weldment | LLO version made using Rev A, LHO version using Rev B. Majority of changes related to making the structure easier to weld and limiting the amount of warping caused by the welding process. |
| D070147 | Top Blade Guard Riser | LHO version includes helicoils to facilitate repeated assembly/disassembly. |
| D020205/D080018 | Upper Blades | LLO version has D020205 blades (spares from the iLIGO IMC); LHO version has D080018 blades, designed for the OMC. |
| D020201/D080019 | Lower Blades | LLO version has D020201 blades (spares from the iLIGO IMC); LHO version has D080019 blades, designed for the OMC. |
| D030449 | Rotational Adjuster Push Plate | Part drawings call out 300-series stainless steel. LLO version is, or may be, made from 303 stainless steel, which has been deemed not UHV-compatible by L080044-v1. LHO version is made from non-303 stainless steel. |
| D030450 | Rotational Adjuster Pull Plate |  |
| D030459 | Upper Blade Clamp, Lower Side, 0.0 Degree |  |
| D020116 | Upper Blade Clamp, Upper Side, 0.0 Degree |  |
| D070022 | Upper Blade Wire Clamp |  |
| D020680 | Upper Blade Clamp Lower Side Shim |  |
| D030042 | Upper Blade Wire Clamp Plate |  |
| D020309 | Upper Mass Wire Clamp Plate |  |
| D020139 | Upper Mass Wire Clamp Plate |  |
| D060491 | Upper Mass Main Section |  |
| D060503 | Upper Mass Pitch Insert |  |
| D070031 | Lower Blade Wire Clamp |  |
| D020133 | Lower Blade Wire Clamp Plate |  |