## Design Specifications for the OMC Suspension

## D Coyne, P Fritschel, J Romie, N A Robertson

## Updated 13 Aug 2007

## Further updated with comments for review 31 Aug 2007 DCC#: T070189-01-R

## Further updated for FDR Feb 2009 by NAR (updates in italics) T070189-v1

## Further updated by NAR Feb 7th 2014, updates in red. T070189-v3

## Note I am calling this v3 as there is confusion in numbering on the DCC between v1 and v2.

| Property | Value or Description | Comment | Comments added for 2nd prototype readiness review Aug/ Sept 2007 Further comments Feb 2009 |
| --- | --- | --- | --- |
| Baseplate Dimensions | 450 mm x 150 mm x 40 mm | Baseplate only | Actual silica bench (aka baseplate) 450 mm x 150 mm x 39 mm aLIGO size 450mm x 150mm x 41.275 mm (D1200105) |
| Payload Mass | 6.0 kg Current design has mass ~ 6.9 kg ALIGO Target 7.0 kg (ref L0900064, pg 3) | Baseplate plus components | Design allows for +/-10% (i.e. maximum of 6.6 kg) Blades redesigned for higher mass Actual ~ 7.2 kg (in ICS entries) |
| Baseplate Material | Light-weighted aluminum, or fused silica | Baseplate provided by ISC | Al bench suspended and tested, silica bench still to be suspended Silica benches now suspended |
| Baseplate internal modes | First mode > 1000 Hz | Get it above IFO noise minimum and violin mode fundamental | FEA shows ~ 1100 Hz (see supporting documentation) |
| Isolation | Double pendulum, with two stages of blades for vertical isolation | Isolation of a double is estimated to be sufficient, but analysis of baseplate vibration needs to be written down | Isolation at 10 Hz Long: ~ 5 x 10^-4 Vert: ~ 4 x 10^-3 (exact values depend on level of damping and details of bench design) |
| Solid-body mode eigenfrequencies | 0.8-2 Hz | This is a guideline only. Modes involving stretching of the bottom stage wires will of course be higher. | Actual frequencies are in range 0.5 Hz (lower yaw mode) to ~ 7 Hz (higher roll mode). Details on OMC Suspension wiki site under “Testing” link Final values in SUS Ops manual under OMCS https://awiki.ligo-wa.caltech.edu/aLIGO/Suspensions/OpsManual |
| Suspension fiber type | Steel - music wire |  |  |
| Beam height | 101.6 mm +/- 2 mm[4.0 inches] above HAM optics table; 25.4 mm +/- 2 mm [1.0 inch] above baseplate Current design has beam 20 mm below the baseplate | same as iLIGO ISC table beam height | Beam is now below bench, not above |
| Suspension structure footprint | TBD | Keep as small as practical, to leave as much room as possible on HAM table for other components |  |
| Structure resonances | First mode > 150 Hz |  | Lowest freq. is ~ 140 Hz (see supporting documentation) |
| Suspension structure height | 725 mm ? | This is not really a spec that needs to defined here | Structure height has been looked at in HAM 6 layout to check it doesn’t hit ceiling. (see supporting documentation) |
| Suspension point locations on baseplate | 4 points | Along (150mm) width, as close to edges as possible; along length, position points to reduce plate motion (e.g., 22% of length from ends minimizes static deflection) | Susp. points moved in from edge in width direction to reduce higher pitch mode from 9 Hz to ~ 4 Hz. Susp points are at 20% of length from ends in the long axis direction. Updated – see FDD T0900060-v2 or above |
| Suspension point design | TBD | Slots in plate, or pegs inserted in side of plate | Countersunk through holes chosen for ease of manufacture of silica bench Updated – see FDD T0900060-v2 or above |
| Local damping | Active, 6 DOF | Same as IMC |  |
| OSEM type | TBD | Probably 'Birmingham OSEMs' | B’ham OSEMS used |
| Baseplate positioning & pointing range (DC) | Few hundred microns, few hundred micro-rads | Guesstimate -- what's the IMC control range? | Pointing range using B’ham OSEMs of order 2 milliradians in roll, pitch and yaw |
| Actuator force spectrum | TBD | Not expected to be critical |  |
| Actuator noise limits | TBD | Not expected to be difficult |  |
| Optical line of sight/clearance reqs |  |  |  |
| Electrical wiring to baseplate | TBD | No., gauge, type, connector type |  |
| Accuracy of mechanical pitch and yaw positioning |  |  |  |
| Accuracy of mechanical vertical positioning |  |  |  |
| Beam dumps on SUS hardware | provide mounting holes on uprights, at beam height |  | Still to be specified |
| Mechanical stops for baseplate |  |  | In place – see detailed mechanical drawings |