All-Sky Burst Searches for Gravitational Waves
at High Frequencies
F. Salemi, AEI Hannover
for the Ligo Scientific Collaboration and the Virgo Collaboration
AMALDI8 Conference, New York
23 June '09
Document Number LIGO-G0900529-v7

---
High Frequency (HF) Burst Searches
During S5/VSR1 we have conducted all-sky burst searches extending the frequency range up to 6 kHz (see S5y1 high-f: arXiv:0904.4910	S5y1 low-f: arXiv:0905.0020 )
PRO: use existing pipelines, less glitchy data, search a frequency with a large number of potential sources (see next slide), Virgo effectively comparable to H1 and L1
CONTRA: Lower sensitivity range of detectors
2 independent searches: the first year of S5 (S5Y1) has been analyzed with a correlation follow-up of coincident single detector triggers(Q-pipeline + CorrPower), the second year of S5 + VSR1 (S5Y2/VSR1) has been analyzed with a coherent pipeline (cWB)
Search bandwidth:
1-6 kHz
> 1 kHz to keep an overlap with standard searches (<2kHz)‏
< 6 kHz technical bound set by LIGO calibration
HF
[Speaker Notes: Cambiare con i colori standard????????]

---
Transient GW sources at a few kHz
Neutron star collapse scenarios resulting in rotating black holes
L. Baiotti et al. Phys Rev. Lett. 99, 141101 (2007).
L. Baiotti et al. Class. Quant. Grav. 24, S187 (2007).
Nonaxisymmetric hypermassive neutron stars resulting from neutron star-neutron star mergers
R. Oechslin and H.-T. Janka, Phys. Rev. Lett. 99, 121102 (2007).
Neutron star f-modes
B.F. Schutz, Class. Quant. Grav. 16, A131 (1999).
Neutron stars undergoing torque-free precession
J.G. Jernigan, AIP Conf. Proc. 586, 805 (2001).
Low-mass black hole mergers
K.T. Inoue and T. Tanaka, Phys. Rev. Lett. 91, 021101 (2003).
SGRs
J.E. Horvath, Modern Physics Lett. A 20, 2799 (2005).
Baiotti et al. waveform

---
S5Y1 HF search: intro
- Based on QPipeline, with cross-correlation followup
- Run on triple-coincident	H1, H2 and L1 data (155.5 days)
- Also check for loud events	in H1H2 only time
- Tuned on background sets from 100 lags of L1 w.r.t. H1H2
- Cuts on single site energy, cross-correlation factor Γ corresponding to a false alarm probability of ~10% (~0.25 year -1)
- Used similar data quality/vetoes as low frequency
See Brennan Hughey's poster for more details

---
S5Y1 HF search: trigger distributions
Cumulative distributions of sub-threshold
events for
Cross-correlation measure CorrPower
Hanford energy distribution
Livingston energy distribution

---
S5Y1 HF search: Upper Limits
90% Confidence Level Upper limit curves for various Sine-Gaussians Q=9 (adjusted for uncertainties)

---
S5Y2/VSR1 HF search: cWB Pipeline
Coherent Waveburst: event selection and reconstruction by constrained maximization of Likelihood.
Main settings specific to this search:
Inputs h(t) resampled at 12.8 kHz
Multi-resolution: 400Hz x 1/800 s, 200Hz x 1/400 s, ..., 12.5Hz x 1/25 s
Search for events (clusters) limited within 1.28-6.0 kHz
Two main test-statistics to select events for detection:
Network correlation coefficient:
rho:
Netcc = {abs{E_{cor}}} over {abs{E_{cor}} + NullEnergy} < 1
where SNR^2 = E_{cor} +E_{incoherent}
%rho = sqrt{{E_{cor} Netcc} over { Ndetector}}

---
RHO vs NetCC: background+signals (SGQ9)
L1H1H2
V1H1H2L1
Glitches
Glitches
Background
Background
Background scatterplots (black) compared to recovered injections color-density plots for V1H1H2L1 (left) and L1H1H2 (right)
Adding a fourth detector (Virgo) helps in reducing the significance of large single detector glitches (i.e. large rho, small netcc )
Injected Signals
Injected Signals

---
Tuning sample with SGQ9: V1H1H2L1
Blind null hypothesis test with target false alarm at ~5 E-9 Hz = 1/6 years
This level is satisfactory for a preliminary selection of candidate events, but not enough to qualify a GW candidate
The tuning procedure sets the thresholds in netcc and ρ as 2 straight orthogonal lines by choosing among a small number of finite steps increments (0.05 for netcc and 0.1 for ρ)
The algorithm: for a given False Alarm rate, choose the combination {netcc; ρ} which produces the lowest SGQ9 Hrss90%: in this case, {0.6;4.3}

---
S5/VSR1 HF search: background and signal injections
Background (BKG) and False Alarm Rate (FAR) estimation:
Efficiency studies:
SineGaussian Q9 (13 central frequencies): all-purpose testing set
SineGaussian waveforms Q 3 and Q 100 linearly polarized :	test sensitivity to shorter/longer waveforms
White Noise Bursts with band/duration =100 Hz / 0.01 s and 1000 Hz / 0.1 s :	test “extreme case” efficiencies
Ringdown waveforms tau=0.2 s linear and circularly polarized:	sensitivity to NS f-modes related to Soft Gamma Repeaters
Numerical SN core collapse to BH, waveforms D1 and D4	(Baiotti et al., PRD 71, 024035 (2005) )
RingDown Q9 linearly and circularly polarized:	calibrate the sensitivity to short Damped Sinusoids with respect to Sine Gaussian
TOT = 244.5 days	10% FA prob.

---
S5Y2/VSR1 HF search: efficiency studies
SineGaussiansQ9
a. u.
Detection efficiency varies for the different injection frequencies, scaling with detector sensitivity, as expected.
The asymptotic efficiency (hrss90%) results are better by a factor 40% for the network including Virgo, due to the better sky coverage achieved with a 3rd site.
Various Waveforms at ~3 kHz (different polarization and bandwidth) show the typical range of variation of the efficiency curves.
a. u.

---
S5/VSR1: Calibration systematics (1/2)
Pipelines used LIGO h(t) data before the final release was available.
Main calibration systematics:
LIGOs (frequency dependent)
Mean offset = (V3-V4)/V4 for h(f)	Standard deviation on HrecV4 h(f)
Virgo
Mean offset = 0	Standard deviation on HrecV2 < 6%
Resulting Correction to 64 – 2048 Hz searches and to S5Y1 HF search:
constant factor on hrss, i.e. scale the hrss values in the the upper limit by +11% for
all detector configurations and waveforms

---
S5/VSR1: Calibration systematics (2/2)
2 – 6 kHz search: situation is more critical w.r.t Low Frequency due to:
- higher calibration uncertainties (H1 sigma on amplitude goes up to 24% in 4-6kHz)
- coherent search  also differential mis-calibration of detectors are important (in particular H1 vs H2)
Monte Carlo methods are needed to fold the effect of calibration systematics in the detection efficiency
1. model amplitude relative systematic uncertainties as gaussian distributed at each detector (and frequency band)
2. perform MDC injections on reference data (JW1) with a relative correction of the injected amplitude sampled from the models (independent samples per each injection)
3. compute the resulting detection efficiency
4. rescale the results from reference data (JW1) to the entire observation time
this estimate of detection efficiency marginalized over the systematic uncertainties should be used to produce HF upper limits
Preliminary results
- V1H1H2L1 SineGaussian Q9 detection efficiency curves including calibration systematics: the increase of hrss50% is in the range 3%-8%
- L1H1H2 SineGaussian Q9 detection efficiency curves including calibration systematics: the increase of hrss50% is in the range 4%-12%

---
Summary
LIGO/Virgo burst analysis extended up to 6 kHZ
The S5Y1 HF: no GW candidates
S5Y1 HF Burst Search paper available on arXiv: gr-qc/0904.4910
S5Y2/VSR1 HF Burst Search with cWB
We are working on folding in Calibration systematics via MonteCarlo sofware injections
Internal review expected to be completed during next few months
Results to be published within the S5Y2/VSR1 burst paper (together with low freq burst searches)
We will continue to look for HF signals with cWB in the off-line searches during S6
[Speaker Notes: Cambiare con i colori standard????????]