- Helicoil,flip then dowel D0900894, move to test-stand

  - 309x   3/8-16 x2d helicoils

  - 12x  1/4-20 x2d helicoils

  - 3x  ½ X1.25 dowels

- Helicoil, dowel D0900895

  - 15x  1/4-20 x2 DIA Helicoils

  - 54x  3/8-16 x 2 DIA Helicoils

  - 12x  5/8-11 x 2 DIA Helicoils

  - 24x  3/8” x 1” dowel pins

  - 6x  1/2” x 1.25” dowel pins

- Mate D0900895 to D0900894, east edge of D0900895 is top of fig. 20

  - 142x  ½-13 x 3 SHCS and vented washers

  - Run  feeler gage at seams

- Helicoil, dowel D0901499 spring post

  - 4x  1/4-20 x 2d helicoils

  - 2x  3/8 x 1” dowels

- Install D0901499 Spring post

  - 4x  5/8-11 x 2.5” HHCS and vented washers

  - Install 6x St0-1 barrel nut bars

- Helicoil D091516 Optical table on granite table

  - 3244x  3/8-16 x 2d helicoils

  - 18x  1/4-20 x 2d helicoils

- Flip D0901516

  - Dowels

  - 3x  ½x1.25 dowels

- Install cover plates  3x (D0901842, D0901843, D0901844) in D0901516

  - 60x  3/8-16 x 1” SHCS and vented washers

  - 15x  1/4-20 x 5/8 SHCS and vented washers

- Put D0901517 Up facing optical table on HAM assembly stand

- Dowel and Helicoil D0901517

  - 36x  3/8-16 x 2d helicoils

  - 33x  3/8 x1” dowels (3 on underside)

- Mate D0901516 & D0901517

  - 306x  3/8-16 x 2” SHCS and vented washers

- Install 3x D1001110 St 0-2 alignment pins

  - 9x  3/8-16 x 1.5” SHCS

- Install 3x D1001111 St 0-2 alignment washers on St 0 on test-stand

- Install optical table assembly, orient so that vent grooves run east-west on test-stand

  - 3x  1/2-13 x 6” SHCS in D1001110 slignment pins pins

  - Install 12x St1-2 Barrel Nut-bars

- Put D0902279 on granite table, bottom up, dowel

  - 6x  3/8 x 1 dowels for D0902282 masses

  - 12x  3/8 x 5/8 dowels for lockers

- Flip helicoil and dowel

  - 21x  ¼-20x2d helicoils

  - 27x  3/8-16 x2d dowels

- Suspend D0902279 (crane or forklift), install 3x D0902280 Ballast masses by lowering plate and aligning dowels with masses

  - 12x  3/8-16 x 1.25” SHCS and vented washers

- Place plate assembly on top of 3x 4-6” cribbing blocks on granite table

- Install D0902272 3x Block links

  - 42x  3/8-16 x 1.25 SHCS and vented washers

- Install D0902282 3x Inner Walls

  - 36x  3/8-16 x 1.25 SHCS and vented washers

  - Run feeler gage at seams

- Install 3x D0902271 Angled Hex Wall

  - 15x  3/8-16 x 1.25 SHCS and vented washers

  - Check gaps between Hex Wall and Block links, make sure they are even, run a feeler gage at seams

- Helicoil and Dowel 3x D0902274

  - 6x  3/8 x 1 dowels

  - 15x  3/8-16 x 2d helicoils

  - 18x  3/8-16 x 1.5d helicoils (for st1 doors)

- Install 3x D0902274

  - 15x  3/8-16 x 1.25 SHCS and vented washers

- Helicoil and dowel 3x D0902278

  - 30x  1/4-20 x2d helicoils

  - 27x  3/8-16 x 1.5d helicoils (for st1 door)

  - 6x  3/8-16 x 2d helicoils

  - 3x  3/8 x 1 dowels

- Install 3x D0902278

  - 21x  3/8-16 x 1.25 SHCS

- Helicoil and dowel 3x D0902276

  - 12x  3/8-16 x 2d helicoils

- Helicoil and dowel 3x D0902277

  - 18x  5/16-18 x 2d helicoils

  - 3x  3/8 x 1 dowels

- Build 3x Flexure Bracket Assembly

  - 6x  1/2-13 x 4 SHCS

  - 12x  1/2-13 x 3.25 SHCS

  - 6x  1/2-13 x 1 AG SHCS

  - 24x  Vented washers

- Install 3x Flexure Bracket Assembly

  - 12x  1/2-13 x 1.5 SHCS

  - 6x  1/2-13 x 2.25 AG SHCS

  - 18x  vented washers

- Install 3x D1001112 Stage 1-2 alignment pins into D902279

  - 6x 3/8-16 x 1.25 SHCS

- Install  3x D1001113 St1-2 alignment washers and move St1 assembly to test-stand

  - 3x  3/8-16 x 3 SHCS (thru pins)

- Helicoil and dowel 3x D0901521

  - 6x  1/4-20 x 2d helicoils

  - 6x  3/8-16 x2d helicoils

  - 6x  3/8-16 x 1d helicoils (outside edge)

  - 6x  ¼ x5/8 dowels

  - 3x  3/8 x 1 dowels

- Install 3x D0901521

  - 7x  3/8-16 x 2” SHCS and vented washers

- Install 3x D0901523

  - 9x  3/8-16 x 1.25 SHCS

  - 18x  3/8-16 x 2 SHCS

  - 27x  vented washers

  - Snug bottoms, snug sides, torque

- Helicoil and dowel 3x D0901522

  - 6x  3/8-16x 2d helicoils

  - 3x  3/8 x 1 dowels

- Install 3x  D0901522

  - 9x  3/8-16 x 1.25 SHCS

  - 18x  3/8-16 x 2 SHCS

  - vented washers

  - Push D0901522 to contact D0901523, snug bottoms, snug sides, torque

- Install 3x D0901524

  - 6x  3/8-16 x 1.25 SHCS

  - 21x  3/8-16 x 2 SHCS

  - vented washers

  - push against D0901521 and D0901522, snug bottoms, snug sides, torque

- Install 3x D0901525

  - 12x  3/8-16 x 2 SHCS and vented washers

- Install 6x D0901538 between D0901524 and D0901525

  - 42x  3/8-16 x 1.5 SHCS and vented washers

  - Snug bolts, check that D0901538 are sitting flush, torque

- Helicoil and dowel D0901520

  - 9x  1/4-20 x 2d helicoils

  - 15x  3/8-16 x 2d helicoils

  - 6x  ¼ x 5/8 dowels

  - 30x  3/8 x 1 dowels

  - 3x  3/8 x 1 thread/vented dowels (inner GS-13 alignment dowel

- Install D0901520

  - 105x  3/8-16 x 1.25 SHCS and vented washers

- Install 6x D0902133 Hex Wall Gussets  on D0901520

  - 6x  3/8-16 x 1.25 SHCS

  - 6x 3/8-16 x 2.25 SHCS

  - Vented washers

- Dowel 3x D0901530

  - 6x  3/8 x 1 Dowels

  - Mate to 3x D0901526

    - 18x  3/8-16 x 1 SHCS

- Install D0901526 Assemblies on D0901520

  - 12x  3/8-16 x 1.25 SHCS to D0902133 gussets

  - 18x  3/8-16 x 1.5 SHCS to D0901520

- Dowel 3x D0901528 Small Hex Wall Adapters

  - 6x  3/8 x 1 dowels

  - Attach to D0901531 Small Hex Wall

    - 12x  3/8-16 x 1 SHCS and vented washers

- Install 3x Small Hex Wall assemblies

  - 12x  3/8-16 x 1.5 SHCS and vented washers

- Install 6x D0901538 Hex Wall Brackets

  - 42x  3/8-16x1.5 SHCS and vented washers

- Helicoil and dowel D0902273

  - 6x  1/4-20 x 2d helicoils

  - 24x  3/8-16 x 2d

  - 3x  3/8 x 1 dowels

- Install D0902273

  - Orient so that corner 1 is on west side of test-stand

  - 120x  3/8-16 x 1.25 SHCS and vented washers

- Helicoil D0902503 close-out plate cover

  - 6x  3/8-16 x 1d helicoils

- Install D0902503

  - 405 1/4-20 x .75 SHCS and vented washers

- Install 3x D0902443  St1 Back rib

  - 36x 3/8-16 x 1.5 SHCS and vented washers

  - snug bolts, check that rib sits flush at both contact points, torque

- Install 6x D0902441 St1 Side Ribs

  - 84x  3/8-16 x 1.5 SHCS and vented washers

  - snug bolts, check that rib sits flush at both contact points, torque

- Helicoil and dowel 3x D0901533 upper outer wall

  - 6x  ½ x 4 dowels

  - 6x 1/2-13 x 4 HHCS and vented washers

  - 6x 1/2-13 AG nuts

  - 3x  3/8 x 1 dowels

  - 24x  3/8 x 1d helicoils

- Install D0901533 walls

  - 18x  3/8-16 x 1.25 SHCS and vented washers

- Install D0901518 Keel plate

  - 51x  3/8-16 x 2 SHCS and vented washers

  - Add ½ x 1.25 dowels after install

- Put D0901519 Keel Plate on Granite table

  - 448x  3/8-16 x 1d helicoils

  - 24x  1/4-20 x 2d helicoils

  - 18x  5/16-24 x 2d helicoils

- Install D0901519

  - Orient so that helicoiled holes form rows at 45 deg to st1 corner 1 (Fig 88, west is on the bottom of the image, the dashed lines are parallel to the test-stand)

  - 127x  3/8-16 x 2 SHCS and vented washers

- Install 12x D0901539 Outer wall Gussets

  - 48x  3/8-16 x 1.25 SHCS

  - 24x  3/8-16 x 2 SHCS

  - vented washers

- Install Horizontal 3x GS-13's

  - Install custom nuts on D1100086 Stiffener

    - 36x  #6 AG SHCS and vented washers

  - Put stiffener plate D110086 on pod with 3 5/16-24 x 1 AG SHCS and 5/16 vented washer with one 2mm and one 3 mm Misumi washer under each bolt (9 of each, for all 3 pods)

  - Use teflon slide blocks, note faint “up” arrows on ends

  - Slide GS-13 in until left side slides over 3/8 dowel in st2 left radial wall.

  - Slide long 3/8 dowel in alignment hole in left radial wall, and align GS-13 pod base, move teflon blocks so they are easy to grab, ok to remove one, after dowels are in

    - 12x  5/16-24 x 1.25 AG SHCS and vented washers

  - Slide teflon block(s) out

  - Install 3x D0902583 spacer

    - 9x 5/16-24 x 1.25 AG SHCS and vented washers

- Install 3x fine horizontal actuators

  - 6x 3/8-16 x 1.25 SHCS and vented washers

  - Install 3x D0902162 to actuator with 1/2-13 x 2.5 HHCS, vented washer and custom spherical washers: D0902156, D1000678, D1000679, D0902157

  - Attach D0902162 to St1 with 3/8-16 x 1.25 SHCS and special thick, smaller OD 3/8 washers. Multiple rounds of torquing one set of bolts, releasing and retorquing perpendicular bolts.

  - Loosen tooling bar, check that actuator doesn't move, remove tooling bar. If actuator shifts, reconnect tooling bar, check that alignment dowels still slide in. Try again.