# LASER INTERFEROMETER GRAVITATIONAL WAVE OBSERVATORY

# -LIGO-

# CALIFORNIA INSTITUTE OF TECHNOLOGY

# MASSACHUSETTS INSTITUTE OF TECHNOLOGY

| Document Type Test Procedure and Results | DCC Number LIGO-T0900558-v1 | Date 18 August, 2009 |
| --- | --- | --- |
| Reading out a Trillium 240 With an STS-2 Interface Chassis |
| Ben Abbott, Daniel Clark |

Distribution of this draft: NSF reviewers, LIGO scientists

This is an internal working note of the LIGO Laboratory

California Institute of Technology	Massachusetts Institute of Technology

LIGO Project – MS 18-33	LIGO Project – MS 20B-145

Pasadena, CA 91125	Cambridge, MA 01239

Phone (626) 395-2129	Phone (617) 253-4824

Fax (626) 304-9834	Fax (617) 253-7014

E-mail: info@ligo.caltech.edu	E-mail: info@ligo.mit.edu

www:  http://www.ligo.caltech.edu/

LIGO-T0900346-v1

Performed by: ______________

Date: ______________

Board Serial Number: ______________________

- Overview

The Streckheisen STS-2 and Trillium 240 triaxial seismometers are similar enough that one can read out T240 signals through an STS-2 Interface after the addition of a single piece of hardware.  These are the instructions on how to do that.

- Necessary Equipment

  - Trillium 240 Seismometer

  - STS-2 Interface Chassis, that is hooked into an ADC through an AA chassis.

  - STS-2 to T240 Interface Chassis (D0901489)

  - T240 in-pod cable which has the round military connector on one end, and a 25-pin Dsub on the other (for the pinout of this cable, see Appendix A)

  - Patch cable between the STS2-to-T240 Interface Chassis (D0901489), and the STS-2 Interface Chassis (D080535-v2)

  - 9-pin Dsub F-F cable to connect your computer’s serial out port to the STS2-to-T240 Interface Chassis.  DO NOT USE A NULL MODEM CABLE.

- Preliminaries

  - Hook up the seismometer to the “STS-2 to T240” Chassis where it reads “to Trillium Flange”.  (Since the interface’s cable, and the in-pod cable are through two flanges, the pin flip is cancelled, and you don’t need to flip any cables to read out the Trillium in this configuration.)

  - Connect the STS-2 Interface to the T240 Interface with the 50-pin Dsub to 25-pin Dsub patch cable.

  - Turn on the STS-2 Interface.

  - At this point you should see some signs of life from the ADC channels.

- RS232 Readout

  - Have Daniel Clark email you the Multi-Threaded TTY program, and launch it.  The settings at the top of the GUI should be set to the following:

Port             COM1

BAUD         9600

PARITY      NONE

Data Bits     8

Stop Bits     1

The following check boxes should all be checked:

√  Local Echo

√  Display Errors

√  CR=> CR/LF

√  Autowrap

  - The XYZ/UVW switch on the STS2-toT240 Interface Chassis (D0901489) should be set to XYZ.  If it is set to UVW, it sets the RS232 TX line high, and you cannot communicate.

  - Click in the command line space, and write the following (<cr> means carriage return (Enter)):

tx <cr>

it should respond: Serial Transmit enabled.

help <cr>

it should print a list of useful commands like this:

txoff

it should respond: Serial Transmit disabled

always disable the serial transmit after communicating if the instrument is being used as a sensor, as we don’t know if the transmitter would inject noise if it was left on.

- Calibration Inputs

The calibration inputs on the T240 work differently than those on the STS-2.  Instead of having a single enable, and three different signals, the T240 has one signal, and three input enable bits.  In order to map these efficiently, I stole some of the channels from the STS-2 box, and made them available for the T240.  In order to use the calibration coils, you must do the following:

  - Insert an appropriate signal into the UCAL BNC on the front of the STS-2 Interface (D080535-v2).

  - To select the direction, use the following switches on the STS-2 Interface Chassis (D080535-v2) (none of the switches on the STS2-to-T240 Interface chassis should be touched for this procedure):

To select the U direction, change the period select switch from “120 sec” to “1 sec”.

To select the V direction, change the Cal switch from “Norm” to “Cal”.

To select the W direction, change the XYX/UVW switch from “XYZ” to “UVW”.

For now, select only one direction at a time.  Tests will have to be done to find out if it is alright to enable more than one direction at any given time.

Appendix A  Trillium Cable Pinout