| APPROVALS | DATE | REV | DCN NO. | BY | CHECK | DCC | DATE |
| --- | --- | --- | --- | --- | --- | --- | --- |
| AUTHOR: K Mailand | 02-25-03 | B |  |  |  |  |  |
| CHECKED: |  |  |  |  |  |  |  |
| APPROVED: |  |  |  |  |  |  |  |
| DCC RELEASE |  |  |  |  |  |  |  |

Our operating conditions:

1. Approx Temp. 68/70 deg. F.

2. Operating Pressure Approx. 200 PSI

3. Flow Approx. 3.2 GPM

4. Continuous operation

Hydraulic Fluid Requirements:

1)	Non-hazardous (e.g. not extremely toxic)

2) 	Water soluble (or easily cleaned up)

3) 	Available in required viscosity, our requirement ~100cps @70F

4) 	Viscosity sensitivity with temperature is no worse than mineral oil.

5) 	Does not support biological growth.

6) 	Does not promote rust or corrosion; i.e. is compatible with the materials in our system.

7) 	Has sufficient lubricity for gear pumps (which may be used in our application)

8) 	Does not break down or coagulate or polymerize under the (very mild) conditions in our application.

9) 	No added dyes -- clear fluid

10)	Meets the ASTM D-2882 wear standard [see description below]

11)	Non-Flammable

Description of wear test: