DCN No.   E040511-00-D

California Institute of Technology

Sheet    1	 of   2

# Massachusetts Institute of Technology

# Document Change Notice (DCN)

DOCUMENT No.			            	TITLE			            		                                 NEW

A1

TCS INTERFACE

(DOC-REV-GP.ID)       						                                                                             REV

D040339-A1-D

CHANGE DESCRIPTION (FROM/TO):	Release Schematic #D040339-A1-D

The connection of the aim laser output to a 9 volt regulator output is changed to a 5 volt regulator output in this schematic.

REASON FOR CHANGE: 5 volt laser diodes were discovered at the sites, which could not run on +9 volts.

ACTION:                X Incorporate Change        Attach DCN to Drawings           X Other Action (specify): RELEASE DWG.

DISPOSITION OF HARDWARE (IDENTIFY SERIAL NUMBERS)

DCN DISTRIBUTION

Barish	Coyne	Fritschel

Giaime	Lazzarini	Lindquist

Raab	Shoemaker	Sibley

Sigg	Tyler	Weiss

Whitcomb	Worden

SAFETY, COST, SCHEDULE, REQUIREMENTS IMPACT?          X NO           YES (If YES, enter CR (CCB) or TCP (TRB) #)

X      List S/Ns to be retested per this change: #1, #2, #3, #4, #5

| APPROVALS: | DATE | OTHER APPROVALS (SPECIFY) | DATE |
| --- | --- | --- | --- |

ORIGINATOR: Jon Allen

12/16/04			04

X      List S/Ns to be reworked/scrapped: #1, #2, #3, #4, #5

List S/N’s to be built with this change:

No hardware was affected (record change only):

DCC RELEASE:

X        List S/Ns which comply already: #6, #7, #8

TASK LEADER: David Ottaway

GROUP LEADER: David Shoemaker

DCN No. E040511-00-D

California Institute of Technology

Sheet 2 of 2

# Massachusetts Institute of Technology

CHANGE DESCRIPTION (FROM/TO):

The PCB trace connecting K1 pin 10 to U10 pin 3 on the circuit side of the PCB is cut, allowing for a wire jumper soldered to U10 pin3 and U9 pin 3. This changes the supply voltage switched to the aim laser output on J3 from +9 volts to +5 volts, allowing for the use of 5 volt laser diodes. This is easily reworked by removing the lower half of the clamshell enclosure by unscrewing the two mounting screws on the lower side of the side extrusions, prying the bottom straight down and off, providing x-acto blade and soldering iron access to the trace and pins mentioned.

# Document Change Notice (DCN)

# Text boxes

LIGO Form DCN-04 (06/2004)

LIGO Form DCN-04 (06/2004)