LIGO- T080211-02-Z

September 8. 2008

LIGO Instrument Science Priority Matrix

The following matrix is intended as a companion to the LSC 2007 Instrument Science White Paper (LIGO-T070137-05-R).  The purpose is to identify the tasks and goals outlined in the white paper with phases or or goals within the larger framework of GW science development.  Specifically, four major motivations for the white paper activities were identified:

Fundamental Science which lays the groundwork broadly for GW development,

AdvLIGO Risk Mitigation (tasks which address problems that might crop up in the planned AdvLIGO program),

“Enhanced AdvLIGO” (developments which might be suitable to incorporate into AdvLIGO after a couple of years of AdvLIGO operation and which might give a moderate performance improvement at a modest cost), and

Third Generation Detectors, which offer very significant performance improvements (either in sensitivity or frequency coverage) but would require major changes or possibly new facilities.

Each task was evaluated to identify which of these categories provided the primary motivation for the activity and further, each task was assigned a priority (high, medium, or low).  Many of the tasks also have one or more secondary motivations, and these were also identified and prioritized.

Three new topics were identified, representing issues which have arisen since the last revision of the LSC Instrument White Paper.  These have been included in the matrix below.

| White Paper section | Topic | Goal | Funda-mental Science | AdvLIGO Risk Mitigation | “Enhanced” AdvLIGO | Third Generation Detectors |
| --- | --- | --- | --- | --- | --- | --- |
| 2. Suspensions and Isolation |
| 2.2.1.2 | Advanced seismometers | Reduce tilt/horizontal coupling in seismometers for active anti-seismic systems |  | Secondary- medium | Primary-medium | Secondary- medium |
| 2.2.1.3 | Suspension point interferometers | Investigate systems for measuring the rotation and position sensing of seismic platforms relative to each other to improve lock acquisition and reduce final stage dynamic range |  | Primary- high | Secondary- medium | Secondary- medium |
| 2.2.2.1 | Excess thermal noise from clamps and break-offs | Investigate of alternative metal wire clamping techniques for reducing thermal noise |  | Secondary - medium | Primary- medium |  |
| 2.2..2.2 | Multiple Pendulum Suspensions, mechanical and control aspects | Improve understanding of AdvLIGO prototype performance, develop novel control strategies for local and global control |  | Primary - high | Secondary - medium |  |
| 2.2.2.3 | Development of monolithic final stage | characterize AdvLIGO baseline design possible improvement to increase dilution factor |  | a) Primary high | a) Secondary high b)Primary high | b) Secondary- medium |
| 2.2.2.4 | Violin mode damping | Develop means to sense and damp violin mode motion |  | Primary- high | Secondary - medium |  |
| 2.2.2.5 | Creep noise | Investigate the rate and amplitude distribution of non-Gaussian noise events in wire and fused silica fiber suspensions |  | Primary- medium | Secondary - medium | Secondary - medium |
| 2.2.2.6 | Time domain modeling of suspensions | Integrate suspension and seismic isolation models to investigate high power effects |  | Primary- medium | Secondary - medium |  |
| 2.3.1.1 | Control aspects and different payloads | Investigate alternate methods for easing lock acquisitition |  | Primary- medium | Secondary - medium |  |
| 2.3.1.2 | Newtonian coupling | Understand Newtonian noise and test techniques to mitigate it |  |  | Primary high | Secondary high |
| 2.3.2.1 | Silicon suspensions | Develop flexures of silicon and measure their properties |  |  |  | Primary - High |
| 2.3.2.2 | Low noise blades | Develop silicon or fused silica blades for vertical isolation |  |  | Secondary - medium | Primary- medium |
| 2.3.2.3 | Novel attachment techniques | Investigate alternates to silicate bond attachments |  |  | Secondary low | Primary medium |
| 2.3.2.4 | Larger masses | Investigate suspensions for larger Test masses/optics |  |  | Secondary - high | Primary high |
| 2.3.2.5 | Cryogenics – suspension aspects | Study designs concepts for cryogenic suspension |  |  |  | Primary high |
| 2.3.2.6 | Cryogenics – radiative cooling | Investigate radiative and evanescent wave cooling |  |  | Secondary - medium | Primary medium |
| 3. Optics |
| 3.1.1 | Optical coating research | Investigate materials and techniques (e.g., annealing) for improving coating performance for GW interferometry | Secondary medium | Primary- high | Secondary - high | Secondary - high |
| NEW | Coating absorption and scattered light | Develop lower absorption and lower scatter loss coatings for the test masses |  | Primary - High | Secondary - High |  |
| 3.1.2 | Fused silica test mass research | Investigate possible trade-off between optical loss and mechanical loss in fused silica, measure uniformity |  | Primary- low | Secondary - medium | Secondary - medium |
| 3.1.3 | Thermal compensation research | Investigate techniques such a barrel coatings that might ease the thermal compensation requirements for high power operation |  | Primary- medium | Secondary - medium |  |
| 3.1.4 | High power effects in Advanced LIGO | Investigate parametric instabilities and means to control them |  | Primary- high | Secondary - high |  |
| 3.1.5 | Modeling thermal effects in Advanced LIGO | Develop improved computer models for simulating thermal effects in Advanced LIGO |  | Primary - High | Secondary - High |  |
| 3.1.6 | Diagnostics for Advanced LIGO optics | Develop improved performance for sensing distortions of AdvLIGO optics in-situ |  |  | Primary- medium |  |
| 3.1.7 | High power optical components | Develop EOMs and FIs capable of higher power operation |  | Primary- high | Secondary - high |  |
| 3.1.8 | Charging of test masses | Directly measure noise due to charge build-up on test mass optics, and develop techniques for controlling charging |  | Primary - High | Secondary - High |  |
| NEW | Charging of test mass and stops | Improve the modeling and calculate impact of charging on interferometer noise |  | Primary- high |  |  |
| 3.1.9 | Variable reflectivity signal recycling mirror | Develop control systems and other hardware needed to implement a variable reflectivity signal recycling mirror |  |  | Primary medium | Secondary medium |
| 3.1.10 | Investigation into sources of non-Gaussian noise | Measure non-Gaussian transient noise burst in optics and understand causes |  | Primary - Low | Secondary - Medium |  |
| 3.2.1 | Mesa beam optics | Develop and test auto alignment sensing schemes for mesa beam optical cavities |  |  | Primary medium | Secondary medium |
| 3.2.2 | Development and characterization of novel optical substrate materials | Develop and characterize sapphire and/or silicon for optical substrates | Secondary medium |  | Secondary low | Primary high |
| 3.2.3 | High efficiency grating development and characterization | Develop, characterize and model large area high efficiency gratings for use in GW interferometers | Secondary medium |  |  | Primary - Medium |
| 3.2.4 | Low loss nonlinear optical materials for squeezed light interferometry | Study loss mechanisms in non-linear materials to improve performance for squeezing and improve long term reliability | Secondary - High |  | Primary - High | Secondary - Medium |
| 3.2.5 | Composite masses | Study composite test masses as a way of reducing quantum radiation pressure noise |  |  |  | Primary - High |
| 3.2.6 | Coating-less or coating-reduced optics | Develop and experimentally test coating-free or reduced coating interferometers |  |  |  | Primary- high |
| 4. Lasers |
| 4.2.1 | High power concepts – Yb:YAG | Characterize Yb:YAG for kilowatt class lasers for GW interferometers | Primary- high |  |  | Secondary - medium |
| 4.2.2 | High power concepts – slabs, rods | Model and characterize slabs and birefringence compensated rods for higher power laser designs |  |  | Primary - Medium | Secondary - medium |
| 4.2.3 | High power concepts – amplifiers | Investigate performance and longevity of optical fiber amplifiers | Secondary- high |  | Secondary - medium | Primary - medium |
| 4.2.4 | High power concepts – adaptive optics | Develop static and/or dynamic wavefront correction techniques for matching laser beam profiles to optical cavities |  |  | Secondary low | Primary Medium |
| 4.2.5 | High power concepts – pump-fiber combine | Test optical pump fiber combiners for long term operation |  |  | Secondary high | Primary High |
| 4.2.6 | Squeezed light sources | Develop reliable high efficiency squeezed light (squeezed vacuum) sources | Secondary - High |  | Primary high |  |
| 4.2.7 | Laser Stabilization | Development of laser stabilization techniques, particularly relative intensity stabilization |  | Primary medium | Secondary high |  |
| 4.2.8 | Photodiodes | Develop high efficiency, high power photodiodes |  | Primary - High | Secondary - high |  |
| 5. Advanced Interferometer Configurations |
| 5.1 | Advanced LIGO and possible enhancements | test interferometer sensing and control component parts for AdvLIGO optimize readout parameters and analysis of AdvLIGO sensing and control scheme Investigate alternative and modified sensing schemes for AdvLIGO |  | a)Primary-high b) Primary-high c) Secondary-medium | c) Primary - high |  |
| 5.2 | Simulation | Model non-linear effects including lock-acquisition analyze thermal effects and optical aberrations Study control schemes Study quantum radiation pressure, optical spring effects and squeezing |  | a) Primary-high b) Primary-high c) Primary-high d) Primary-high | a) Secondary - medium b) Secondary - medium c) Secondary - medium d) Secondary - medium |  |
| - | Beyond Advanced LIGO: quantum techniques | a) development of squeezed light sources b) development of filter cavities c) development of optical configurations beyond the standard quantum limit d) investigation of displacement-free interferometry | a) Secondary - medium c) Secondary - medium d) Secondary - medium |  | a) Primary-high b) Primary-high c) Primary-high | a) Secondary -high b) Secondary -high c) Secondary -high d) Primary-medium |
| 5.3 | Generic techniques in configurations | control of high power coupled cavity systems new readout schemes theoretical modeling of radiation pressure in coupled cavities interferometer configurations based on diffractive or polarizing optics | b) Secondary - medium c) Secondary - medium |  | a) Primary-high b) Primary-high c) Primary-high | b) Secondary - medium d) Primary - high |