LIGO Laboratory / LIGO Scientific Collaboration

LIGO- E1100306 	                 LIGO                   October 2nd, 2012

aLIGO BSC-ISI, Pre-integration Testing report,

Phase I (post-assembly)

E1100306 – V1

Adrien Le Roux, Celine Ramet

Distribution of this document:

Advanced LIGO Project

This is an internal working note

of the LIGO Laboratory

| California Institute of Technology LIGO Project – MS 18-34 1200 E. California Blvd. Pasadena, CA 91125 Phone (626) 395-2129 Fax (626) 304-9834 E-mail: info@ligo.caltech.edu | Massachusetts Institute of Technology LIGO Project – NW22-295 185 Albany St Cambridge, MA 02139 Phone (617) 253-4824 Fax (617) 253-7014 E-mail: info@ligo.mit.edu |
| --- | --- |
| LIGO Hanford Observatory P.O. Box 1970 Mail Stop S9-02 Richland WA 99352 Phone 509-372-8106 Fax 509-372-8137 | LIGO Livingston Observatory P.O. Box 940 Livingston, LA 70754 Phone 225-686-3100 Fax 225-686-7189 |

Table of contents:

Introduction	4

I.	Pre-Assembly Testing	5

	Step 1 - CPS Test and calibration – E1100369	5

	Step 2 - GS13 – Inspection/Assembly – E1000058 – E1100740	6

	Step 3 - L4C – Inspection/Assembly – E1000136 – E1100740	8

Step 4 - T240 – Inspection/Assembly - E1100326 – E1100740	11

	Step 5 - Actuators - T0900564 - T1100234 – E1100741	14

II.	Tests to be performed during assembly	15

	Step 1 - Test stand level	15

	Step 2 - Actuators Inventory	15

	Step 3 - Sensors Inventory	15

	Step 4 - Electronics Inventory	17

	Step 5 - Check level of Stage 0 after top-bottom plate assembly	18

	Step 6 - Check gaps under the blade posts	18

	Step 7 - Blade post shim thickness	18

	Step 8 - Blade 0-1 post launch angle	19

	Step 9 - Gap checks on actuators	19

	Step 10 - Mass budget	20

	Step 11 - Lockers adjustment	23

	Step 12 – Cables inventory – E1100822	24

	Step 13 - Cable routing	24

III.	Tests to perform after assembly	25

	Step 1- Geophones pressure readout	25

	Step 2- Set up sensors gap – Locked vs unlocked position	26

	Step 3 - Measure the Sensor gap	27

Step 4- Performance of the limiters	27

o	Step 4.1 - Test Nº1 - Push “in the general coordinates Z/RZ”	27

o	Step 4.2 - Test Nº2 – Push “locally”	28

	Step 5 - Sensors Powespectra	28

	Step 6 - Coil Driver, cabling and resistance check	33

	Step 7- Actuators Sign and range of motion (Local drive)	34

o	Step 7.1 - Actuators sign	34

o	Step 7.2 - Range of motion - Local drive	34

	Step 8 - Vertical Sensor Calibration	35

	Step 9 - Vertical Spring Constant	36

	Step 10 - Static Testing (Tests in the local basis)	38

	Step 11- Static Testing - In the general coordinate basis (Static test - CPS)	41

o	Step 11.1 – Change of basis matrices from Cartesian to Local	41

o	Step 11.2 – Base change matrices from Cartesian to Cartesian	43

	Step 12 - Linearity test	45

	Step 13 – Transfer functions – Local to Local	49

	Step 14 - Symmetrization – Calibration	64

	Step 15 – Change of base – Cartesian to Local - Simulations	64

	Step 16- Transfer functions - Cartesian to Cartesian - Measurements	64

	Step 17 - Lower Zero Moment Plan	64

o	Step 17.1 - Stage 1 - LZMP	64

o	Step 17.2 - Stage 2 - LZMP	64

	Step 18- Damping Loops – Transfer function – Simulations	64

o	Step 18.1 - Damping Loops – Stage 2	64

o	Step 18.2 - Damping Loops – Stage 1	64

	Step 19- Damping Loops – Powerspectra	64

	Step 20- Isolation Loops – for one unit per site	67

IV.	BSC-ISI testing Summary	68

Introduction

The BSC-ISI testing is performed in three phases:

1) BSC-ISI, Pre-integration Testing, Phase I (post-assembly)

2) BSC-ISI, Pre-integration Testing, Phase II: Tests done after Transport (and possible storage), during mating phase with Suspensions, before insertion.

3) BSC-ISI, Integration Phase Testing: Procedure and results related to the commissioning in the chamber.

This document presents the series of tests (Phase I) performed on the ISI-BSC3 (ITMX) in the High Bay before its move to the LVEA (Test stand). First set of tests were done during August 2012. But because of Hurricane Isaac and a power outage of ~30 hours in the LVEA causing corrosion on the BSC Lockers (without A/C, the Temperature and Humidity went up inside the cleanroom, causing condensation on the BSC and thus oxidation. The only parts really affected were the Lockers and after further investigations, it turns out that it is because they are made of a different type of Aluminum than the rest of the ISI: stronger but less resistant to oxidation!). After noticing that, we had to swap the Lockers and sent the oxidized set through clean and bake, and so we decided to restart the Testing from scratch.

This is the third “aLigo BSC-ISI” built and tested with the “aLigo electronic” at the LLO site. The testing procedure document E1000486-v3 was used.

All results are posted on the SVN at:

https://svn.ligo.caltech.edu/svn/seismic/BSC-ISI/X2/Data/BSC3/

The following type of document can be found in the SVN:

- Excel spreadsheet (.xls)

- Data location

- Figures location

- Masses distribution scheme (ppt)

# Pre-Assembly Testing

## Step 1 - CPS Test and calibration – E1100369

CPS sensors are tested (calibration and noise test) at MIT before being cleaned and baked at LLO. The list of installed sensors used for testing (phase I) are reported in step II.3.

All data related to the CPS testing can be found in the SVN at

/svn/seismic/Common/Data/aLIGO_BSC_ISI_CPS/

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 2 - GS13 – Inspection/Assembly – E1000058 – E1100740

GS13 are tested and podded at LLO. We had to replace one GS-13 on this Unit due to a bad feed thru, the cable screw wouldn’t go all the way, leaving the cable the possibility to wobble. The feed thru is going to be inspected and tested again.

The list of installed sensors used for testing (phase I) are reported in step II.3.

All the data related to GS-13 post podding testing can be found in the SVN at : /svn/seismic/Common/Data/aLIGO_GS13_TestData/PostMod_TestResults_PDFs

Figure 1: Huddle Test Transfer Function of the Horizontal GS-13 SN 811, 844 & 858 after aLIGO modifications

Figure 2: Huddle Test Transfer Function of the Vertical GS-13 SN 745, 722 & 689 after aLIGO modifications

Figure 3: Driven Transfer Function of the Vertical GS-13 SN 745, 722 & 689 after aLIGO modifications

E1000058 and E1100740 spreadsheets provide the status of each individual GS-13 at LLO site for HAM-ISI and BSC-ISI and the installation location of the geophones.

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 3 - L4C – Inspection/Assembly – E1000136 – E1100740

L4C are tested and podded at LLO. The list of installed sensors used for testing (phase I) are reported in step II.3.

All the data related to L4C post podding testing can be found in the SVN at : /svn/seismic/Common/Data/aLIGO_L4C_TestData/TestResults_PDFs/

Figure 4: Huddle Test Transfer Function of the Horizontal L4-C SN 1111, 822 & 966

Figure 5: Huddle Test Transfer Function of the Vertical L4-C SN 1081, 926 & 1082

Note: No record of the Huddle Test Transfer Function for the Horizontal L4-C SN 1081

E1000136 and E1100740 spreadsheets provide the status of each individual L4C at LLO site for HAM-ISI and BSC-ISI and the installation location of the geophones.

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 4 - T240 – Inspection/Assembly - E1100326 – E1100740

T240 are tested and podded at LLO. We haven’t had to replace the T240s on this Unit, and these are the ones with the new Voltage Regulator, it seems that they are working fine and keep the pressure sensor from dying. The list of installed sensors used for testing (phase I) are reported in step II.3.

All the data related to T240 post podding testing can be found in the SVN at :

seismic/Common/Data/aLIGO_T240_TestData/AsReceived_TestResults_PDFs.

Figure 6: Huddle Test Transfer Function of the X, Y & Z axis of the T240 SN 114

Figure 7: Huddle Test Transfer Function of the X, Y & Z axis of the T240 SN 148

Figure 8: Huddle Test Transfer Function of the X, Y & Z axis of the T240 SN 120

E1100326 and E1100740 spreadsheets provide the status of each individual T240 at LLO site for BSC-ISI and the installation location of the geophones.

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 5 - Actuators - T0900564 - T1100234 – E1100741

The list of installed sensors used for testing (phase I) are reported in step II.2

Large actuators data can be found at: T0900564. Actuator inventory is made at Section II – Step 2.

Small actuators data can be found at: T1100234. Actuator inventory is made at Section II – Step 2.

|  | Stage 0-1 | Stage 1-2 |
| --- | --- | --- |
| H1 | Actuator Serial #: L026 Operator Name: Smith, Lane Date: 8/13/2009 Time: 3:18 PM Actuator Coil Resistance: 6.45 Ohms, PASS Ambient Temperature: 73.3 F Hi Pot Test Results: 1000 MOhms, PASS X Travel Limit (inches): 0.518 Y Travel Limit (inches): 0.207 Z Travel Limit (inches): 0.504 | Actuator Serial #: S083 Operator Name: Gordon, Matt Date: 4/13/2011 Time: 3:29 PM Actuator Coil Resistance: 10.56 Ohms, PASS Ambient Temperature: 75.6 F Hi Pot Test Results: 1000 MOhms, PASS X Travel Limit (inches): 0.646 Y Travel Limit (inches): 0.205 Z Travel Limit (inches): 0.507 |
| H2 | Actuator Serial #: L025 Operator Name: Smith, Lane Date: 8/12/2009 Time: 10:56 AM Actuator Coil Resistance: 6.39 Ohms, PASS Ambient Temperature: 71.3 F Hi Pot Test Results: 1000 MOhms, PASS X Travel Limit (inches): 0.523 Y Travel Limit (inches): 0.205 Z Travel Limit (inches): 0.503 | Actuator Serial #: S075 Operator Name: Gordon, Matt Date: 4/13/2011 Time: 1:30 PM Actuator Coil Resistance: 10.23 Ohms, PASS Ambient Temperature: 75.6 F Hi Pot Test Results: 1000 MOhms, PASS X Travel Limit (inches): 0.662 Y Travel Limit (inches): 0.205 Z Travel Limit (inches): 0.512 |
| H3 | Actuator Serial #: L068 Operator Name: Gordon, Matt Date: 11/19/2009 Time: 1:27 PM Actuator Coil Resistance: 6.28 Ohms, PASS Ambient Temperature: 73.1 F Hi Pot Test Results: 1000 MOhms, PASS X Travel Limit (inches): 0.532 Y Travel Limit (inches): 0.205 Z Travel Limit (inches): 0.503 | Actuator Serial #: S093 Operator Name: Gordon, Matt Date: 4/14/2011 Time: 1:11 PM Actuator Coil Resistance: 10.46 Ohms, PASS Ambient Temperature: 75.6 F Hi Pot Test Results: 1000 MOhms, PASS X Travel Limit (inches): 0.661 Y Travel Limit (inches): 0.206 Z Travel Limit (inches): 0.513 |
| V1 | Actuator Serial #: L003 Operator Name: Smith, Lane Date: 8/12/2009 Time: 3:17 PM Actuator Coil Resistance: 6.40 Ohms, PASS Ambient Temperature: 71.3 F Hi Pot Test Results: 1000 MOhms, PASS X Travel Limit (inches): 0.520 Y Travel Limit (inches): 0.204 Z Travel Limit (inches): 0.504 | Actuator Serial #: S072 Operator Name: Gordon, Matt Date: 4/13/2011 Time: 10:09 AM Actuator Coil Resistance: 10.31 Ohms, PASS Ambient Temperature: 75.6 F Hi Pot Test Results: 1000 MOhms, PASS X Travel Limit (inches): 0.665 Y Travel Limit (inches): 0.205 Z Travel Limit (inches): 0.512 |
| V2 | Actuator Serial #: L029 Operator Name: Smith, Lane Date: 8/11/2009 Time: 4:56 PM Actuator Coil Resistance: 6.35 Ohms, PASS Ambient Temperature: 72.5 F Hi Pot Test Results: 1000 MOhms, PASS X Travel Limit (inches): 0.527 Y Travel Limit (inches): 0.193 Z Travel Limit (inches): 0.483 | Actuator Serial #: S080 Operator Name: Gordon, Matt Date: 4/13/2011 Time: 2:33 PM Actuator Coil Resistance: 10.57 Ohms, PASS Ambient Temperature: 75.6 F Hi Pot Test Results: 1000 MOhms, PASS X Travel Limit (inches): 0.634 Y Travel Limit (inches): 0.205 Z Travel Limit (inches): 0.514 |
| V3 | Actuator Serial #: L0093 Operator Name: Gordon, Matt Date: 11/21/2009 Time: 11:03 AM Actuator Coil Resistance: 6.29 Ohms, PASS Ambient Temperature: 68.9 F Hi Pot Test Results: 1000 MOhms, PASS X Travel Limit (inches): 0.529 Y Travel Limit (inches): 0.205 Z Travel Limit (inches): 0.504 | Actuator Serial #: S097 Operator Name: Gordon, Matt Date: 4/14/2011 Time: 2:06 PM Actuator Coil Resistance: 10.58 Ohms, PASS Ambient Temperature: 75.6 F Hi Pot Test Results: 1000 MOhms, PASS X Travel Limit (inches): 0.684 Y Travel Limit (inches): 0.205 Z Travel Limit (inches): 0.512 |

Test result:	Passed:   X   	Failed:         .	Waived :.     .

# Tests to be performed during assembly

## Step 1 - Test stand level

The HAM-ISI Test Stand was transformed and re-leveled to dock a BSC-ISI.

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 2 - Actuators Inventory

The actuators S/N are reported in the table below. Further information can be found in T0900564 and T1100234.

| Stage 0-1 | Stage 1-2 |
| --- | --- |
| Actuator | Actuator S/N | Actuator | Actuator S/N |
| H1 | L026 | H1 | S083 |
| H2 | L025 | H2 | S075 |
| H3 | L068 | H3 | S093 |
| V1 | L003 | V1 | S072 |
| V2 | L029 | V2 | S080 |
| V3 | L093 | V3 | S097 |

Table 1 - Actuators' inventory

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 3 - Sensors Inventory

The sensors S/N are reported in the table below.

| CPS Stage 0-1 | CPS S/N | ADE board serial # |
| --- | --- | --- |
| H1 | 13552 | 15689 |
| H2 | 13626 | 15842 |
| H3 | 13466 | 12660 |
| V1 | 13622 | 15682 |
| V2 | 13621 | 15857 |
| V3 | 12909 | 12419 |

Table 2 - Capacitive position sensors' inventory – Stage 1

| CPS Stage 1-2 | CPS S/N | ADE board serial # |
| --- | --- | --- |
| H1 | 13236 | 12547 |
| H2 | 13637 | 15903 |
| H3 | 13435 | 12588 |
| V1 | 13467 | 12518 |
| V2 | 13414 | 12450 |
| V3 | 13461 | 12584 |

| Geophones GS13 | Serial Number | POD |
| --- | --- | --- |
| H1 | 811 | 2 |
| H2 | 844 | 34 |
| H3 | 858 | 103 |
| V1 | 745 | 18 |
| V2 | 722 | 1 |
| V3 | 689 | 88 |

Table 3 - GS13 inventory

| Geophones L4C | Serial Number | POD |
| --- | --- | --- |
| H1 | 1111 | 2 |
| H2 | 822 | 57 |
| H3 | 966 | 139 |
| V1 | 1081 | 118 |
| V2 | 926 | 121 |
| V3 | 1082 | 144 |

Table 4 - L4C inventory

| Geophones T240 | Serial Number | POD |
| --- | --- | --- |
| 1 | 114 | 12 |
| 2 | 148 | 17 |
| 3 | 120 | 31 |

Table 5 - T240 inventory

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 4 - Electronics Inventory

Write down in the table below all serial numbers all the electronic equipment:

| Hardware | LIGO reference | S/N |
| --- | --- | --- |
| Interface Chassis - Corner 1 | D1002432 | S1102219 |
| Interface Chassis - Corner 2 |  | S1106356 |
| Interface Chassis - Corner 3 |  | S1106358 |
| Anti-Alliasing Chassis - Corner 1 | D1002693 | S1106137 |
| Anti-Alliasing Chassis - Corner 2 |  | S1106138 |
| Anti-Alliasing Chassis - Corner 3 |  | S1106136 |
| Anti-image Chassis | D070081 | S1000249 |
| Binary Input Chassis | D1001726 | S1101287 |
| Binary Input Chassis |  | S1101285 |
| Binary Output Chassis | D1001728 | S1101322 |
| T240 Interface - Corner 1 | D1002694 | S1104420 |
| T240 Interface - Corner 2 |  | S1104422 |
| T240 Interface - Corner 3 |  | S1104426 |
| I/O Chassis | n/a | XP 005 |
| Coil driver Pod 1 | D0902744 | S1103354 |
| Coil driver Pod 2 |  | S1000316 |
| Coil driver Pod 3 |  | S1103313 |

Table 6 - Electronic equipment

Note: We had to replace the anti-image Chassis S1000251 by S1000249 because it was causing Stage 0-1 H1 Actuator to have only half of his actuating range.

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 5 - Check level of Stage 0 after top-bottom plate assembly

Note: This test has not been performed

Test result:	Passed:      	Failed:         .	Waived :.   X   .

## Step 6 - Check gaps under the blade posts

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 7 - Blade post shim thickness

This table shows the shims thickness installed under the lockers.

| Stage 0-1 | Stage 1-2 |
| --- | --- |
| Lockers | Shim thickness (mil) | Lockers | Shim thickness (mil) |
| A | 127 | A | 114 |
| B | 125 | B | 118 |
| C | 129 | C | 115 |

Table 7 - Shims thickness

Acceptance criteria: Both D0901805 Stage 0-1 Locker Shims & D0902551 Stage 1-2 Locker Shims goes from .110” up to .130” with an increment of .001”.

So far (LHO 2 first Units and LLO 2 first Units):

|  | Max | Min | Average |
| --- | --- | --- | --- |
| Stage 0-1 | .129” | .120” | .1257” |
| Stage 1-2 | .130” | .114” | .1232” |

The values of this LLO 3rd Unit seem coherent with the ones of the previous Units.

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 8 - Blade 0-1 post launch angle

This test has not been performed on LLO Unit 2.

Test result:	Passed:      	Failed:         .	Waived :.   X  .

## Step 9 - Gap checks on actuators

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 10 - Mass budget

The figure below presents the location of the masses on both stages.

Figure 9: Masses distribution

Stage 1:

| Stage 1 |
| --- |
| Location | Weight (lb) | Weight (Kg) |
| C1-1 | 12 | 5.44 |
| C1-2 | 15 | 6.80 |
| C1-3 | 4.5 | 2.04 |
| C2-1 | 0 | 0.00 |
| C2-2 | 0 | 0.00 |
| C2-3 | 15 | 6.80 |
| C3-1 | 12 | 5.44 |
| C3-2 | 15 | 6.80 |
| C3-3 | 13.5 | 6.12 |
| Total | 87 | 39.46 |

Table 8 - Payload Stage 1

Nominal payload: 108.9Kg – 240lb
Added masses are 69Kg – 152lb lighter than expected.
Total mass of stage 1=916Kg - 2019lb

Stage 2:

Table 9 - Payload Stage 2

Nominal payload: 1183.4Kg – 2609lb
The added masses is 22.1Kg – 48.7lbs lighter than expected.

Total nominal mass of Stage 2: 2913.9Kg – 6424lb
Error on the nominal overall mass of stage 2: 22.1/2913.9=0.8%

Summary:

| Unit 3 |
| --- |
|  | Plan | 8/13/2012 | % diff from Plan | Mass Diff from Plan |
| Stage 1 | 108.86 | 39.46 | -63.75 | -69.40 |
| Stage 2 | 1183.42 | 1161.33 | -1.87 | -10.66 |

LLO Unit 1 & 2 Results:

| Unit 1 |
| --- |
|  | Plan | Original | 3/1/2012 | 3/9/2012 | % Diff from Plan | Mass Diff from Plan |
| Stage 1 | 108.86 | 148.10 | 19.50 | 36.29 | -66.67 | -72.57 |
| Stage 2 | 1183.42 | 989.42 | 1089.07 | 1096.83 | -7.32 | -86.59 |

| Unit 2 |
| --- |
|  | Plan | 6/12/2012 | % diff from Plan | Mass Diff from Plan |
| Stage 1 | 108.86 | 60.06 | -44.83 | -48.81 |
| Stage 2 | 1183.42 | 1071.93 | -9.42 | -111.49 |

LLO Unit 3 is the first one to use these Silver Plated Eastwood Bolts for the Spring Blades and we can see the benefits of it especially on Stage 2!

Previous Units Results:

|  | Plan | LHO Unit 1 | LHO Unit 2 | LLO Unit 1 | LLO Unit 2 | Avg (4 1st Units) | STD | LLO Unit 3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Stage 1 | 108.86 | 35.6 | 58.6 | 36.29 | 60.06 | 47.64 | 11.71 | 39.46 |
| Stage 2 | 1183.42 | 1082.4 | 1059.5 | 1096.83 | 1071.93 | 1077.67 | 13.72 | 1161.33 |
| Stage 1 | 175.86 | -9.79 | 48.50 | -8.04 | 52.20 | 20.72 | % of Diff/LLO Unit 3 |
| Stage 2 | 1.90 | -6.80 | -8.77 | -5.55 | -7.70 | -7.20 |  |

Note: This Unit is the first one with the Silver Plated Eastwood Bolts for the Blades. Since the Silver Plating allows a better friction with the Nitronic of the Barrel Nuts, we decided to go back to the initial torque value for these bolts: 110 ft.lbs.

Even if the mass budget on Stage 1 is light compared to the original plan, by comparing it with the Previous Units built at LHO & LLO, we can see that this Unit is in the general tendency:

- Stage 2 Mass Budget is the closest one to the Plan built to date: less than 2% difference.

- Stage 1 Mass Budget is in the general tendency of the four first previous Units.

Not only that but this Unit is the closest one to the theoretical Mass Plan ever built!

In conclusion, the BSC-ISI seems to benefit a lot from these new bolts.

Note: This Unit is the last one built with the D1100570-V1 & D1100564-V1 Angled Blade Spacers. Starting on next Unit at LLO, we will use the Version 2 of these Angled Blade Spacers on both Stages to try to come even closer to the Plan Mass Budget. This Version 2 has a slightly different launching angle than the first Version and that should bring the whole BSC-ISI closer to the Plan Mass Budget.

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 11 - Lockers adjustment

When we first Unlocked the BSC (both Stages), we had an initial twist of :

- -0.002” on corner 1

- +0.0045” on corner 2

- -0.005” on corner 3

But these numbers don’t have a lot of sense since the BSC was not balanced. So after leveling individually both stage (starting with Stage 2) and then adjusting the weight on the BSC fully Unlocked, here are the values of the twist:

|  | Stage 0-2 (both Stage unlocked after leveling) |
| --- | --- |
| D.I at Lockers | Dial indicators V | Dial indicators H |
| A | 0 | -10.5 |
| B | 0 | -3 |
| C | 0 | -14.5 |

Table 11: Initial Dial Indicators read-out (both Stage Unlocked)

After a few iterations, to center each Locker horizontally, here are the final values of the Dial:

|  | Stage 0-2 (both Stage unlocked after leveling) |
| --- | --- |
| D.I at Lockers | Dial indicators V | Dial indicators H |
| A | 0 | 0 |
| B | 1 | 0 |
| C | 0 | 0 |

Table 12: Final Dial Indicators read-out (both Stage Unlocked)

Measurements using the CPS sensors when the stages are locked and unlocked have been done Step III.2.

Note: After the lockers swap, when we opened the Lockers without correcting the twist, we found some very similar results showing that the twist comes from the Blade/Flexure and is consistent.

Test result:	Passed:   X   	Failed:         .	Waived :.      .

## Step 12 – Cables inventory – E1100822

The final Class A cables have been used for the testing of this Unit.

|  | Type of Cable | Corner 1 | Corner 2 | Corner 3 |
| --- | --- | --- | --- | --- |
| St 0-1 V Actuators | Pigtail | D1100150 – S1107139 | D1100151 – S1107215 | D1100151 – S1107218 |
|  | Extension | D1100148 – S1106976 | D1100148 – S1106972 | D1100148 – S1106939 |
| St 0-1 H Actuators | Pigtail | D1100150 – S1107133 | D1100151 – S1107165 | D1100151 – S1107219 |
|  | Extension | D1100148 – S1106932 | D1100148 – S1106934 | D1100148 – S1106960 |
| St 1-2 V Actuators | Pigtail | D1100150 – S1107140 | D1100150 – S1107132 | D1100151 – S1107220 |
|  | Extension | D1100148 – S1106948 | D1100148 – S1106947 | D1100148 – S1106961 |
| St 1-2 H Actuators | Pigtail | D1100150 – S1107134 | D1100150 – S1107088 | D1100151 – S1107147 |
|  | Extension | D1100148 – S1106967 | D1100148 – S1106946 | D1100148 – S1106957 |
| L4C | Pigtail | D1100154 – S1107333 | D1100154 – S1107330 | D1100155 – S1104249 |
|  | Extension | D1100152 – S1107246 | D1100153 – S1107284 | D1100153 – S1107269 |
| GS-13 | Pigtail | D1100154 – S1107336 | D1100155 – S1107379 | D1100155 – S1104252 |
|  | Extension | D1100153 – S1107313 | D1100153 – S1104571 | D1100153 – S1107277 |
| T240 |  | D1100153 – S1107280 | D1100153 – S1107283 | D1100152 – S1107259 |

Note: Some changes might occur later in the cabling. Indeed, installing our first BSC-ISI in chamber gave us a better idea of where to put which length of cable (to be able to reach their feed through…).

Test result:	Passed:   X   	Failed:         .	Waived:.     .

## Step 13 - Cable routing

The final Class A cables have been used for the testing of this Unit.

The cabling has been done following E1101027 aLIGO BSC-ISI Cable Routing Manual.

Test result:	Passed:   X   	Failed:         .	Waived :.     .

# Tests to perform after assembly

## Step 1- Geophones pressure readout

|  | Pressure (counts) |
| --- | --- |
| Sensors | Corner 1 | Corner 2 | Corner 3 |
| ST1-L4C-P | 100.1 | 100.54 | 100.07 |
| ST1-L4C-D | 0.19051 | -0.98714 | -0.075725 |
| ST1-GS13-P | 100.3 | 77.345 | 77.27 |
| ST1-GS13-D | -0.62561 | 0.3819 | -0.2195 |
| ST1-T240-P | 154.72 | 153.9 | 154.04 |

Nominal Value for the Pressure Readout: 100 counts

Test mitigation:

On LLO BSC Unit 1, L4C-P in Corner 1 was giving strange signal, but it didn’t come from the pressure sensor, it was coming from the interface SN S1106357. This interface was replaced with S1102219.

Replacing the Interface Chassis of Corner 1 fixed the issue we had about the pressure sensor Readout on the GS-13. This issue is still here on Corner 2 & 3, but we know the problem comes from the interfaces used for these Corners. That explains why we have reading ~77 counts on these GS-13’s.

The Pressure value on the Trillium is ~150 counts, which is not realistic. We’ve always had that issue (probably due to the Interfaces) but we know that a pressure readout of ~150 counts means that the pressure sensor works (otherwise the pressure readout is 30 counts!).

So we know we have good pressure sensors in this Unit’s pods.

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 2- Set up sensors gap – Locked vs unlocked position

During this step, sensors gap are adjusted. This step considers that the lockers have been finely setup during assembly.

| May-2012 |  |  |  |  |
| --- | --- | --- | --- | --- |
|  | Table locked | Table unlocked | Difference locked - unlocked |
| Sensors | Offset (Mean) | Std deviation | Offset (Mean) | Std deviation | Offset (Mean) | mil |
| ST1 - H1 | 134.25 | 44.599 | 455.63 | 67.804 | -321.38 | -0.38 |
| ST1 - H2 | 283.15 | 28.549 | -33.747 | 57.589 | 316.90 | 0.38 |
| ST1 - H3 | 79.286 | 16.59 | -502.79 | 51.582 | 582.08 | 0.69 |
| ST1 - V1 | -26.259 | 49.102 | 46.069 | 84.512 | -72.33 | -0.09 |
| ST1 - V2 | 286.47 | 47.697 | 237.8 | 144.6 | 48.67 | 0.06 |
| ST1 - V3 | 183.76 | 25.814 | 867.87 | 187.06 | -684.11 | -0.81 |
| ST2 - H1 | -1180.7 | 93.857 | 874.55 | 74.748 | -2055.25 | -0.61 |
| ST2 - H2 | -24.412 | 105.24 | 1078.1 | 87.874 | -1102.51 | -0.33 |
| ST2 - H3 | 650.42 | 141.84 | 687.52 | 80.724 | -37.10 | -0.01 |
| ST2 - V1 | 987.77 | 283.78 | 1082.9 | 269.19 | -95.13 | -0.03 |
| ST2 - V2 | 271.16 | 120.69 | 1277.3 | 415.84 | -1006.14 | -0.30 |
| ST2 - V3 | 543.82 | 177.08 | 598.8 | 464.92 | -54.98 | -0.02 |

Table 12 - Capacitive position sensors readout after gap set-up

Acceptance criteria:

- In the locked position, all mean values must be lower than 400 counts for stage 1 CPS and 1600 counts for stage 2 CPS (a bit less than .0005”).

- In the locked position, all standard deviations below 25 counts for stage 1, 100 counts for stage 2

- Absolute values of the difference between the unlocked and the locked table must be below:

Stage 1

  - 1600 cts for horizontal sensors (~0.002”)

  - 1600 cts for vertical sensors (~0.002”)

Stage 2

  - 6500 cts for horizontal sensors (~0.002”)

  - 6500 cts for vertical sensors (~0.002”)

- Considering the acceptance criteria of step 2, all mean values must be lower than

Stage 1

  - 2000 cts for horizontal sensors (~0.0025”)

  - 2000 cts for vertical sensors (~0.0025”)

Stage 2

  - 8000 cts for horizontal sensors (~0.0025”)

  - 8000 cts for vertical sensors (~0.0025”)

Test result:	Passed:   X   	Failed:         .	Waived :.      .

## Step 3 - Measure the Sensor gap

Test Failure mitigation:

This test was not performed. The sensor gaps have not been measured. These sensors have already been tested at LASTI. Moreover, risks of scratching the target are so high that we preferred not performing this test. In the future, this test will be removed from the testing procedure.

Test result:	Passed:      	Failed:         .	Waived :.   X   .

## Step 4- Performance of the limiters

## Step 4.1 - Test Nº1 - Push “in the general coordinates Z/RZ”

|  | CPS read out | Calculated after calibration |
| --- | --- | --- |
| Sensors | "-Z" (Counts) | "+Z" (Counts) | "-Z" (mil) | "+Z" (mil) |
| ST1 - V1 - ST2 LCK | -16015.0 | 17452 | -19.1 | 20.8 |
| ST1 - V2 - ST2 LCK | -17324.0 | 16732 | -20.6 | 19.9 |
| ST1 - V3 - ST2 LCK | -17443.0 | 17257 | -20.8 | 20.5 |
| ST2 - V1 - ST1 LCK | -32768.0 | 32767.0 | -9.8 | 9.8 |
| ST2 - V2 - ST1 LCK | -32768.0 | 32767.0 | -9.8 | 9.8 |
| ST2 - V3 - ST1 LCK | -32768.0 | 32767.0 | -9.8 | 9.8 |

|  | CPS read out | Calculated after calibration |
| --- | --- | --- |
| Sensors | "-RZ" (Counts) | "+RZ" (Counts) | "-RZ" (mil) | "+RZ" (mil) |
| ST1 - H1 - ST2 LCK | 14252.0 | -10172.0 | 17.0 | -12.1 |
| ST1 - H2 - ST2 LCK | 15661.0 | -17769.0 | 18.6 | -21.2 |
| ST1 - H3 - ST2 LCK | 17458.0 | -12369.0 | 20.8 | -14.7 |
| ST2 - H1 - ST1 LCK | -17069.0 | 27978.0 | -5.1 | 8.3 |
| ST2 - H2 - ST1 LCK | -32768.0 | 20060.0 | -9.8 | 6.0 |
| ST2 - H3 - ST1 LCK | -18637.0 | 28206.0 | -5.5 | 8.4 |

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 4.2 - Test Nº2 – Push “locally”

| Sensors | Push in positive direction | Push in negative direction | Mil | Mil | Railing | Actuator Gap Check |
| --- | --- | --- | --- | --- | --- | --- |
| ST1 - H1 | -21000 | 16158 | -25 | 19 |  | OK |
| ST1 - H2 | -20731 | 16790 | -25 | 20 |  | OK |
| ST1 - H3 | -17324 | 18257 | -21 | 22 |  | OK |
| ST1 - V1 | 19279 | -23239 | 23 | -28 |  | OK |
| ST1 - V2 | 22434 | -24887 | 27 | -30 |  | OK |
| ST1 - V3 | 22075 | -26512 | 26 | -32 |  | OK |
| ST2 - H1 | 32767 | -32768 | 10 | -10 | X | OK |
| ST2 - H2 | 32767 | -32768 | 10 | -10 | X | OK |
| ST2 - H3 | 32767 | -32768 | 10 | -10 | X | OK |
| ST2 - V1 | 32767 | -32765 | 10 | -10 | X | OK |
| ST2 - V2 | 32767 | -32768 | 10 | -10 | X | OK |
| ST2 - V3 | 32767 | -32768 | 10 | -10 | X | OK |

Table 13 - Stages range of motion – “Push locally”

Acceptance criteria:

- The vertical sensor readout must be positive when the optical table is pushed in the +Z direction

- The horizontal sensor readout on Stage 2 must be positive when the optic table is pushed in the +RZ direction

- Step 4.2

  - Absolutes value of all estimated motions must be higher than 15000counts for stage 1 (~0.018”)

  - Absolutes value of all estimated motions must be higher than 32000counts for stage 2 (~0.010”)

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 5 - Sensors Powespectra

The geophones powerspectra have been measured and can be found in the SVN:

/seismic/BSC-ISI/X2/BSC3/Data/Figures/Spectra/Undamped/

- LLO_ISI_BSC3_Powerspectra_ct_ST1_Unlocked_ST2_Unlocked_2012_09_26.fig

- LLO_ISI_BSC3_Powerspectra_ct_ST1_Locked_ST2_Locked_2012_09_26.fig

- LLO_ISI_BSC3_Powerspectra_ct_ST1_Locked_ST2_Unlocked_2012_09_26.fig

- LLO_ISI_BSC3_Powerspectra_ct_ST1_Unlocked_ST2_Locked_2012_09_26.fig

- LLO_ISI_BSC3_Tilted_ASD_CT_LOC_ST1_L4C_2012_10_01.fig

- LLO_ISI_BSC3_Tilted_ASD_m_LOC_ST1_L4C_2012_10_01.fig

- LLO_ISI_BSC3_Tilted_ASD_CT_LOC_ST2_GS13_2012_10_01.fig

- LLO_ISI_BSC3_Tilted_ASD_m_LOC_ST2_GS13_2012_10_01.fig

/seismic/BSC-ISI/X2/BSC3/Data/Spectra/Undamped

- LLO_ISI_BSC3_ASD_m_LOC_CPS_T240_L4C_GS13_2012_09_24_205825.mat

- LLO_ISI_BSC3_ASD_m_L4C_GS13_Stage_Tilted_2012_10_01.mat

Stage locked – unlocked

The powerspectra are measured in four different configurations:

- Stage 1 locked – Stage 2 locked

- Stage 1 unlocked – Stage 2 locked

- Stage 1 locked – Stage 2 unlocked

- Stage 1 unlocked – Stage 2 unlocked

The series of plots below present calibrated powerspectra:

- The de-whitening filters are suppressed

Figure 10: Spectra Stage 1 Locked Stage 2 Locked

Figure 11: Spectra Stage 1 Unlocked Stage 2 Locked

Figure 12: Spectra Stage 1 Locked Stage 2 Unlocked

Figure 13: Spectra Stage 1 Unlocked Stage 2 Unlocked

Stage Tilted

The powerspectra are measured when the ISI is unlocked a mass is placed on stage 2 to tilt Stage 1 and Stage 2.

The six configurations are the following in six different configurations:

- Mass placed in the actuator pocket at corner 1

- Mass placed in the pocket under the blade 0-1 at corner 1

- Mass placed in the actuator pocket at corner 2

- Mass placed in the pocket under the blade 0-1 at corner 2

- Mass placed in the actuator pocket at corner 3

- Mass placed in the pocket under the blade 0-1 at corner 3

Figure 14 - ST1 L4C – Tilted

Figure 15 - ST1 GS13 – Tilted

## Step 6 - Coil Driver, cabling and resistance check

Resistances of the couple actuator + cables are reported in the table below:

| Actuator | Coil driver name | Resistance (Ω) |
| --- | --- | --- |
| ST1 H1 | Coil1 Coarse 1 | 6.7 |
| ST2 H1 | Coil 1 Fine 1 | 10.7 |
| ST2 V1 | Coil 1 Fine 2 | 10.6 |
| ST1 V1 | Coil 1 Coarse 2 | 6.7 |
| ST1 H2 | Coil 2 Coarse 1 | 6.8 |
| ST2 H2 | Coil 2 Fine 1 | 10.5 |
| ST2 V2 | Coil 2 Fine 2 | 11 |
| ST1 V2 | Coil 2 Coarse 2 | 6.7 |
| ST1 H3 | Coil 3 Coarse 1 | 6.6 |
| ST2 H3 | Coil 3 Fine 1 | 10.9 |
| ST2 V3 | Coil 3 Fine 2 | 10.8 |
| ST1 V3 | Coil 3 Coarse 2 | 6.8 |

Acceptance criteria:

- For the actuators of stage 1, the measured resistance between the middle pin and one side pin must be 6.3 +/-0.5 ohms

- For the actuators of stage 2, the measured resistance between the middle pin and one side pin must be 10.3 +/-0.5 ohms

- Actuator neutral pins must be connected on pin #1 (left side pin of the plug)

- Actuator drive pins must be connected on pin #2 (middle pin of the plug)

- Actuator ground shield pins must be connected on pin #3 (right pin of the plug)

- All LEDs on the coil driver front panel must be green the binary input bit must be in the upper state.

Test result:	Passed:      	Failed:    X     .	Waived :.     .

## Step 7- Actuators Sign and range of motion (Local drive)

## Step 7.1 - Actuators sign

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 7.2 - Range of motion - Local drive

In this step, range of motion of the two stages is checked when applying a local drive (30000 counts) on actuators.

| Sensor readout (counts) | Negative drive | no drive | Positive drive | Amplitude count | mil |
| --- | --- | --- | --- | --- | --- |
| ST1 - H1 | -16875 | 498 | 16044 | 32919 | 39 |
| ST1 - H2 | -15944 | 1 | 16975 | 32919 | 39 |
| ST1 - H3 | -15162 | -462 | 17430 | 32592 | 39 |
| ST1 - V1 | -14887 | 174 | 15160 | 30047 | 36 |
| ST1 - V2 | -14703 | 395 | 15414 | 30117 | 36 |
| ST1 - V3 | -15290 | 1012 | 17183 | 32473 | 39 |
| ST2 - H1 | -9241 | 943 | 11042 | 20283 | 6 |
| ST2 - H2 | -8897 | 1164 | 11222 | 20119 | 6 |
| ST2 - H3 | -9103 | 725 | 10527 | 19630 | 6 |
| ST2 - V1 | -10648 | 1315 | 13156 | 23804 | 7 |
| ST2 - V2 | -10469 | 1388 | 13255 | 23724 | 7 |
| ST2 - V3 | -11000 | 782 | 12564 | 23564 | 7 |

Table 14 - Range of motion - Local drive

Acceptance criteria:

- Amplitude must be at least 32000 counts (+/-0.02”) for H Stage 1 CPS

- Amplitude must be at least 29000 counts (~0.010”) for V Stage 1 CPS

- Amplitude must be at least 19000 counts (+/-0.02”) for H Stage 2 CPS

- Amplitude must be at least 23000 counts (~0.010”) for V Stage 2 CPS

- Signs of actuators drive and sensors read out have to be the same

Note: The motion of the platform can be computed. For a 30000 counts drive in the +Z direction, the platform should move by 12.6 mil on Stage 1 and 3.6mil on Stage 2.

In the Cartesian basis, the platform should move (calculation) by:

| Stage 1 - Platform move for 32K counts drive: | 12.63 | mil |
| --- | --- | --- |
| Stage 2 - Platform move for 32K counts drive: | 3.59 | mil |

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 8 - Vertical Sensor Calibration

This test is inaccurate due to the important hysteresis introduced by the dial indicators. Moreover, the sensors calibrations have been checked at LASTI. This test has not been performed on LLO Unit 2.

Test result:	Passed:      	Failed:         .	Waived :.   X   .

## Step 9 - Vertical Spring Constant

This test is realized by loading the ISI when one stage is locked and using the capacitive position sensors as reference.

The stiffness measurements of the spring are reported in the tables below. The nominal blade stiffness are:

- Stage 1: 1241lb/in

- Stage 2: 1465lb/in

Blade Stage 0-1

Stage 2 Locked & Stage 1 Unlocked. Stage 1 is loaded with 3 x 10Kg masses and the measurements are repeated three times (by rotating the masses).

|  | No load | Load 15 Kg | Load 30Kg | Diff 1 | Diff 2 |
| --- | --- | --- | --- | --- | --- |
| V1 | 299.91 | 0.00 | -14898.67 | -299.91 | -15198.58 |
| V2 | 590.17 | 0.00 | -14459.33 | -590.17 | -15049.50 |
| V3 | 1345.10 | 0.00 | -13750.33 | -1345.10 | -15095.43 |

| -15114.50444 | count |
| --- | --- |
| -17.99345767 | mil |
| -1224.135579 | lb/in |
| 1.358938067 | % |

The blades from stage 0 to stage 1 are too soft by 1.35%.

Blade Stage 1-2

Stage 1 Locked & Stage 2 Unlocked. Stage 2 is loaded with 3 x 5Kg masses and the measurements are repeated three times (by rotating the masses).

|  | No load | Load | Diff |
| --- | --- | --- | --- |
| V1 | 2233.10 | -23029.67 | 25262.77 |
| V2 | 1935.30 | -23403.67 | 25338.97 |
| V3 | 1489.80 | -23895.33 | 25385.13 |

| 25328.96 | count |
| --- | --- |
| 7.54 | mil |
| 1448.19326 | lb/in |
| 1.147217777 | % |

The blades from stage 1 to stage 2 are too soft by 1.14%.

Note:

A dirty assembly was build at LASTI for fit-check and testing purpose before the first assembly at LHO & LLO. During balancing, the total added mass on top of stage 2 to simulate the payload was far from nominal. Investigations on the blades stiffness showed an extra softness of the blade of both stages. But the mass deduction to compensate this extra softness didn’t explain the difference with the nominal payload. In order to be closer to the nominal payload, the angles of the blade spacers were corrected (correction equivalent to +253lb on stage 0-1 blade and +507lb on stage 1-2 blade). These discrepancies between the initial design and assembly can be explained by:

- Inaccuracy in Solidworks estimation. It might underestimate masses of actual components (metal parts, hardware, instruments...)

- Measurement errors of the blade stiffness

- Machining errors (launch angles, assembly stack up...)

- Extra compliance due to the stages deformation

This is the third Unit built at LLO, but the first one using Silver Plated Eastwood SHCS to clamp the Spring Blade which allows a better friction coefficient and thus for the same torque value more clamping force than with the previous Stainless Eastwood Bolts. Since our first Unit, we also use oversized .5015” dowel pins, with the Blade brought as far back as possible to guarantee repeatability.

The very good results on the Mass Budget and on this Vertical Spring Constant Test show us that switching from the Stainless to the Silver Plated Bolts was the right decision!

Facts:

- Nominal load on Stage 0-1 blades is 8240 lb (per initial design estimation)

- -1.35% of 8240 lb is -111.24 lbs.

- +253 lb are compensated per ST1 - launch angle correction (E1100284, line 9)

- So we should be at +253-111.24= 142 lb over nominal (64kg).

But in reality, we are 80 kg too light, so we have 80 + 64 = 144 kg unexplained!

Therefore, we will have another iteration of angled Blade Spacers made for our last two Units, with different launching angle to try to come closer to the Plan.

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 10 - Static Testing (Tests in the local basis)

The table below shows the main and the cross-coupling when the actuators are driven in the local basis:

The static tests results are reported in the SVN at :

/seismic/BSC-ISI/X2/BSC3/Data/Static_Tests/

- LLO_ISI_BSC3_Offset_Local_Drive_20120926.mat

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST1 - H1 | ST1 - H2 | ST1 - H3 | ST1 - V1 | ST1 - V2 | ST1 - V3 |
| Actuators | ST1 - H1 | 4366.9 | 1762.3 | 1756.9 | 22.3 | -21.9 | -9.3 |
|  | ST1 - H2 | 1757.6 | 4376.1 | 1761.9 | -1.9 | -4.5 | -17.3 |
|  | ST1 - H3 | 1742.9 | 1758.3 | 4338.5 | 2.4 | 6.1 | 17.2 |
|  | ST1 - V1 | 73.5 | -151.6 | 119.1 | 3540.7 | -658.7 | -650.4 |
|  | ST1 - V2 | 108.4 | 36.9 | -159.0 | -631.0 | 3529.7 | -695.8 |
|  | ST1 - V3 | -152.8 | 117.1 | 79.1 | -664.1 | -625.3 | 3803.9 |

Table 15 - Static test - Local to local - Stage 1

Table 16: Static Test – Local to Local – Stage 1 Results (min & max) from the previous BSC Units

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST1 - H1 (min, max) | ST1 - H2 (min, max) | ST1 - H3 (min, max) | ST1 - V1 (min, max) | ST1 - V2 (min, max) | ST1 - V3 (min, max) |
| Actuators | ST1 - H1 | 4333.0 | 4462.0 | 1716.0 | 1780.0 | 1744.7 | 1794.0 | -15.0 | 29.0 | -23.2 | -7.0 | 14.0 | 19.8 |
|  | ST1 - H2 | 1715.0 | 1770.8 | 4224.0 | 4393.3 | 1705.0 | 1786.2 | -15.5 | 8.5 | -22.5 | 46.2 | -8.7 | 7.0 |
|  | ST1 - H3 | 1734.0 | 1748.5 | 1716.0 | 1759.7 | 4246.0 | 4363.1 | -17.8 | 2.0 | -5.3 | 3.8 | 8.8 | 65.4 |
|  | ST1 - V1 | 33.3 | 79.0 | -184.6 | -161.6 | 75.4 | 109.0 | 3481.0 | 3587.0 | -665.0 | -616.5 | -607.9 | -588.0 |
|  | ST1 - V2 | 91.0 | 132.0 | 34.0 | 87.0 | -178.3 | -135.0 | -614.8 | -597.3 | 3385.0 | 3560.3 | -664.8 | -615.0 |
|  | ST1 - V3 | -159.1 | -102.0 | 93.0 | 128.0 | 31.0 | 76.0 | -648.9 | -591.0 | -636.0 | -570.0 | 3347.0 | 3604.1 |

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST2 - H1 | ST2 - H2 | ST2 - H3 | ST2 - V1 | ST2 - V2 | ST2 - V3 |
| Actuators | ST2 - H1 | 2389.6 | 351.6 | 353.7 | -33.6 | -46.3 | -64.9 |
|  | ST2 - H2 | 341.7 | 2365.1 | 371.0 | -15.6 | -27.2 | -81.4 |
|  | ST2 - H3 | 340.5 | 351.3 | 2313.9 | -56.5 | -33.8 | -66.4 |
|  | ST2 - V1 | 66.6 | 115.7 | -215.2 | 2769.6 | 274.8 | -106.4 |
|  | ST2 - V2 | -200.0 | 50.3 | 99.7 | -80.5 | 2599.9 | 225.5 |
|  | ST2 - V3 | 101.3 | -229.2 | 79.8 | 250.7 | -46.4 | 2707.1 |

Table 17 - Static test - Local to local - Stage 2

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST2 – H1 (min, max) | ST2 - H2 (min, max) | ST2 - H3 (min, max) | ST2 - V1 (min, max) | ST2 - V2 (min, max) | ST2 - V3 (min, max) |
| Actuators | ST1 - H1 | 2316.0 | 2439.3 | 349.5 | 383.5 | 337.0 | 371.0 | 1.7 | 18.0 | -77.9 | 50.1 | -10.4 | 36.0 |
|  | ST1 - H2 | 324.0 | 366.4 | 2338.0 | 2454.7 | 336.3 | 373.0 | -65.8 | 27.0 | -85.9 | 62.3 | -12.0 | 51.4 |
|  | ST1 - H3 | 311.0 | 406.5 | 341.5 | 411.4 | 2332.0 | 2390.7 | -77.1 | 31.0 | -79.7 | 59.4 | -134.8 | 53.9 |
|  | ST1 - V1 | 65.0 | 107.4 | 122.0 | 142.3 | -220.0 | -203.1 | 2773.0 | 3018.1 | 213.4 | 349.0 | -62.2 | 59.5 |
|  | ST1 - V2 | -244.0 | -153.0 | 68.7 | 180.9 | 94.0 | 127.0 | -161.4 | 15.1 | 2891.9 | 2937.0 | 242.7 | 400.9 |
|  | ST1 - V3 | 78.5 | 163.2 | -202.1 | -152.6 | 41.0 | 97.0 | 266.3 | 349.0 | -140.0 | -27.4 | 2830.1 | 2960.0 |

Table 18: Static Test – Local to Local – Stage 2 Results (min & max) from the previous BSC Units

Acceptance criteria:

- Main couplings readout must be positive

- Comparison with the reference tables:

  - Main coupling differences mustn’t exceed 200 counts

  - Cross coupling differences mustn’t exceed 50 counts

Reference tables for acceptance criteria:

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST1 - H1 | ST1 - H2 | ST1 - H3 | ST1 - V1 | ST1 - V2 | ST1 - V3 |
| Actuators | ST1 - H1 | 4380 | 1750 | 1750 | 0 | 0 | 0 |
|  | ST1 - H2 | 1750 | 4380 | 1750 | 0 | 0 | 0 |
|  | ST1 - H3 | 1750 | 1750 | 4380 | 0 | 0 | 0 |
|  | ST1 - V1 | 50 | -170 | 90 | 3500 | -650 | -650 |
|  | ST1 - V2 | 90 | 50 | -170 | -650 | 3500 | -650 |
|  | ST1 - V3 | -170 | 90 | 50 | -650 | -601 | 3500 |

Table - Main couplings – Static – Stage 1

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST2 - H1 | ST2 - H2 | ST2 - H3 | ST2 - V1 | ST2 - V2 | ST2 - V3 |
| Actuators | ST2 - H1 | 2401 | 360 | 360 | 0 | 0 | 0 |
|  | ST2 - H2 | 360 | 2401 | 360 | 0 | 0 | 0 |
|  | ST2 - H3 | 360 | 360 | 2377 | 0 | 0 | 0 |
|  | ST2 - V1 | 80 | 130 | -200 | 3050 | 330 | 0 |
|  | ST2 - V2 | -200 | 80 | 130 | 0 | 2950 | 330 |
|  | ST2 - V3 | 130 | -200 | 80 | 330 | 0 | 2950 |

Table - Main couplings – Static – Stage 2

Test result:	Passed:      	Failed:   X      .	Waived :.     .

## Step 11- Static Testing - In the general coordinate basis (Static test - CPS)

## Step 11.1 – Change of basis matrices from Cartesian to Local

The table below shows the main and the cross-coupling when the actuators are driven in the Cartesian basis:

The static tests results are reported in the SVN at :

/seismic/BSC-ISI/X2/BSC3/Data/Static_Tests/

- LLO_ISI_BSC3_Offset_Cartesian_Drive_20120926.mat

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST1 - H1 | ST1 - H2 | ST1 - H3 | ST1 - V1 | ST1 - V2 | ST1 - V3 |
| Actuators | ST1 - X | 1745 | -863 | -862 | 1 | -17 | -12 |
|  | ST1 - Y | 22 | 1519 | -1485 | 3 | -7 | -22 |
|  | ST1 - Z | 8 | -19 | -6 | 746 | 748 | 824 |
|  | ST1 - RX | -18 | 126 | -165 | -2937 | 2470 | 486 |
|  | ST1 - RY | -196 | 110 | 100 | -1173 | -1955 | 3310 |
|  | ST1 - RZ | 3191 | 3186 | 3172 | -12 | -24 | 8 |

Table 19 - Static test cartesian drive – Cartesian to local – Stage 1

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST1 - H1 (min, max) | ST1 - H2 (min, max) | ST1 - H3 (min, max) | ST1 - V1 (min, max) | ST1 - V2 (min, max) | ST1 - V3 (min, max) |
| Actuators | ST1 - X | 1733.6 | 1803.0 | -868.3 | -839.0 | -859.8 | -812.0 | -26.0 | 23.0 | -3.0 | 0.4 | -26.1 | 32.5 |
|  | ST1 - Y | -32.0 | 12.3 | 1493.0 | 1527.9 | -1505.1 | -1463.8 | -15.6 | 14.3 | -11.4 | 55.2 | -46.6 | -14.0 |
|  | ST1 - Z | -33.0 | -3.0 | -14.0 | 0.6 | -27.5 | 16.0 | 728.5 | 772.0 | 709.0 | 758.3 | 711.0 | 784.6 |
|  | ST1 - RX | -7.3 | 40.0 | 152.1 | 189.0 | -150.8 | -137.0 | -2918.3 | -2877.0 | 2408.0 | 2469.0 | 413.8 | 452.0 |
|  | ST1 - RY | -196.5 | -162.0 | 77.0 | 111.0 | 64.2 | 120.0 | -1185.9 | -1119.0 | -1955.6 | -1871.0 | 2959.0 | 3182.3 |
|  | ST1 - RZ | 3162.0 | 3230.0 | 3124.0 | 3229.0 | 3166.0 | 3213.3 | -20.5 | 18.0 | -32.9 | 23.0 | -27.0 | 43.6 |

Table 20 - Static test cartesian drive – Cartesian to local – Stage 1 Results (min & max) from the previous BSC Units

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST2 - H1 | ST2 - H2 | ST2 - H3 | ST2 - V1 | ST2 - V2 | ST2 - V3 |
| Actuators | ST2 - X | 665 | -1354 | 658 | -63 | 16 | 1 |
|  | ST2 - Y | 1158 | -18 | -1137 | -89 | -43 | -103 |
|  | ST2 - Z | 9 | -1 | -13 | 1019 | 956 | 929 |
|  | ST2 - RX | -276 | -25 | 283 | -2398 | 2289 | -112 |
|  | ST2 - RY | 156 | -319 | 157 | -1474 | -1257 | 2644 |
|  | ST2 - RZ | 1758 | 1766 | 1741 | -101 | 8 | -66 |

Table 21 - Static test cartesian drive – Cartesian to local – Stage 2

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST2 - H1 (min, max) | ST2 - H2 (min, max) | ST2 - H3 (min, max) | ST2 – V1 (min, max) | ST2 - V2 (min, max) | ST2 - V3 (min, max) |
| Actuators | ST2 - X | 670.0 | 716.0 | -1389.8 | -1312.0 | 653.0 | 676.0 | -34.4 | 31.0 | -79.0 | 15.0 | -77.7 | 44.0 |
|  | ST2 - Y | 1144.0 | 1198.0 | -52.5 | 18.0 | -1193.9 | -1153.0 | -33.0 | 42.0 | -136.0 | 10.0 | -62.0 | 15.0 |
|  | ST2 - Z | -3.0 | 19.9 | -15.5 | 12.1 | -33.0 | 14.0 | 1017.9 | 1133.0 | 939.0 | 1135.0 | 982.4 | 1104.0 |
|  | ST2 - RX | -312.0 | -277.0 | -3.0 | 45.5 | 243.5 | 288.0 | -2572.0 | -2469.1 | 2352.0 | 2574.0 | -153.7 | -49.0 |
|  | ST2 - RY | 116.6 | 200.0 | -405.4 | -303.0 | 116.0 | 189.0 | -1595.0 | -1499.7 | -1513.4 | -1123.3 | 2762.7 | 2972.0 |
|  | ST2 - RZ | 1738.0 | 1797.0 | 1715.0 | 1822.0 | 1728.0 | 1792.0 | -81.3 | 46.0 | -122.0 | 7.0 | -64.0 | 47.5 |

Table 22 - Static test cartesian drive – Cartesian to local – Stage 2 Results (min & max) from the previous BSC Units

Reference table static test Cartesian to local:

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST1 - H1 | ST1 - H2 | ST1 - H3 | ST1 - V1 | ST1 - V2 | ST1 - V3 |
| Actuators | ST1 - X | 1800 | -820 | -820 | 0 | 0 | 0 |
|  | ST1 - Y | 0 | 1500 | -1500 | 0 | 0 | 0 |
|  | ST1 - Z | 0 | 0 | 0 | 772 | 750 | 700 |
|  | ST1 - RX | 0 | 160 | -160 | -2950 | 2450 | 450 |
|  | ST1 - RY | -200 | 110 | 70 | -1150 | -2000 | 3050 |
|  | ST1 - RZ | 3200 | 3200 | 3200 | 0 | 0 | 0 |

Table 23 - Reference table - Cartesian to Local - Stage 1

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST2 - H1 | ST2 - H2 | ST2 - H3 | ST2 - V1 | ST2 - V2 | ST2 - V3 |
| Actuators | ST2 - X | 700 | -1350 | 650 | 0 | 0 | 0 |
|  | ST2 - Y | 1200 | 0 | -1150 | 0 | 0 | 0 |
|  | ST2 - Z | 0 | 0 | 0 | 1100 | 1100 | 1100 |
|  | ST2 - RX | -300 | 0 | 300 | -2500 | 2500 | -50 |
|  | ST2 - RY | 200 | -300 | 200 | -1500 | -1400 | 3000 |
|  | ST2 - RZ | 1800 | 1800 | 1800 | 40 | 40 | 40 |

Table 24 - Reference table - Cartesian to Local - Stage 2

Acceptance criteria:

- Comparison with the reference tables:

  - Differences mustn’t exceed 100 counts

Test result:	Passed:      	Failed:    X     .	Waived :.     .

## Step 11.2 – Base change matrices from Cartesian to Cartesian

The static tests results are reported in the SVN at :

/seismic/BSC-ISI/X2/Data/BSC3/Static_Tests/

- LLO_ISI_BSC3_Offset_Cartesian_Drive_20120926.mat

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST1 - X | ST1 - Y | ST1 - Z | ST1 - RX | ST1 - RY | ST1 - RZ |
| Actuators | ST1 - X | 1732 | -1 | -7 | -1 | -5 | 12 |
|  | ST1 - Y | -8 | 1747 | -6 | 2 | -4 | 16 |
|  | ST1 - Z | -12 | 1 | 775 | 15 | 58 | 0 |
|  | ST1 - RX | 5 | 368 | 7 | 3052 | 19 | -15 |
|  | ST1 - RY | -387 | 12 | 67 | 25 | 3188 | 12 |
|  | ST1 - RZ | -18 | 19 | -27 | 2 | 12 | 3314 |

Table 25 - Static Test - Cartesian to Cartesian – Stage 1

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST1 - X (min, max) | ST1 - Y (min, max) | ST1 - Z (min, max) | ST1 - RX (min, max) | ST1 - RY (min, max) | ST1 - RZ (min, max) |
| Actuators | ST1 - X | 1715.0 | 1772.1 | -12.4 | 9.0 | 4.1 | 10.9 | -13.5 | 6.0 | -20.6 | 1.0 | -2.0 | 59.0 |
|  | ST1 - Y | -9.1 | 8.7 | 1720.0 | 1734.4 | -12.4 | 11.0 | -10.0 | 31.2 | -54.3 | 3.0 | -4.0 | 24.4 |
|  | ST1 - Z | -15.0 | 10.2 | -8.7 | 17.0 | 729.0 | 753.0 | -25.0 | 6.2 | -27.0 | 3.9 | -14.9 | -4.0 |
|  | ST1 - RX | -6.0 | 40.8 | 351.9 | 380.0 | -25.0 | -5.2 | 2985.0 | 3058.0 | -23.5 | 7.0 | -9.0 | 29.0 |
|  | ST1 - RY | -384.6 | -342.0 | -5.6 | 16.0 | -19.7 | 5.0 | -5.0 | 17.0 | 2901.0 | 3068.7 | -5.1 | 9.8 |
|  | ST1 - RZ | -12.9 | 24.0 | -4.0 | 4.1 | -21.0 | 16.0 | -6.0 | 19.5 | -2.0 | 20.0 | 3276.0 | 3346.1 |

Table 26 - Static Test - Cartesian to Cartesian – Stage 1 Results (min & max) from the previous BSC Units

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST2 - X | ST2 - Y | ST2 - Z | ST2 - RX | ST2 - RY | ST2 - RZ |
| Actuators | ST2 - X | 1333 | 40 | -24 | 38 | 22 | -16 |
|  | ST2 - Y | 32 | 1337 | -43 | -5 | 3 | 14 |
|  | ST2 - Z | 6 | 13 | 968 | -38 | 10 | -9 |
|  | ST2 - RX | 21 | -11 | -155 | 4007 | 64 | -9 |
|  | ST2 - RY | 33 | -1 | -47 | 112 | 4086 | -8 |
|  | ST2 - RZ | -13 | 18 | -69 | 21 | 2 | 2536 |

Table 27 - Static Test - Cartesian to Cartesian – Stage 2

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST2 - X (min, max) | ST2 - Y (min, max) | ST2 - Z (min, max) | ST2 - RX (min, max) | ST2 - RY (min, max) | ST2 - RZ (min, max) |
| Actuators | ST2 - X | 1317.0 | 1377.4 | -16.2 | 25.0 | -53.4 | 29.0 | -22.0 | 55.5 | -18.6 | 24.0 | -10.1 | 24.0 |
|  | ST2 - Y | -10.0 | 13.0 | 1331.0 | 1358.0 | -53.2 | 20.0 | -53.0 | 59.0 | -41.6 | 55.0 | -26.2 | 34.0 |
|  | ST2 - Z | -6.0 | 24.9 | -17.2 | 2.0 | 1022.5 | 1114.0 | -91.0 | 52.7 | -73.0 | 28.0 | -18.0 | 14.0 |
|  | ST2 - RX | -62.3 | 8.0 | -31.1 | -8.5 | -98.0 | 22.0 | 4223.0 | 4356.2 | -105.3 | 58.0 | -18.0 | 26.2 |
|  | ST2 - RY | -8.0 | 40.3 | -17.8 | 30.0 | -127.1 | 56.9 | 15.0 | 241.5 | 4055.2 | 4319.0 | -39.2 | 24.0 |
|  | ST2 - RZ | -9.5 | 21.0 | -7.2 | 9.0 | -71.6 | 29.0 | -35.0 | 73.9 | -28.9 | 52.0 | 2509.0 | 2602.0 |

Table 28 - Static Test - Cartesian to Cartesian – Stage 2 Results (min & max) from the previous BSC Units

Reference table static test Cartesian to Cartesian:

|  |  | Sensors |
| --- | --- | --- |
|  |  | ST1 - X | ST1 - Y | ST1 - Z | ST1 - RX | ST1 - RY | ST1 - RZ |
| Actuators | ST1 - X | 1750 | 0 | 0 | 0 | 0 | 0 |
|  | ST1 - Y | 0 | 1750 | 0 | 0 | 0 | 0 |
|  | ST1 - Z | 0 | 0 | 750 | 0 | 0 | 0 |
|  | ST1 - RX | 0 | 375 | 0 | 3000 | 0 | 0 |
|  | ST1 - RY | -375 | 0 | 0 | 0 | 3000 | 0 |
|  | ST1 - RZ | 0 | 0 | 0 | 0 | 0 | 3300 |
|  |  | Sensors |
|  |  | ST2 - X | ST2 - Y | ST2 - Z | ST2 - RX | ST2 - RY | ST2 - RZ |
| Actuators | ST2 - X | 1350 | 10 | 30 | 0 | 25 | 20 |
|  | ST2 - Y | -10 | 1350 | 20 | -25 | 0 | 20 |
|  | ST2 - Z | 0 | 0 | 1100 | -10 | -30 | 20 |
|  | ST2 - RX | 10 | -15 | 20 | 4300 | 30 | 20 |
|  | ST2 - RY | 30 | 0 | 30 | 40 | 4300 | 20 |
|  | ST2 - RZ | 0 | 10 | 30 | -25 | -15 | 2600 |

Acceptance criteria:

- Main couplings readout must be positive

- Comparison with the reference tables:

  - Main coupling differences mustn’t exceed 200 counts

  - Cross coupling differences mustn’t exceed 50 counts

Note: We have highlighted in yellow the values that don’t satisfy the acceptance criteria. But by comparing these values with the ones from the previous Units built at LHO and LLO, we can clearly see that they are similar to our previous results and therefore acceptable!

Test result:	Passed:      	Failed:    X     .	Waived :.     .

## Step 12 - Linearity test

The linearity test figure are reported in the SVN at :

/seismic/BSC-ISI/X2/BSC3/Data/Figures/Linearity_Test/

- LLO_ISI_BSC3_Linearity_test_20121004.fig

- LLO_ISI_BSC3_Linearity_test_20121004.pdf

Figure 16 - Linearity Test

Slope – Offset:

|  |  | Slope | Offset | Average slope | Variation from average (%) |
| --- | --- | --- | --- | --- | --- |
| Stage 1 | ST1 - H1 | 0.62119 | 303 | 0.6195 | 0.271 |
|  | ST1 - H2 | 0.62351 | -333 |  | 0.645 |
|  | ST1 - H3 | 0.61384 | -686 |  | -0.916 |
|  | ST1 - V1 | 0.50231 | 325 | 0.5165 | -2.755 |
|  | ST1 - V2 | 0.50374 | 549 |  | -2.477 |
|  | ST1 - V3 | 0.54356 | 1335 |  | 5.232 |
| Stage 2 | ST2 - H1 | 0.34062 | 987 | 0.3356 | 1.488 |
|  | ST2 - H2 | 0.33679 | 1078 |  | 0.346 |
|  | ST2 - H3 | 0.32947 | 614 |  | -1.834 |
|  | ST2 - V1 | 0.39743 | 2270 | 0.3974 | 0.014 |
|  | ST2 - V2 | 0.39906 | 2014 |  | 0.422 |
|  | ST2 - V3 | 0.39565 | 1603 |  | -0.436 |

Table - Slopes and offset of the triplet Actuators - BSC-ISI - Sensors

Previous Results:

| Averages (LHO Unit 1 & 2, LLO Unit 1 & 2) | Comparisons with LLO Unit 3 |
| --- | --- |
|  |  | Slope | Offset | Average slope | Standard Deviation to Average Slope | % Slope Previous Units/ LLO Unit 3 Slope | % Average Slope of Previous Units / LLO Unit 3 Average Slope |
| Stage 1 | ST1 - H1 | 0.631 | 36.584 | 0.624 | 0.002 | -1.538 | -0.68 |
|  | ST1 - H2 | 0.622 | -130.014 |  |  | 0.201 |  |
|  | ST1 - H3 | 0.618 | 60.969 |  |  | -0.719 |  |
|  | ST1 - V1 | 0.503 | 292.270 | 0.501 | 0.003 | -0.138 | 2.95 |
|  | ST1 - V2 | 0.501 | 693.317 |  |  | 0.495 |  |
|  | ST1 - V3 | 0.500 | 268.249 |  |  | 8.106 |  |
| Stage 2 | ST2 - H1 | 0.345 | 899.569 | 0.343 | 0.002 | -1.286 | -2.11 |
|  | ST2 - H2 | 0.343 | 1702.082 |  |  | -1.845 |  |
|  | ST2 - H3 | 0.341 | 2331.741 |  |  | -3.348 |  |
|  | ST2 - V1 | 0.423 | -878.881 | 0.419 | 0.003 | -6.433 | -5.43 |
|  | ST2 - V2 | 0.418 | 365.397 |  |  | -4.810 |  |
|  | ST2 - V3 | 0.415 | -111.935 |  |  | -4.892 |  |

Looking at the average Slopes from the Previous BSC-ISI Units, we can see that this Unit follows the general trend.

Acceptance criteria:

- Horizontal and vertical slopes of the triplet actuators x BSC-ISI x sensors:  Average slope +/- 2.5%

Note: The variation from average value on Stage 1 V1 and V3 is a little bit high (especially V3), such that we fail this test but looking at the comparisons with averages from the Previous Units, we can conclude that it is acceptable (within ~8%).

In order to find why Stage 1 V3 has a slightly different slope than the other Stage 1 V, we did a test that consists of driving Stage V3 in normal conditions and re-do this step with a different CPS box (Stage 1 H3) to make sure it is not coming from the CPS. With both a positive and a negative drive, we got very similar results, so in conclusion, this issue comes from the actuator V3.

Test result:	Passed:      	Failed:    X     .	Waived :.     .

## Step 13 – Transfer functions – Local to Local

Data files measurement of local to local transfer functions in SVN at:

/svncommon/SeiSVN/seismic/BSC-ISI/X2/BSC3/Data/Transfer_Functions/Measurements/Undamped

- LLO_ISI_BSC3_Data_L2L_10Hz_100Hz_ST1_ST2_20120927-153448.mat

- LLO_ISI_BSC3_Data_L2L_100mHz_700mHz_ST1_ST2_20120927-181139.mat

- LLO_ISI_BSC3_Data_L2L_700mHz_10Hz_ST1_ST2_20120928-015730.mat

- LLO_ISI_BSC3_Data_L2L_10mHz_100mHz_ST1_ST2_20120927-233431.mat

- LLO_ISI_BSC3_Data_L2L_100Hz_500Hz_ST1_ST2_20120927-141457.mat

- LLO_ISI_BSC3_Data_L2L_500Hz_1000Hz_ST1_ST2_20120927-131030.mat

Script file for processing and plotting local to local transfer functions in SVN at:

/seisvn/seismic/BSC-ISI/X2/Scripts/Control_Scripts

- Step_1_TF_L2L_10mHz_1000Hz_LLO_ISI_BSC2.m

Figures of local to local transfer functions (Main couplings) in SVN at:

/seisvn/seismic/BSC-ISI/X2/BSC3/Data/Figures/Transfer_Functions/Measurements/Undamped

- LLO_ISI_BSC3_TF_L2L_Raw_from_ST1_ACT_to_ST1_CPS_2012_09_28.fig

- LLO_ISI_BSC3_TF_L2L_Raw_from_ST1_ACT_to_ST1_L4C_2012_09_28.fig

- LLO_ISI_BSC3_TF_L2L_Raw_from_ST2_ACT_to_ST2_CPS_2012_09_28.fig

- LLO_ISI_BSC3_TF_L2L_Raw_from_ST2_ACT_to_ST2_GS13_2012_09_28.fig

Measured of local to local transfer functions in the SVN at:

/svncommon/seisvn/seismic/BSC-ISI/X2/BSC3/Data/Transfer_Functions/Simulations/Undamped

- LLO_ISI_BSC3_TF_L2L_Raw_10mHz_1000Hz_2012_06_06.mat

Note 1:  The transfer functions are measured from the Output filter bank (excitation variable) to the input (IN1) of the input filter bank. The transfer functions presented below are raw transfer functions without any electronic compensation of the sensor electronic. The actuator and the coil driver electronic compensation are introduced in these transfer functions.

Note 2: The L4Cs are out of phase (should be -90 before 1Hz). A minus sign is added in the calibration filters that convert count to nm/s.

Note 3: We don’t see any resonance of the Test Stand at 16Hz on Stage 1 CPS like LHO did.

Note 4: The first high frequency resonance observed on stage 1 by the L4C is at 216.4Hz. The next resonance is observed at 247.8Hz. The first mode of the blade has been measured at ~250Hz at LASTI, but it shouldn’t be the Blades’ resonances thanks to the Tuned Mass Dampers (tuned at 253 ± 4 Hz Hz) already installed on Stage 0-1 Blades on this Unit.

Note 5: There is a poor coherence on the GS13 transfer functions. It can be explained by the weak drive of the fine actuators. Moreover, the stage 2 of the ISI is strongly excited by the fans of the clean rooms. These two factors strongly affect the quality of the measurements. Also, we might have an issue with the GS-13 gain because they were saturating a lot, which can also explain the poor quality of the signal.

Note 6: On the ST2-ACT to ST2-GS13 transfer functions, the first high frequency resonances are observed at 120Hz (electric noise, harmonic of 60Hz?) and 141Hz.

Figure 21: TF L2L Raw - ST1 Act to ST1 CPS

Figure 22: TF L2L Raw - ST1 Act to ST1 L4C

Figure 23: TF L2L Raw - ST2 Act to ST2 CPS

Figure 24: TF L2L Raw - ST2 Act to ST2 GS13

We then also decided to compare these results with previous Units (LHO BSC8 & LLO BSC2).

Figure 25: TF L2L Comparison between LLO BSC 3 & LHO BSC 8 & BSC 2 – H ST1 Actuator to ST1 CPS

Figure 26: TF L2L Comparison between LLO BSC 3 & LHO BSC 8 & BSC 2 – H ST1 Actuator to ST1 L4C

Figure 27: TF L2L Comparison between LLO BSC 3 & LHO BSC 8 & BSC 2 – V ST1 Actuator to ST1 CPS

Figure 28: TF L2L Comparison between LLO BSC 3 & LHO BSC 8 & BSC 2 – V ST1 Actuator to ST1 L4C

Figure 29: TF L2L Comparison between LLO BSC 3 & LHO BSC 8 & BSC 2 – H ST2 Actuator to ST2 CPS

Figure 30: TF L2L Comparison between LLO BSC 3 & LHO BSC 8 & BSC 2 – H ST2 Actuator to ST2 GS13

Figure 31: TF L2L Comparison between LLO BSC 3 & LHO BSC 8 & BSC 2 – V ST2 Actuator to ST2 CPS

Figure 32: TF L2L Comparison between LLO BSC 3 & LHO BSC 8 & BSC 2 – V ST2 Actuator to ST2 GS13

By comparing it to BSC 8 & BSC 2, we can conclude that BSC 3 is in the general trend of the previous BSCs built!

Test result:	Passed:   X   	Failed:         .	Waived :.     .

Due to schedule pressure, it was decided it was reasonable to postpone the following tests. They will be performed during Phase II.

## Step 14 - Symmetrization – Calibration

Not performed

## Step 15 – Change of base – Cartesian to Local - Simulations

Not performed

## Step 16- Transfer functions - Cartesian to Cartesian - Measurements

Not performed

## Step 17 - Lower Zero Moment Plan

## Step 17.1 - Stage 1 - LZMP

Not performed

## Step 17.2 - Stage 2 - LZMP

Not performed

## Step 18- Damping Loops – Transfer function – Simulations

## Step 18.1 - Damping Loops – Stage 2

Not performed

## Step 18.2 - Damping Loops – Stage 1

Not performed

## Step 19- Damping Loops – Powerspectra

Data files measurement of damping Power Spectra in SVN at:

/svncommon/SeiSVN/seismic/BSC-ISI/X2/BSC3/Data/Spectra/Damping

- LLO_ISI_BSC3_ASD_m_L4C_GS13_Undamped_vs_Damping_2012_10_04_090654.mat

Figures of local to local transfer functions (Main couplings) in SVN at:

/seisvn/seismic/BSC-ISI/X2/BSC3/Data/Figures/Spectra/Damping

- LLO_ISI_BSC3_ASD_CT_CART_ST1_L4C_Undamped_vs_Damping_2012_10_04_090654.fig

- LLO_ISI_BSC3_ASD_m_CART_ST1_L4C_Undamped_vs_Damping_2012_10_04_090654.fig

- LLO_ISI_BSC3_ASD_CT_CART_ST2_GS13_Undamped_vs_Damping_2012_10_04_090654.fig

- LLO_ISI_BSC3_ASD_m_CART_ST2_GS13_Undamped_vs_Damping_2012_10_04_090654.fig

Figure 33: LLO ISI BSC3 ASD CT CART Stage 1 L4C Undamped vs Damping

Figure 34: LLO ISI BSC2 ASD m CART Stage 1 L4C Undamped vs Damping

Figure 35: LLO ISI BSC3 ASD CT CART Stage 2 GS 13 Undamped vs Damping

Figure 36: LLO ISI BSC3 ASD m CART Stage 2 GS 13 Undamped vs Damping

Test result:	Passed:   X   	Failed:         .	Waived :.     .

## Step 20- Isolation Loops – for one unit per site

Not performed

# BSC-ISI testing Summary

This is the second “aLigo BSC-ISI” tested at LLO. The testing procedure document E1000483-v3 was used. Tests were done during September & October 2012.

The ISI-BSC3 is officially validated per the tests presented in this report. All results are posted on the SVN at:

https://svn.ligo.caltech.edu/svn/seismic/BSC-ISI/X2/BSC3/Data

FAILED AND WAIVED TESTS

- List of tests that failed/waived and won’t be redone

- List of tests that failed/waived, that need to be re-done during phase 2

- Step III. 6 Coil Driver, Cabling and Resistance Check – This test fails by a very small amount but to be safe we will re-do it in the LVEA.

- Step III. 10 & 11 Static Testing – These tests fail but not by much and looking at the average values obtained from the previous Units, we can conclude that the criteria is maybe a little bit too strong.

- Step III. 12 Linearity Test – This test fails on Stage 1 V1 & V3 Actuators. V1 result is acceptable but V3 is twice as high as the criteria, so we’ll keep an eye on it and re-do this test in the LVEA. It is more than likely that this test failed because of the actuator V3. We will keep an eye on it and like it is said above, re-check Step 6 Coil Driver, Cabling and Resistance Check.

- List of tests skipped that won't be performed because not feasible during phase II (i.e. stage 0 leveling)

- Step II.5 – Check level of Stage 0 after top-bottom plate assembly

- Step II.8 – Blade 0-1 Post Launch Angle – No need for this test, the budget mass looks good and we already reposition the Blades after noticing a gap between the Blade and its Spacer on Stage 0-1 (see comment on Step 9 – Vertical Spring Constant).

- List of tests skipped that we won't do because they are not essential (i.e. redundant with another test)

- Step III.3 – Measure the Sensor gap - This test was not performed. The sensor gaps have not been measured. These sensors have already been checked at LASTI. Moreover, risks of scratching the target are so high that we preferred not performing this test. In the future, this test will be removed from the testing procedure.

- Step III.8 – Vertical sensor calibration - The test is not realized in a proper way to evaluate accurately the calibration of the vertical CPS.

- Lists of tests skipped that needs to be done during phase II.

- Step III.14 – Symmetrization – Calibration

- Step III.15 – Change of bases – Cartesian to local - Simulations

- Step III.16 – Transfer functions – Cartesian to Cartesian - Simulations

- Step III.17 – Lower Zero Moment Plan

- Step III.18.1 – Damping Loops – Stage 2

- Step III.18.2 – Damping Loops – Stage 1

- Step III.20 – Isolation loops

The ISI-BSC will be moved from the HighBay to the LVEA test stand as soon as it has been approved.