## Slide 1: Actuator Sizing of a Quad Pendulum for Gravitational Wave Detectors
Brett Shapiro
Kamal Youcef-Toumi
Nergis Mavalvala
ACC 2011 – San Francisco
June 29

## Slide 2: Gravitational Waves
Pulsar
Supernova
Merging Black Holes
Supernovae
  Asymmetry required
Coalescing Binaries
  Black Holes or Neutron Stars
  Mergers
Pulsars
    Asymmetry required
Stochastic Background
(Big bang, etc.)
Wave of strain amplitude h
Notes: GWs are predicted by Einstein’s theory of General Relativity.
Produced from accelerating mass, analogous to accelerating charges producing EM
Weakly interacting, so only very energetic massive events such as supernovae, merging black holes, or pulsars can be reasonably detected.

## Slide 3: The Laser Interferometer Gravitational-wave Observatory (LIGO)
Livingston, LA
Hanford, WA
3, 4 km and long interferometers at 2 sites in the US
Michelson interferometers with
Fabry-Pérot arms
Optical path enclosed in vacuum
Sensitive to displacements around 10-19mrms
Funded by

## Slide 4
LIGO Scientific Collaboration
Australian Consortium for Interferometric Gravitational Astronomy
The Univ. of Adelaide
Andrews University
The Australian National Univ.
The University of Birmingham
California Inst. of Technology
Cardiff University
Carleton College
Charles Sturt Univ.
Columbia University
CSU Fullerton
Embry Riddle Aeronautical Univ.
Eötvös Loránd University
University of Florida
German/British Collaboration for the Detection of Gravitational Waves
University of Glasgow
Goddard Space Flight Center
Leibniz Universität Hannover
Hobart & William Smith Colleges
Inst. of Applied Physics of the Russian Academy of Sciences
Polish Academy of Sciences
India Inter-University Centre for Astronomy and Astrophysics
Louisiana State University
Louisiana Tech University
Loyola University New Orleans
University of Maryland
Max Planck Institute for Gravitational Physics
University of Michigan
University of Minnesota
The University of Mississippi
Massachusetts Inst. of Technology
Monash University
Montana State University
Moscow State University
National Astronomical Observatory of Japan
Northwestern University
University of Oregon
Pennsylvania State University
Rochester Inst. of Technology
Rutherford Appleton Lab
University of Rochester
San Jose State University
Univ. of Sannio at Benevento, and Univ. of Salerno
University of Sheffield
University of Southampton
Southeastern Louisiana Univ.
Southern Univ. and A&M College
Stanford University
University of Strathclyde
Syracuse University
Univ. of Texas at Austin
Univ. of Texas at Brownsville
Trinity University
Tsinghua University
Universitat de les Illes Balears
Univ. of Massachusetts Amherst
University of Western Australia
Univ. of Wisconsin-Milwaukee
Washington State University
University of Washington

## Slide 5: Quadruple Pendulum
Copyright Science and Technology Facilities Council (UK)
Test Mass
40 Kg
≈2 m
Prototype quad pendulum

## Slide 6: Quadruple Pendulum (Quad) Isolation
K2
K1
K1
K2
K3
K3
0.5M
M
M
0.5M
xg(t)
x4(t)
x4(s)/xg(s)
steep roll off!
K4
K4

## Slide 7: Actuator Frequency Response
u1
u2
u3
u4
205 mN DC
205 mN DC
3.4 mN DC
0.095 mN
Electromagnetic actuator
Electrostatic actuator

## Slide 8: Location of Quadruple Pendulums

## Slide 9: Advanced LIGO Sensitivity

## Slide 10: Outline
Gravitational Waves and LIGO
Quadruple Pendulum
Quad Pendulum Actuator Specifications
Actuator Sizing
Conclusion

## Slide 11: Optical Arm Cavity Control
Laser
(4+ ) km
Reflected beam
Photodiode
Incident beam
100 W
Cavity Resonant beam
800 kW
Pendulum 2
Pendulum 1
Control Law
Error Signal
Actuation
Goal:
u1
u2
u3
u4
High sensitivity means a limited operating point.
1064 nm
near infrared
Actuator size considerations
Large enough to position mirrors
Small enough to limit noise, cost, and complexity

## Slide 12: Optical Arm Cavity Control
Pendulum 2
Pendulum 1
u1
u2
u3
u4
R
Standard tracking diagram

## Slide 13: Arm Control Block Diagram
± 10V
* What is the minimum baseline target size for each actuator,
without considering an infinite set of possible controller designs?

## Slide 14: Disturbance Spectrum
Goal:
LIGO sensitivity spectrum

## Slide 15: Outline
Gravitational Waves and LIGO
Quadruple Pendulum
Quad Pendulum Actuator Specifications
Actuator Sizing
Conclusion

## Slide 16: Outline
Gravitational Waves and LIGO
Quadruple Pendulum
Quad Pendulum Actuator Specifications
Actuator Sizing
Conclusion

## Slide 17: Arm Control Block Diagram
†
†
± 10V
† -> Moore-Penrose pseudoinverse

## Slide 18: Minimum Least Squares Actuation
†
The relative magnitudes between curves quantifies the relative ‘effectiveness’ of an actuator.

## Slide 19: Conclusions
The pseudoinverse of the combined plant TF shows the actuators have enough range with reasonable margin.
Also shows which actuator is most effective at each frequency.
No feedback design is required.
The pseudoinverse can guide feedback design.

## Slide 20: Back Ups

## Slide 21: Example Feedback Loop Gains
Feedback RMS (V)
3.7*10^-3
0
2*10^-2
8*10^-5

## Slide 22: Seismic Noise
Tides - ≈ 10-5 Hz
Microseismic peak - ≈ 0.1 to 0.3 Hz
Anthropogenic Noise - ≈ 1 to 10 Hz
BU

## Slide 23: Thermal Noise
m
x(t)
b = dissipation factor (damping)
T = Temperature (Kelvin)
kb = Boltzmann’s Constant
b
k
Mean energy:
(equipartition function)
System in thermal equilibrium
BU

## Slide 24: Quantized Optical Noise
Laser
Photodetector
Laser light consists of a finite (and uncertain) numbers of photons.
The momentum transfer onto the test mass from a random distribution of photons produces radiation pressure noise.
The random distribution of photons arriving at the photodetector produces shot noise.
Discrete Photons in laser beam
Test Mass
BU

## Slide 25: Actuators

## Slide 28: Advanced LIGO Schedule
Pre-assembly happening now
2010
2011
2012
2013
2014
2015
Installation
Testing
Likely first science run
Other observatories around the world collecting data during this time.

## Slide 29: Advanced LIGO
LIGO infrastructure designed for a progression of instruments
  Nominal 30 year lifetime
All subsystems to be replaced and upgraded
  More powerful laser – from 10W to 180 W
  Larger test masses – from 10 kg to 40 kg
  More aggressive seismic isolation
  Lower thermal noise coatings
Quantum noise limited in much of band
Thermal noise in most sensitive region
About factor of 10 better sensitivity
Expected sensitivity
  Neutron star inspirals to about
    200 Mpc, ~40/yr
  10 MO black hole inspirals to
  775 Mpc, ~30/y
Advanced LIGO Astronomical Reach

## Slide 30: Seismic Isolation
7 cascaded stages of seismic isolation
  External Hydraulic Pre-Isolator (HEPI). Active isolation up to 10 Hz.
  2 stage Internal Seismic Isolation (ISI). Active isolation up to 30 Hz, passive above.
  4 stage Quadruple Pendulum (Quad). Mirror is the final stage. Passive isolation above 1 Hz.
ISI and Quad in LIGO Vacuum Chamber
Prototype ISI and Quad at MIT
Overall Isolation 9 to 10 orders of magnitude at 10 Hz.

## Slide 31: Mirrors Suspend from Glass Fibers
Developed by the University of Glasgow
Suspension thermal noise suppressed by suspending low loss fused silica test masses from fused silica fibers.
0.6m long, 400 µm diameter silica fibers pulled from 3 mm diameter stock and laser welded between the two silica lower stages of the quadruple pendulum.

## Slide 32
Pendulum
Actuators
Control
Sensors
DAC
ADC
-
R
y
Super Plant
G1x4(s)
Control
C4x1(s)
Sensors
DAC
ADC
-
R
y