## Slide 1: An Overview of Control Theory and Digital Signal Processing
Luca Matone
Columbia Experimental Gravity group (GECo)
LHO Jul 18-22, 2011
LLO Aug 8-12, 2011
LIGO-G1100863

## Slide 2: Syllabus (tentative)
Day | Topic | Textbooks
1 | Control theory: Physical systems, models, linear systems, block diagrams, differential equations, feedback loops, cruise control example, MATLAB implementation. | Chau, Pao C. Process Control: A First Course with MATLAB®. Cambridge University Press, 2002. ISBN 0-521-00255-9. Ingle, Vinay K. and John G. Proakis. Digital Signal Processing using Matlab®. Brooks/Cole 2000. ISBN 0-534-37174-4. Smith, Steven W. The Scientist and Engineer’s Guide to Digital Signal Processing. California Technical Publishing 1999. http://www.dspguide.com/
2 | Control theory: Laplace transform and its inverse , transfer functions, partial fraction expansion, first-order and second-order systems, dynamic response, bode plots, stability criteria, MATLAB implementation. | 
3 | Control theory: robustness, typical compensators, noise suppression, one arm cavity lock example, MATLAB implementation and time-domain simulations with SIMULINK. | 
4 | DSP: Discrete-time signals and systems, impulse response, system stability, convolution and correlation, differential to difference equations, the Z transform, the Discrete-time Fourier Transform (DTFT), the Discrete Fourier Transform (DFT), MATLAB implementation. | 
5 | DSP: The Fast-Fourier Transform (FFT), power spectral density, sampling theorem, aliasing, analog-to-digital transformations, digital filtering, FIR filters, IIR filters, moving average filter, filter design, ADC and DACs, MATLAB implementation. | 

## Slide 3: Objective
Control System
Manages and regulates a set of variables in a system
  SISO – single-input-single-output
  MIMO – multiple-input-multiple-output
A quantity is measured then controlled
Requirements
  Bandwidth
  Rise time
  Overshoot
  Steady state error
  …

## Slide 4: Objective
Digital Signal Processing
Measure and filter an analog signal
Digital signal
  Created by sampling an analog signal
  Can be stored
Analog filters
  Cheap, fast and have a large dynamic range in both amplitude and frequency
Digital filters
  Can be designed and implemented “on-the-fly”
  Superior level of performance.
    Example: a low pass digital filter can have a gain of , a frequency cutoff at , and a gain of less than for frequencies above . A transition of !

## Slide 5: Control Theory 1
Given a physical system
  Objective: sense and control a variable in the system
Examples
  As basic as
    a car’s cruise control (SISO) or
  Not so basic as
    Locking the full LIGO interferometer (MIMO)

## Slide 6: Example: Cruise Control
Objective
  Car needs to maintain a given speed
Physical system includes
  car’s inertia
  friction
Direction of motion
Normal force (n)
Force from engine (f)
Weight (mg)
Friction force (ffr)
Force or free body diagram: allows to analyze the forces at play

## Slide 7: Physical model
Physical system described by the following equation of motion
Simplifying and assuming friction force is proportional to speed
Direction of motion
Force from engine (f)
Normal force (n)
Weight (mg)
Friction force (ffr)

## Slide 8: First-order differential equation
Solving for first-order differential equation (assuming is a constant)
  yields the solution
Direction of motion
Engine force (f)
Friction force (ffr)
Speed at regime
Time constant

## Slide 9: MATLAB implementation
  The linear differential equation describing the dynamics of the system
Using MATLAB’s Symbolic Math Toolbox
>> dsolve('m*Dy=f-b*y','y(0)=0')
ans =
(f - f/exp((b*t)/m))/b
Direction of motion
Engine force (f)
Friction force (ffr)

## Slide 10: Results:
cruise_timedomain.m

## Slide 11: Block diagram: representing the physical system
To illustrate a cause-and-effect relationship
A single block represents a physical system
Blocks are connected by lines
  Lines represent how signals flow in the system
In general, a physical system G has signal x(t) as input and signal y(t) as output
G is the transfer function of the system
G
x(t)
y(t)

## Slide 12: Car’s body
Transfer function G represents the car’s body
  G converts the force from the engine (input signal, ) to the car’s actual speed (output signal, )
    with
  Units:
G
f(t)
v(t)

## Slide 13: Setting the desired speed
Second transfer function H (the controller)
  Converts the desired speed (or reference) to a required force
  Sets the throttle
  For simplicity, H is set to a constant
  must be dimensionless
G
f
v
vr
H

## Slide 14: Plotting results
With the actual speed is the reference:
Simulate: setting desired speed to 25 m/s (55 mph)
Generated force by controller H
Resulting speed v
Desired speed vr
cruisefeedback_timedomain.m

## Slide 15: Introducing a disturbance – a hill
In the presence of a hill the equation of motion needs to be re-visited
Assuming a small angle θ
Weight (mg)
Direction of motion
Force from engine (f)
Friction force (ffr)
θ
Added term

## Slide 16: Introducing a disturbance – a hill
Weight (mg)
Direction of motion
Force from engine (f)
Friction force (ffr)
ϑ
Added term
Assuming and are constants

## Slide 17: Modifying the block diagram
G
v
f
vr
H
K
θ
+
-
Summation junction

## Slide 18: Modifying the block diagram
G
v
f
vr
H
K
θ
+
-
Summation junction

## Slide 19: Plotting results
Setting desired speed to 25 m/s and slope of
Generated force by controller H
Resulting speed v
Desired speed
Problem!
cruisefeedback_timedomain.m

## Slide 20: Negative Feedback
Let’s measure the car’s speed and
Correct for it by feeding back into the system a measure of the actual speed
G
v
f
vr
H
K
θ
+
-
c
e
Correction signal
Error signal
-
+

## Slide 21: Negative Feedback
Let’s measure the car’s speed and
Correct for it by feeding back into the system a measure of the actual speed
G
v
f
vr
H
K
θ
+
-
c
e
Correction signal c: in this case it is just a measure of the actual speed
Error signal e: the difference between the desired speed and the measured speed. If null, then
-
+

## Slide 22: Negative feedback
Plot of force vs. time and speed vs. time with negative feedback
Setting
Result:
  Faster response with feedback (compare blue against red curves)
  Speed at regime: (error of )
cruisefeedback_timedomain2.m

## Slide 23: Negative feedback
Increasing the controller’s gain (H)
  decreases the rise time
  while decreasing the steady state error
Setting
Result:
  Even faster response
  Speed at regime: (error of )
cruisefeedback_timedomain3.m
Yes but… how does it work?

## Slide 24: Signal flow and block diagrams
G
v
f
vr
H
K
θ
+
-
e
-
+
c

## Slide 25
G
v
f
vr
H
K
θ
+
-
e
-
+
c
System’s open loop gain (dimensionless)

## Slide 26
G
v
f
vr
H
K
θ
+
-
e
-
+
c
(high gain, closed loop, with feedback)
(low gain, open loop, or no feedback)
Error signal in closed loop: close to zero, proportional to angle
The higher the controller’s gain, the lower e

## Slide 27
G
v
f
vr
H
K
θ
+
-
e
-
+
c
With no feedback

## Slide 28
G
v
f
vr
H
K
θ
+
-
e
-
+
c
(high gain, closed loop, with feedback)
(low gain, open loop or no feedback)
Actual speed : close to with an error proportional to when in closed loop. The higher the controller’s gain, the lower the speed error.

## Slide 29
G
v
f
vr
H
K
θ
+
-
e
-
+
c

## Slide 30
G
v
f
vr
H
K
θ
+
-
e
-
+
c
(high gain, closed loop, with feedback)
(low gain, open loop, or no feedback)
Force : at regime, it does not depend on the gain in while proportional to angle

## Slide 31: Plotting and
Open loop
Closed loop
Setting
Plotting the open loop transfer function vs. time and the closed loop transfer function vs. time
Notice the rapid rise time for the closed loop case
cruisefeedback_timedomain2.m

## Slide 32: The error signal e
Plot of error signal e vs time
Error signal decreases to 3 m/s.
Notice a steady state error
cruisefeedback_timedomain2.m

## Slide 33: Open and closed loop TF with

## Slide 34: Error signal e with

## Slide 35: Cruise control example
First-order differential equation
Simplest controller: simply a gain with no time constants involved
How to handle more complicated problems?

## Slide 36: Block diagram reduction
P1
x
y
P2
P1P2
y
x
P1
x
y
P2
P1 ±P2
y
x
P1
x
y
P2
y
x

## Slide 37: Practice
Determine the output C in terms of inputs U and R.
U
C
R
+
+
-
+

## Slide 38: Practice
Determine the output in terms of inputs and .
U1
C
R
+
+
+
+
U2
+
+

## Slide 39: More practice
Determine C/R for the following systems.
(a)
(b)
(c)
R
+
+
+
+
C
R
+
+
+
+
C
R
+
+
+
+
C

## Slide 40: How do we MEASURE the OL TF of a system when the loop is closed?
Add an injection point in a closed loop system
Inject signal and read signal (just before the injection) and (right after the injection)
Solve for the ratio
+
+

## Slide 41: So far…
Control theory builds on differential equations
Block diagrams help visualize the signal flow in a physical system
The cause-and-effect relationship between variables is referred to as a transfer function (TF)
The system’s open-loop TF is the product of transfer functions
  cruise control example:
  Two cases: and
MATLAB implementation
  Functions used: dsolve

## Slide 42: Laplace Transforms
The technique of Laplace transform (and its inverse) facilitates the solution of ordinary differential equations (ODE).
Transformation from the time-domain to the frequency-domain.
Functions are complex, often described in terms of magnitude and phase

## Slide 43: Linear systems
To map a model to frequency space
  System must be linear
  Output proportional to input
Given system P
  Input signals: and
  Output signals (response): and
System P is linear
  If input signal:
  Then output signal:
  Superposition principle
P
x
y

## Slide 44: Example
Is a linear system?
  Knowing that and
  If input is , output is
  System is linear

## Slide 45: Example
Is a linear system?
  Knowing that and
  If input is , output is
  System is not linear

## Slide 46: In general
Output
Input
For a stable system

## Slide 47: Laplace Transform L
Transforms a linear differential equation into an algebraic equation
Tool in solving differential equations
Laplace transform of function f
Laplace inverse transform of function F
where is the transform variable
Imaginary unit

## Slide 48: Time domain ↔ Laplace domain
Input
Output

## Slide 49: Laplace Transform L

## Slide 50: (Some) Laplace transform pairs
Unit step |  | 
Unit ramp |  | 
Exponential |  | 
Sinusoid |  | 
SHO |  | 
Unit step |  | 
Unit ramp |  | 
Exponential |  | 
Sinusoid |  | 
SHO |  | 

## Slide 51: Laplace transform properties
Linearity
Derivatives
  First-order:
  Second-order:
Integral

## Slide 52: Solution to ODEs
Laplace transform the system’s ODE
Solve the algebraic equation in s
Inverse transform back to the time domain

## Slide 53: Transfer Function
Using derivative property
Algebraic equation in s, the ratio of 2 polynomials in s
Transfer function relates input to output .

## Slide 54: Transfer Function
The roots of the numerator are referred to as zeros.
The roots of the denominator are referred to as poles.
Transfer function can be defined by
The coefficients of s or
Its poles and zeros

## Slide 55: Let’s apply it to the cruise control example: transfer function (the car’s body)
Direction of motion
Engine force (f)
Friction force (ffr)
G(t)
f(t)
v(t)
G(s)
F(s)
V(s)
Pole at

## Slide 56: Dynamic response: using lookup tables to inverse transform
Laplace inverse transform using lookup tables
Input: step function, amplitude
The response (in frequency space) is
The time-domain response is

## Slide 57: Dynamic response: using lookup tables to inverse transform
Laplace inverse transform using lookup tables
Pole

## Slide 58: First-order system step response
63 %
Pole p
firstorder.m

## Slide 59: MATLAB implementation
The step response of transfer function
>> G=tf(5, [1 5]);
>> step(G);

## Slide 60: Partial fraction expansion
Reduce a complex function to a collection of simpler ones
Then use lookup table
Order m
Order n

## Slide 61: Comments
Poles of F(s) determine the time evolution of f(t)
Zeros of F(s) affect coefficients
Poles closer to origin → larger time constants

## Slide 62: Example
Find of the Laplace transform
Sol: Using MATLAB
>> [R,P,K]=residue([6 0 -12],[1 1 -4 -4])
R =
3.0000
1.0000
2.0000
P =
-2.0000
2.0000
-1.0000
K =
[]

## Slide 63: Example: LRC circuit

## Slide 64: Example: LRC circuit

## Slide 65: Example: LRC circuit

## Slide 66: LRC circuit: transfer function
Setting L = 1 H, C = 1 F and R = 1 Ω

## Slide 67: LRC circuit: dynamic response to step
Setting the input to a step of amplitude 1 V
The unit step response is

## Slide 68: LRC circuit: dynamic response to step
Using MATLAB for the solution
  >> n = [1];
  >> d = [1 1 1 0];
  >> [α, a, k] = residue(n, d);
Coefficient vector for polynomial at numerator
Coefficient vector for polynomial at denominator

## Slide 69: Plotting results of two methods
  >> y=α.'*exp(a*t);
  >> plot(t, y, 'bo');
  >> y2=step(1,[1 1 1],t);
  >> plot(t, y2, ‘r.’);
OR

## Slide 70: Second-order system step response
Overshoot
Period of oscillation
Settling time: time to settle to ±5% of final value (determined by the term)
secondorder.m
Note: often the response of a high-order system is similar to the second-order one

## Slide 71: Verify the following

## Slide 72: Back to cruise control: system’s step response
G
v
f
vr
H
K
θ
+
-
c
e
-
+

## Slide 73: Step response

## Slide 74: Back to cruise control
  >> n = [k/m];
  >> d = [1 (b+k)/m 0];
  >> [α, a, k] = residue(n, d);
  >> y=α.'*exp(a*t);
  >> plot(t, y, 'bo');
OR

## Slide 75: Back to cruise control
  >> G = tf([1/m],[1 b/m]);
  >> H = k;
  >> CL = G * H / (1 + G * H);
  >> [y, t] = step(CL);
  >> plot(t, y, 'b.');

## Slide 76: Transfer function, poles and zeros
It is convenient to express a transfer function G(s) in terms of its poles and zeros:
k is the gain of the transfer function

## Slide 77: Summary of pole characteristics
Real distinct poles (often negative)
Real poles, repeated m times (often negative)
↕

## Slide 78: Summary of pole characteristics
Complex-conjugate poles
often re-written as a second-order term
Poles on imaginary axis
  Sinusoid
  Pole at zero: step function
Poles with a positive real part
  Unstable time-domain solution

## Slide 79: Summary
The Laplace transform is a tool to facilitate solving for ODEs.
Systems need to be linear
No need to do the transform (integral)
  Use transform pairs, transform tables
  Laplace transform properties: linearity, derivatives and integrals.
Once in the Laplace domain, a TF is simply the ratio of two polynomials in s. Carry out algebra to solve the problem.
No need to do the inverse transform
  Use transform pairs, transform tables
  For high-order TFs, use the partial-fraction expansion to reduce the problem to simpler parts
IMPORTANT:
  Poles of a transfer function determine the time evolution of the system
  Poles with a real positive part correspond to unstable and unphysical systems
  The system TF needs to have poles with a negative real part
MATLAB implementation
  Functions used: step, residue, tf

## Slide 80: Solutions

## Slide 81: Practice
Determine the output C in terms of inputs U and R.
Sol:
U
C
R
+
+
-
+

## Slide 82: Practice
Determine the output in terms of inputs and .
Sol:
U1
C
R
+
+
+
+
U2
+
+

## Slide 83: More practice
Determine C/R for the following systems. Sol:
(a)
(b)
(c)
R
+
+
+
+
C
R
+
+
+
+
C
R
+
+
+
+
C

## Slide 84: How do we MEASURE the OL TF of a system when the loop is closed?
Add an injection point in a closed loop system
Inject signal and read signal (just before the injection) and (right after the injection)
Solve for the ratio
Sol:
+
+

## Slide 85: Partial-fraction examples
Denominator: has distinct, real roots
  Example 2.4, 2.5, 2.6
Denominator: complex roots
  Example 2.7, 2.8
Denominator: repeated roots
  Example 2.9

## Slide 86: Practice: verify the following