## Slide 1: To recap
A system’s TF is a complex function
  Represented in terms of its magnitude and phase
Bode plots
  plot of magnitude and phase
Bode plots of complex TFs can be expressed in terms of simpler terms
Stability criteria:
  The feedback control system is stable if and only if all the poles of the closed loop transfer function have a negative real part. Otherwise the system is unstable.

## Slide 2: To recap
Stability in terms of the open loop gain
  A closed loop system is stable if the unity gain frequency is lower than the crossing.
  Rule of thumb: the system is (almost always) stable if at the unity gain frequency
How close to instability is a system?
  Gain and phase margin
Typical compensators
  Phase-lag
  Phase-lead
  “Boost”

## Slide 3: SIMULINK
Simulating systems in the time-domain
Let’s refer back to the cruise control example
Parameters used previously
G
v
f
vr
H
K
θ
+
-
e
-
+
c

## Slide 4: OL TF bode plot
UGF @160 mHz
cruise_freqdomain.m

## Slide 5: Building the model
First we need to model the response of the car to an input force .
This was previously described by transfer function
was derived from
SIMULINK simulates this differential equation

## Slide 6: Building the model
Type simulink at the MATLAB prompt
  >> simulink
The “Simulink Library Browser” window opens.
File → New → Model
The model window opens

## Slide 7: Building the model
The relationship between and is simply . Add the Integrator block by selecting it and dragging it to the model window. The integrator block is in the simulink library browser under the continuous section.
Extend the signal in and signal out lines, double click on top of each line and label them as and

## Slide 8: Building the model
Re-arranging terms : the change in velocity is times . In the library browser, under the math operations section, select and drag the Gain block.
Connect its output to the integrator’s input.
Double-click on the gain block, set the gain value to , and click ok.
Double-click right under the gain block and label it as .

## Slide 9: Building the model
Under the math operations section, select and drag the Add block.
Connect the add block with the gain block
Double-click the add block and change the sign as shown in figure .
One input to the add block will be the engine force while the other will be the friction force

## Slide 10: Building the model
Add another Gain block, and change its orientation by selecting it, clicking on Format → Flip block
Double-click on it, set the gain to and click ok.
Double-click right under the block and re-name it as .
Connect the output of the integrator to the input gain block .
Connect the output of gain block with the negative input of the add block.

## Slide 11: Building the model
In the library browser, under the sources section, select and drag the Step block.
Connect the step block to the add block.
Double-click on the step block and set the final value to 500 (the same value we had used before)
In the Sinks section, select Scope and drag it to the window. Connect it to the output of the step block.
Select and drag a second scope and connect it to the integrator’s output
We are ready for the simulation

## Slide 12: Results
At the MATLAB prompt set the parameters
  >> f=500;b=50;m=1000;
Under the Simulations tab, click Configuration parameters, set the end time to 100 and click ok.
Under the Simulations tab, click Start.
Once the simulation is finished, double-click on each scope, and graphing windows appear (you probably need to autoscale)
The time evolution is identical to the one we had obtained before.
cruiseG.mdl

## Slide 13: Results
SIMULINK is a time-domain simulation and handles linear and non-linear systems. The frequency-domain analysis presented so far can only handle linear models. To produce bode plots we need to linearize the model.
Erase the two scopes and the step block.
In the Sources section, add an In block and connect it to the add block.
In the Sinks section, add an Out block and connect it to the output of the integrator.
Save the model as “SubsystemG.mdl”
At the MATLAB prompt type the commands on the right which reproduce the transfer function we were using before
>> [A,B,C,D]=linmod('subsystemG');
>> [num,den]=ss2tf(A,B,C,D);
>> H=tf(num,den)
Transfer function:
0.001
--------
s + 0.05
Note: A, B, C, D is a state space representation of the system

## Slide 14: Implementing feedback
Create a new model calling it “cruise_control.mdl”
Select and drag from the library the Ports & Subsystems → Subsystem block.
Double-click on the subsystem block, erase the contents
Double-click on the subsystemG.mdl model, select all and copy. Paste in the subsystem block.

## Slide 15: Implementing feedback
cruise_control.mdl

## Slide 16: Let’s setup a SIMULINK model of the accelerometer shown before
Position y is with respect of the case, the case’s position is x. What is the transfer function between the input acceleration and the output y?
M
y
k
B
x

## Slide 17: Rule of thumb
For a system represented by an nth order input/output ordinary differential equation it is necessary to integrate the highest derivative n times to obtain the output.
Rearranging terms

## Slide 18: The model
acc.mdl

## Slide 19: Results
>> m=1;k=1;B=1;
>> [A,B,C,D]=linmod('acc');
>> [num,den]=ss2tf(A,B,C,D);
>> H=tf(num,den)
Transfer function:
1
-----------
s^2 + s + 1
Which confirms our previous finding.

## Slide 20: Model the following LRC circuit

## Slide 21: Model the following LRC circuit

## Slide 22: Digital Signal Processing 1
Moving to the digital world
Two classes of signals
  Analog
  Discrete
Analog signal
  Denoted with
  represents time in seconds
Discrete signal
  Number sequence
  is an integer, represents discrete instances in time
digsig.m

## Slide 23: Types of sequences
Unit sample sequence
sequences.m

## Slide 24: Types of sequences
Unit step sequence
sequences.m

## Slide 25: Discrete systems
Linear time-invariant (LTI) system L
  Satisfies the principle of superposition
  The input-output pair, and , is invariant to a shift

## Slide 26: Discrete systems
Any sequence can be written in terms of scaled and delayed unit sample sequences
The response of an (LTI) system can then be re-written as

## Slide 27: Discrete systems
is the unit sample or impulse response of LTI system
Convolution

## Slide 28: Let’s compute the convolution between two sequences
Let’s define and and let’s determine
For
k
-4
-3
-2
-1
0
1
2
3
4
5
x(k)
-
-
-
-
1
2
3
-
-
-
y(k)
-
-
-
-
3
2
1
-
-
-
y(-k)
-
-
1
2
3
-
-
-
-
-
-k
4
3
2
1
0
-1
-2
-3
-4
-5
x(k)y(-k)
-
-
-
-
3
-
-
-
-
-
3

## Slide 29: Let’s compute the convolution between two sequences
Let’s define and and let’s determine
For
k
-4
-3
-2
-1
0
1
2
3
4
5
x(k)
-
-
-
-
1
2
3
-
-
-
y(k)
-
-
-
-
3
2
1
-
-
-
y(1-k)
-
-
-
1
2
3
-
-
-
-
1-k
5
4
3
2
1
0
-1
-2
-3
-4
x(k)y(1-k)
-
-
-
-
2
6
-
-
-
-
8

## Slide 30: Let’s compute the convolution between two sequences
Let’s define and and let’s determine
Using MATLAB to confirm results
>> conv([3 2 1],[1 2 3])
ans =
3 8 14 8 3
n | 
0 | 3
1 | 8
2 | 14
3 | 8
4 | 3
n | 
0 | 3
1 | 8
2 | 14
3 | 8
4 | 3

## Slide 31: Stability
An LTI system is stable if and only if its impulse response is absolutely summable

## Slide 32: Correlation of sequences
The correlation between two sequences and is defined as
where
  is the correlation (degree to which the two signals are similar) and
  is the lag.

## Slide 33: Example
Generating two identical random sequences, one of them shifted by 50 samples.
conv_example2.m

## Slide 34: Example
Taking the correlation between them using MATLAB’s xcorr command we find highest correlation at lag 50.
conv_example2.m

## Slide 35: Example
Using MATLAB’s xcorr or conv command.
conv_example2.m
>> [r,lags]=xcorr(x,y);
>> plot(lags,r,'bo')
or
>> r2=conv(x,fliplr(y),'same');

## Slide 36: Exercise
In a certain concert hall, echoes of the original audio signal are generated due to reflections at the walls and ceiling. The audio signal experienced by the listener is a combination of and its echoes. Let
where k is the amount of delay in samples and is its relative strength.
Estimate the delay assuming the original signal is a Sine-Gaussian
with , and .

## Slide 37
ex28.m

## Slide 38: Signal Energy
The energy of a sequence is given by

## Slide 39: Differential to difference equations
In the analog world:
x(t)
y(t)

## Slide 40: Differential to difference equations
In the digital world:
The original differential equation is approximated by a difference equation
In the limit

## Slide 41
difference.m
In the limit
>> diff(x)

## Slide 42
difference.m
In the limit
>> diff(x)

## Slide 43: Difference equations
In general, a difference equation is of the form
  where is the input sequence
  is the output sequence and
  and are the coefficients of and respectively.
The MATLAB filter command solves the difference equations numerically – filtering input sequence
>> y = filter(b, a, x)

## Slide 44: Impulse response
To generate the impulse response of an LTI system described by the difference equation
use the filter command:
>> h = filter(b, a, delta)
By plotting you can visualize if the system is stable

## Slide 45: Example
An LTI system is described by the following difference equation
Plot the impulse response for and determine if system is stable.

## Slide 46: Example
An LTI system is described by the following difference equation
Plot the impulse response for and determine if system is stable.
Generating the delta function with MATLAB
>> x = zeros(1,100);
>> x(1) = 1;
>> plot(x,'bo-')
ex29.m

## Slide 47: Example
An LTI system is described by the following difference equation
Plot the impulse response for and determine if system is stable.
Generating the response
>> b=1;
>> a=[1 -1 0.9];
>> h=filter(b,a,x);
>> plot(h,'bo-')
System is stable
ex29.m

## Slide 48: Exercise
An LTI system is described by the difference equation
Plot its impulse response and determine the stability of the system.

## Slide 49
Generating the response
>> b=[1 2 0 1];
>> a=[1 -0.5 0.25];
>> h=filter(b,a,);
>> plot(h,'b-')
ex216.m

## Slide 50: Cruise control case
Physical system described by the following equation of motion
Simplifying and assuming friction force is proportional to speed
Direction of motion
Force from engine (f)
Normal force (n)
Weight (mg)
Friction force (ffr)

## Slide 51: In the digital world

## Slide 52: Numerical solution
difference2.m
In the limit

## Slide 53: Numerical solution
difference2.m
In the limit

## Slide 54: Summary
SIMULINK – time domain simulation, can handle non-linear systems.
  Tutorial
  A suggestion for re-writing the differential equation is given in order to facilitates designing the model
Analog to digital
  Signals to sequences
  Impulse response of a system
  Convolution and correlation
  Condition of stability
  Differential to difference equations
  General form of a difference equation
  MATLAB’s filter to numerically solve difference equations
  Impulse response can be determined by using the filter command and setting the input to a delta sequence.