## Slide 1: So far
We have introduced the Z transform
  The digital equivalent of the Laplace transform
  It facilitates the solving of difference equations
  It allows to easily evaluate the system’s response
  It is critical in designing linear filters
The Discrete-time Fourier Transform (DTFT)
  in the transform
  Mapping into frequency space
The Discrete Fourier Transform (DFT)
  The sampling of the DTFT in the frequency domain
  FFT: Fast Fourier Transform
    Algorithm for the efficient computation of DFTs
Sampling principle
  The signal’s bandwidth must be less than the Nyquist frequency in order to avoid aliasing

## Slide 2: Digital Signal Processing 3
Digital Filters
An LTI system to frequency select or discriminate
Two classes
  Finite-duration impulse response (FIR) Filters
  Infinite-duration impulse response (IIR) Filters

## Slide 3: FIR filter
The filter’s unit impulse response is of finite duration
  Its response settles to zero in a finite time
  There is no “feedback”
Difference equation
Also referred to as recursive or moving average filters.

## Slide 4: IIR filter
The filter’s unit impulse response is of infinite duration
Difference equation
Output is recursively computed from previous computed values → infinite duration response

## Slide 5: FIR filter example: Moving Average (MA)
In general
For

## Slide 6: To the Z domain
Recall: when an LTI system is represented by the difference equation
Then

## Slide 7: System function
Coefficients a and b are
With a pole at the origin, and a zero at -1.

## Slide 8
>> a=1; b=[1/2 1/2];
>> zplane(b,a)
MA_example.m

## Slide 9: Recall: difference equation and the filter command
In general, a difference equation is of the form
The MATLAB filter command solves the difference equations numerically
  Given the input sequence , the output sequence is computed using
>> y = filter(b, a, x)

## Slide 10: Let’s apply the filter to a data stream
Step function imbedded in noise is shown to the right.
Let’s apply the N=2 moving average filter
>> a=1;
>> b=[1/2 1/2];
>> y = filter(b, a, x);
MA_example.m

## Slide 11
MA_example.m

## Slide 12: The impulse response function
>> h = filter(b, a, delta)
MA_example.m

## Slide 13: The impulse response function
From the filter command
The system’s response

## Slide 14: Comparing the filter output with convolution
>> y = conv(x,h,’same’)
MA_example.m

## Slide 15: Increasing filter order
MA_exampleB.m

## Slide 16: Increasing filter order
MA_exampleB.m

## Slide 17: Increasing filter order
MA_exampleB.m

## Slide 18: Frequency response of moving average filter
MA_exampleB.m
>> [H, f]= freqz(b,a,1000,Fs)

## Slide 19: Suppression but with phase delay
MA_exampleC.m

## Slide 20: Analog-to-digital filter transformation
First, we design an analog filter that satisfies the specifications.
Then we transform it into the digital domain.
Many transformations are available
  Impulse invariance
    Designed to preserve the shape of the impulse response from analog to digital
  Finite difference approximation
    Specifically designed to convert a differential equation representation to a difference equation representation
  Step invariance
    Designed to preserve the shape of the step response
Bilinear transformation
  Most popular technique
  Preserves the system’s function representation from analog to digital

## Slide 21: Filter stability in the analog and digital domain
21
Analog domain
(s-plane)
Digital domain
(z-plane)
Region of stability
Poles must have a negative real part
Poles are inside the unit circle

## Slide 22: Bilinear transformation
22
Analog domain
(s-plane)
Digital domain
(z-plane)
Mapping between the two stability regions

## Slide 23: Bilinear transformation
23
Analog domain
(s-plane)
Digital domain
(z-plane)
Sampling time

## Slide 24: Transformation example
Transform
into a digital filter with sampling .
Sol.

## Slide 25: Transformation example
bilinearexample.m

## Slide 26: Transformation example
bilinearexample3.m

## Slide 27: Filter Design
Filter specifications
  Constraints on the suppression factor
  Constraints on the phase response
  Constraints on the impulse response
  Constraints on the step response
  FIR or IIR
  Filter order
Typical filters
  Low pass, High pass, Band pass and Band stop

## Slide 28: FIR or IIR?
Advantages of FIR filters over IIR
  Can be designed to have a “linear phase”. This would “delay” the input signal but would not distort it
  Simple to implement
  Always stable
Disadvantages
  IIR filters are better in approximating analog systems
  For a given magnitude response specification, IIR filters often require much less computation than an equivalent FIR

## Slide 29: Low pass (LP) filter specifications
LP filter
  low frequencies pass, high frequencies are attenuated.
Include
  target magnitude response
  phase response, and
  the allowable deviation for each
Transition band
  frequency range from the passband edge frequency to the stopband edge frequency
Ripples
  The filter passband and stopband can contain oscillations, referred to as ripples. Peak-to-peak value, usually expressed in dB.

## Slide 30: High pass (HP) filter specifications
HP filter
  High frequencies pass, low frequencies are attenuated.

## Slide 31: Band pass (BP) filter specifications
BP filter
  a certain band of frequencies pass while lower and higher frequencies are attenuated.

## Slide 32: Band stop (BS) filter specifications
BS filter
  attenuates a certain band of frequencies and passes all frequencies not within the band.

## Slide 33: A few types of IIR filters
Butterworth
  Designed to have as flat a frequency response as possible in the passband
Chebyshev Type 1
  Steeper roll-off but more pass band ripple
Chebyshev Type 2
  Steeper roll-off but more stop band ripple
Elliptic
  Fastest transition

## Slide 34: Comparison
Sampling frequency set to 16384 Hz
Filter order set to 10, cutoff set at 1 kHz
Difficult comparison: specifications for each filter can be very different
filter_plots.m

## Slide 35: Comments
Chebyshev filter has a steeper roll-off with respect to the Butterworth filter
The elliptical filter has the fastest roll-off
Elliptical’s attenuation factor at high frequency is constant, unlike the others.
Elliptical has the least phase delay with respect to the others
Notice: the performance of a FIR window filter of 10th order is also shown. For it to achieve the same performance as the others, the filter order must be increased significantly
filter_plots.m

## Slide 36: Comments
The Butterworth filter has a flattest response when compared to the others.
There is a trade off
  The faster the roll-offs, the greater the ripples
filter_plots.m

## Slide 37: MATLAB’s fdatool
Filter Design and Analysis Tool
Allows you to design (visually) a digital filter
Can export the filter into different formats
  Filter coefficients
  MATLAB’s transfer function object
  …
>> fdatool

## Slide 38: MATLAB’s fdatool
Exporting
Coefficients a, b
Transfer function object Hd
Second-order-sections sos
  The system function H(z) can be factored into second-order-sections. The system is then represented as a product of these sections.
Assuming input signal x, the output y:
  y = filter(Hd,x)
  y = filter(b,a,x)
  y = sosfilt(sos,x)

## Slide 39: Sampling: Analog-to-Digital conversion
Transforms analog signal to digital sequence
Main components of an A/D converter
C/D
Quantizer
Encoder
c
Analog signal : real valued function of a continuous variable
Bit stream : corresponds to discrete time sequence

## Slide 40: Sampling: Analog-to-Digital conversion
Transforms analog signal to digital sequence
Main components of an A/D converter
C/D
Quantizer
Encoder
c
Sampler C/D: continuous-to-discrete converter or an ideal A/D converter:
Quantizer: maps continuous range of possible amplitudes into a discrete set of amplitudes
Quantization interval : amplitude is integer multiple of (determined by the number of bits)

## Slide 41: Sampling: Analog-to-Digital conversion
Transforms analog signal to digital sequence
Main components of an A/D converter
C/D
Quantizer
Encoder
c
Encoder: produces a sequence of binary codewords

## Slide 42: Sampling: Analog-to-Digital conversion
Anti-aliasing filter
  Signals in physical systems will never be exactly bandlimited, aliasing can occur
  (Analog) lowpass at the Nyquist frequency.
    This minimizes signal energy above the Nyquist frequency, minimizing aliasing
C/D
AA

## Slide 43: Sampling: Analog-to-Digital conversion
Anti-aliasing filter
  Signals in physical systems will never be exactly bandlimited, aliasing can occur
  Analog lowpass filter that minimizes signal energy above the Nyquist frequency
C/D
AA

## Slide 44: And back: Digital-to-Analog conversion
Two steps involved
Conversion to rectangular pulses
Pulses cause multiple harmonics above the Nyquist frequency
This excess noise is reduced with an (analog) low pass filter (or reconstruction filter)
Convert to impulses
LP filter

## Slide 45
Thank You!!