Statement of Work

Acquisition of Shielded Pair Cables Needed for aLIGO Suspension System

C1105864-v3

Note to LIGO users: all red text in this template is font type ‘hidden’ and comprises instructions to complete the SOW.  Easier than deleting them, you can hide all red text before saving.  In Word 2010, click File, Options (on the left side), Display (on the left side), and then unclick “Hidden Text”.

The “TEMPLATE” watermark can be removed by clicking Page Layout, Watermark, and then Remove Watermark.

- Scope

This Statement of Work is for the procurement of two types of individually, twisted, shielded pair cables needed for the aLIGO Suspension System. The quantities, lengths and types are called out in the tables in Section 5 of this document. Note that for each type of cable, there are multiple lengths required.

The description for each type of cable is shown in the table below.

| Drawing Number | Description |
| --- | --- |
| D1002956-v1 (See Sec. 3.0) | DB25 Male to DB25 Female Cable with individually twisted, shielded pairs. The shield is terminated at the Male connector end only and the pairs are per the table in the schematic. |
| D1002958-v1 (See Sec. 3.0) | DB15 Male to DB15 Female Cable with individually twisted, shielded pairs. The shield is terminated at the Male connector end only and the pairs are per the table in the schematic. |

Each of the drawings for the desired cables call out a specific example of a cable type to be used for the manufacture of these cables, specifically Alpha 6017C and Alpha 6014C for D1002956 and D1002958, respectively. These specific Alpha cables are meant to be representative of the type of cable to be used for fabrication. Alternative, equivalent, cable types can be used, but must meet or exceed the Alpha cable types in the following areas:

- Each twisted pair must have its own individual shield

- Minimum 22 AWG wire

- 300V insulation rating

- In the case of D1002958, Alpha 6014C is a 9 pair cable type, but only 7 pairs are needed. Alternative cable types may have 7 individual pairs.

If alternative cable types are proposed for fabrication, the quote should state the cable type to be used and a datasheet for that cable type shall be included with the quote.

Briefly describe the work.  For example: Fabrication of Vacuum Pod components for Advanced LIGO BSC-ISI Seismometers.

- Document Access

Many supplemental documents and specifications are incorporated into, and made a part of, this Statement of Work.  Click on the document links to access these documents from the LIGO Document Control Center (DCC) or go on line to the LIGO Public DCC at https://dcc.ligo.org/ to access the DCC#.

- Commercial Terms and Applicable LIGO Specifications:

Note: The documents listed below are invoked for this Statement of Work and comprise additional requirements which are integral to this Statement of Work.

Important: C080185 and Q0900001 apply to all SOWs. Add/delete others as appropriate.

Check to be sure the latest revisions are specified below (please notify QAME or Systems if this template needs to be updated).

- LIGO-C080185-v1	LIGO Commercial Items or Services Contract General Provisions

- LIGO-Q0900001-v5 	Advanced LIGO Supplier Quality Requirements

- D1002956-v1                    DB25 Male-Female Cable, Indiv. Twist/Shield Pair

- D1002958-v1                    DB15 Male-Female Cable, Indiv. Twist/Shield Pair

- Quality System:

Referring to the above referenced LIGO Specification Q0900001, Suppliers should include a copy of their current ISO 9001, AS9100, or TS16949 certification in their bid package.  Suppliers lacking current certification should send a copy of their Quality Manual with their bid package.

- Parts/Assemblies to be manufactured and Quantity Required:

Note: refer to Section 8.0 for delivery schedule and location

The quantities for each length of the DB25 Male to DB25 Female Cable (D1002956 (See Sec. 3.0)) are shown in the table below.

| Drawing Number | Length | Quantity |
| --- | --- | --- |
| D1002956 | 6 feet | 115 |
| D1002956 | 10 feet | 130 |
| D1002956 | 50 feet | 5 |
| D1002956 | 60 feet | 30 |
| D1002956 | 90 feet | 12 |
| D1002956 | 100 feet | 18 |
| D1002956 | 120 feet | 5 |
| D1002956 | 140 feet | 45 |
| D1002956 | 150 feet | 20 |
| D1002956 | 165 feet | 10 |
| D1002956 | 200 feet | 20 |

The quantities for each length of the DB15 Male to DB15 Female Cable (D1002958 (See Sec. 3.0)) are shown in the table below.

| Drawing Number | Length | Quantity |
| --- | --- | --- |
| D1002958 | 90 feet | 12 |
| D1002958 | 100 feet | 18 |
| D1002958 | 120 feet | 5 |
| D1002958 | 140 feet | 45 |
| D1002958 | 150 feet | 20 |
| D1002958 | 165 feet | 10 |
| D1002958 | 200 feet | 20 |

List all parts to be made, including the public hyperlink to the latest revision, and the total quantity required.  If you have more than ten parts, create a separate drawing document posted to the DCC as a public document, and link here.

Note 1: Care should be given to the selection of the AQL number.  Consider the amount of time (which equals cost) required to 100% inspect a given number of parts.  Contact QAME for advice.

Note 2: Additional inspection instructions beyond the AQL number can be given – such as 100% inspection of all threaded holes.

- Manufacturing:

# Requirements:

# Suppliers must refer to the LIGO Specifications referenced in Section 3 for additional, and in some cases, non-industry standard requirements.

# Sub-Contracted Work:

# LIGO expects that at least 2/3 (by dollar value) of the contracted work be performed by the Supplier named on the Purchase Order.  The Supplier shall be responsible for all sub-contracted work.

# Precedence:

The drawings typically represent the finished part as needed for use in service.  There may be requirements on the drawing (such as coatings) which are specifically defined as not the responsibility of the supplier in this SOW.  Suppliers should always contact a LIGO representative to resolve any discrepancies or uncertainties in the documentation or instructions.

# Special Considerations:

# It is recognized that there are minimum quantity purchases for the types of cable material that is being requested. If the quantities requested in this statement of work do not allow the vendor to meet these minimum quantities, the quote should state the number of additional feet of each type of cable that would be required to meet the minimum quantity. Add special manufacturing notes

# Testing  & Inspection Requirements:

# All cables must be visually inspected for quality workmanship, cleanliness and free of defects.

# All cables must be electrically tested for continuity, shorting and withstand voltage.

# Marking:

# The drawing/part number, revision, length and serial number shall be placed onto each cable (preferably the backshell). The method used for marking is unimportant except that it should be permanent. The serial number sequence will be prescribed by LIGO Lab. Example:

# D1002956-v1  6ft

# S1101234

- End Item Data Package:  Add/delete lines as necessary

Before delivery of the parts, the Supplier shall provide the following data, as a minimum:

- Any as-built modifications (with approval of the LIGO Contracting Officer) as mark-ups to the drawings

- Certificate of compliance for each part number stating conformance to contract and drawing requirements

- Delivery Requirements:

  - Shipping Containers and Packaging:

The contractor is responsible for providing shipping containers and transportation which protects these parts from damage from the transportation environment (weather, handling, accidents, etc.).  Mating edges of parts should be especially protected from damage during shipping.

Note any special packaging requirements here (i.e., wrap in UHV foil and Ameristat).

  - Shipping Destination(s):

The deliveries are FOB at these destinations, i.e. the Supplier has the responsibility for shipping title and control of goods until they are delivered and the transportation has been completed. The contractor selects the carrier and is responsible for the risk of transportation and for filing claims for loss or damage.

Delete shipping destinations that don’t apply to this SOW.  Be sure to reference the shipping abbreviations (i.e., LLO) in the Delivery Schedule if there is more than one shipping destination.

LHO Cable Totals:

The following tables detail the cables that will be delivered to the LIGO Hanford Observatory.

| Drawing Number (DB25 Cable) | Length | Quantity |
| --- | --- | --- |
| D1002956 | 6 feet | 90 |
| D1002956 | 10 feet | 100 |
| D1002956 | 50 feet | 5 |
| D1002956 | 60 feet | 15 |
| D1002956 | 90 feet | 12 |
| D1002956 | 100 feet | 18 |
| D1002956 | 120 feet | 5 |
| D1002956 | 140 feet | 38 |
| D1002956 | 150 feet | 20 |
| D1002956 | 165 feet | 10 |
| D1002956 | 200 feet | 20 |

| Drawing Number (DB15 Cable) | Length | Quantity |
| --- | --- | --- |
| D1002958 | 90 feet | 12 |
| D1002958 | 100 feet | 18 |
| D1002958 | 120 feet | 5 |
| D1002958 | 140 feet | 38 |
| D1002958 | 150 feet | 20 |
| D1002958 | 165 feet | 10 |
| D1002958 | 200 feet | 20 |

Shipping Location:

LIGO Hanford Observatory
127124 North Route 10
Richland, WA 99354

Attn: Terry Santini / Jodi Fauver

LLO Cable Totals:

The following tables detail the cables that will be delivered to the LIGO Livingston Observatory.

| Drawing Number (DB25 Cable) | Length | Quantity |
| --- | --- | --- |
| D1002956 | 6 feet | 25 |
| D1002956 | 10 feet | 30 |
| D1002956 | 60 feet | 15 |
| D1002956 | 140 feet | 7 |

| Drawing Number (DB15 Cable) | Length | Quantity |
| --- | --- | --- |
| D1002958 | 140 feet | 7 |

Shipping Location:

LIGO Livingston Laboratory
19100 LIGO Lane
Livingston, LA 70754

Attn: Willie Hawkins / Celine Ramet

  - Delivery Schedule:

Delivery is expected within 8 weeks ARO.

Insert a list or table detailing the delivery requirements (by P/N, as necessary).  Delivery should be specified in weeks ARO (after receipt of order).  Please also specify the shipping destination (i.e. LLO).

Note any first article requirements.  If applicable, the SOW must state upfront that LIGO wants to assemble the first articles for fit check before the rest of the order is completed.

# Text boxes

# LIGO LABORATORY

California Institute of Technology

1200 E. California Blvd.

Pasadena, CA  91125