LASER INTERFEROMETER GRAVITATIONAL WAVE OBSERVATORY

-LIGO-

CALIFORNIA INSTITUTE OF TECHNOLOGY

MASACHUSETTS INSTITUTE OF TECHNOLOGY

LIGO- E1100984-v1 10/4/11

SLC Signal Recycling Cavity Baffle Install Hazard Analysis

Michael Smith

LIGO Hanford Observatory		LIGO Livingston Observatory

P.O. Box 1970; Mail Stop S9-02		19100 LIGO Lane

Richland, WA 99352			Livingston, LA 70754

Phone (509) 37208106			Phone (225) 686-3100

Fax (509) 372-8137				Fax (225) 686-7189

E-mail: info@ligo.caltech.edu		E-mail: info@ligo.caltech.edu

California Institute of Technology		Massachusetts Institute of Technology

LIGO – MS 18-34				LIGO – MS NW22-295

Pasadena, CA 91125				Cambridge, MA 01239

Phone (626) 395-2129				Phone (617) 253-4824

Fax (626) 304-9834				Fax (617) 253-7014

E-mail: info@ligo.caltech.edu		E-mail: info@ligo.mit.edu

APPROVAL SIGNATURES

___________________________________________________________

Eric Gustafson, AOS Group leader			            	 Date

__________________________________________________________

Michael Smith, SLC Task Leader					  Date

__________________________________________________________

David Nolting, LIGO Lab Safety Officer 				Date

__________________________________________________________

John Worden, LHO Site Safety Officer 				Date

__________________________________________________________

Rusyl Wooley, LLO Site Safety Officer 				Date

__________________________________________________________

Brian O’Reilly, Advanced LIGO LLO Installation Lead 		Date

__________________________________________________________

Michael Landry, Advanced LIGO LHO Installation Lead 		Date

__________________________________________________________

David Shoemaker, aLIGO Leader					Date

__________________________________________________________

Albert Lazzarini, LIGO Directorate 					Date

# Scope

This document covers safety concerns related to the assembly and installation of the Signal Recycling Cavity Baffles in HAM4, HAM5, HAM9, and HAM10.

It must be read before beginning the installation of the Signal Recycling Cavity Baffles, and used in conjunction with the SLC and Viewports Installation plan Document, document number LIGO-E1000099-v1.

# Summary of Hazards

The baffles weigh < 25 lbs, and they will be lifted manually onto the HAM ISI table and slid into position; during this operation, the installer must lean over the table, and could be subject to back strain. The baffle base will be clamped with appropriate dog-clamps; the installer could hurt their hand or fingers by improper use of the torque wrench used to tighten the dog-clamp bolts.

The baffles will be aligned by projecting an infrared autocollimator beam onto an alignment target placed on the baffle. Serious eye hazard could result if the installer does not wear proper safety goggles/glasses.

- Eye damage from exposure to infrared autocollimator beam (4E)

This hazard is described in detail later in the document.

# Overview

The signal recycling cavity baffles weigh < 25 lbs, and they will be lifted manually onto the HAM ISI table and slid into position. The baffle base will be clamped with appropriate dog-clamps. The baffles will be aligned by projecting an infrared autocollimator beam onto an alignment target attached to the baffle.

During the assembly and installation of the Mode Cleaner Tube Baffle, a task leader shall be assigned to supervise all activities. The IR beam will require the use of protective goggles/glasses to avoid eye damage. This assembly and installation requires overall common sense and good lab practices. Personnel must have good working knowledge of how to safely use the tools associated with the build and installation, and be aware of the hazards associated with working near a high power infrared light beam. All personnel must have appropriate safety training to work at a LIGO facility.

Figure 1: H1 & L1 HAM4: SR2 Scraper Baffle, SR2 AR Baffle, Hartmann Scraper Baffle, Hartmann Beam Dump

Figure 2: H1 HAM5: SR3 HR Baffle, SR3 AR Baffle, SRM HR Baffle

Figure 3: H2 HAM9: SR2 Scraper Baffle, SR2 AR Baffle, Hartmann Scraper Baffle, Hartmann Beam Dump

Figure 4: H2 HAM10: SR3 HR Baffle, SR3 AR Baffle, SRM HR Baffle

# Related Documentation

SLC and Viewports Installation Plan (LIGO- LIGO-E1000099-v1)

Advanced LIGO Safety: Processes and Guidelines (LIGO-M070360)

LIGO Project System Safety Plan (LIGO-M950046)

LIGO Hanford Observatory Contamination Control Plan (LIGO-M990034)

Chamber Entry/Exit Checklist (LIGO-E000065)

LIGO Hanford Observatory Laser Safety Plan (LIGO-M020131)

LLO Safety Procedure documents (http://www.ligo-la.caltech.edu/contents/internalmain.htm)

# Hazard Analysis

## Eye Hazard

The infrared autocollimator beam may have a power level exceeding 1 W; looking directly into the beam may cause retinal damage.

# 6.  Manifold/Cryopump Baffle Hazard Analysis Severity Table

| Item # | Hazard | Cause | Effect | Unmitigated Severity | Unmitigated Probability Level | Unmitigated Risk Index | Comment | Mitigation | Mitigation Severity | Mitigated Probability Level | Mitigated Risk Index |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Eye damage | Looking directly into IR autocollimator beam | Injury to personnel | Critical | occasional | 2C | May cause serious retinal damage | Wear appropriate eye safety glasses goggles | minor | improbable | 4E |

|  |  |  | PROBABILITY |  |  |
| --- | --- | --- | --- | --- | --- |
| SEVERITY OF | E | D | C | B | A |
| CONSEQUENCE | Improbable | Remote | Occasional | Probable | Frequent |
| 1 |  |  |  |  |  |
| Catastrophic |  |  |  |  |  |
| 2 |  |  |  |  |  |
| Critical |  |  |  |  |  |
| 3 |  |  |  |  |  |
| Marginal |  |  |  |  |  |
| 4 |  |  |  |  |  |
| Negligible |  |  |  |  |  |
| Hazard Risk Index |  |  | Risk Code Criteria |  |
| 1A, 1B, 1C, 2A, 2B, 3A |  | Unacceptable |  |  |
| 1D, 2C, 2D, 3B, 3C |  | Undesirable (Directorate decision required) |
| 1E, 2E, 3D, 3E, 4A, 4B |  | Acceptable with review by Directorate |
| 4C, 4D, 4E |  | Acceptable without review |  |

# Text boxes

SR2 Scraper Baffle

SR2

SR3 HR Baffle

Hartmann Beam Dump (typical)

Hartmann Scraper Baffle

SR2 AR Baffle

SR3

SR3 AR Baffle

SRM

SRM HR Baffle

Hartmann Beam Dump (typical)

Hartmann Scraper Baffle

SR2

SR2 Scraper Baffle

SR2 AR Baffle

SR2

SR3 AR Baffle

SRM HR Baffle

SR3

SR3 HR Baffle