LASER INTERFEROMETER GRAVITATIONAL WAVE OBSERVATORY

-LIGO-

CALIFORNIA INSTITUTE OF TECHNOLOGY

MASACHUSETTS INSTITUTE OF TECHNOLOGY

LIGO- E1100984-v3 03/15/2012

SLC Signal Recycling Cavity Baffle Install Hazard Analysis

Michael Smith, Lisa C. Austin

LIGO Hanford Observatory		LIGO Livingston Observatory

P.O. Box 1970; Mail Stop S9-02		19100 LIGO Lane

Richland, WA 99352			Livingston, LA 70754

Phone (509) 37208106			Phone (225) 686-3100

Fax (509) 372-8137				Fax (225) 686-7189

E-mail: info@ligo.caltech.edu		E-mail: info@ligo.caltech.edu

California Institute of Technology		Massachusetts Institute of Technology

LIGO – MS 18-34				LIGO – MS NW22-295

Pasadena, CA 91125				Cambridge, MA 01239

Phone (626) 395-2129				Phone (617) 253-4824

Fax (626) 304-9834				Fax (617) 253-7014

E-mail: info@ligo.caltech.edu		E-mail: info@ligo.mit.edu

APPROVAL SIGNATURES

___________________________________________________________

Eric Gustafson, AOS Group leader			            	 Date

__________________________________________________________

Michael Smith, SLC Task Leader					  Date

__________________________________________________________

David Nolting, LIGO Lab Safety Officer 				Date

__________________________________________________________

John Worden, LHO Site Safety Officer 				Date

__________________________________________________________

Rusyl Wooley, LLO Site Safety Officer 				Date

__________________________________________________________

Brian O’Reilly, Advanced LIGO LLO Installation Lead 		Date

__________________________________________________________

Michael Landry, Advanced LIGO LHO Installation Lead 		Date

__________________________________________________________

David Shoemaker, aLIGO Leader					Date

__________________________________________________________

Albert Lazzarini, LIGO Directorate 					Date

CHANGE LOG

| Date, version | Summary of Changes |
| --- | --- |
| 2012-03-15 V3 | Added Change Log Corrected HAM references in Section 1. Added hyperlinks as needed Updated Sections: 2. Summary of hazards, 3. Overview, 5. Hazards Analysis, and 6. Signal Recycling Cavity Baffles Hazard Analysis Severity Table |

# Scope

This document covers safety concerns related to the assembly and installation of the Signal Recycling Cavity Baffles in HAM4, HAM5, HAM10, and HAM11.

It must be read before beginning the installation of the Signal Recycling Cavity Baffles, and used in conjunction with the SLC and Viewports Installation Plan Document, document number LIGO-E1000099-v1.

# Summary of Hazards

There are 5 Hazards to be concerned with in the installation of the Signal Recycling Cavity Baffles

- Eye damage from exposure to infrared autocollimator beam (4E)

- Back strain due to heavy lifting and bending

- Bumping one’s head or body in the tighter spaces of the HAM chamber

- Finger damage from torque wrench

- Contamination hazard of the vacuum system

These hazards are described in detail later in the document.

# Overview

During the assembly, installation and alignment of the signal recycling cavity baffles, a task leader shall be assigned to supervise all activities.

Most of the signal recycling cavity baffles weigh < 25 lbs, and they will be lifted manually onto the HAM ISI table and slid into position. The SR2 Scraper Baffle weighs approximately 66 lbs, and must be lifted by two persons onto the HAM ISI table and slid into position. The baffle base will be clamped with appropriate dog-clamps.

As work will be done in a semi-enclosed space, O2 levels should be measured in the area of work (HAM chamber) prior to the start of the work.

The baffles may be installed when HAM tables are occupied with their optics.

Following installation, the baffles will be aligned by projecting an infrared autocollimator beam onto an alignment target attached to the baffle. Serious eye hazard could result if the installer does not wear proper safety goggles/glasses. The IR beam will require the use of protective goggles/glasses to avoid eye damage.

This assembly and installation requires overall common sense and good lab practices. Personnel must have good working knowledge of how to safely use the tools associated with the build and installation, and be aware of the hazards associated with working near a high power infrared light beam. All personnel must have appropriate safety training to work at a LIGO facility.

Figure 1: H1 & L1 HAM4: SR2 Scraper Baffle, SR2 AR Baffle, Hartmann Scraper Baffle, Hartmann Beam Dump

Figure 2: H1 HAM5: SR3 HR Baffle, SR3 AR Baffle, SRM HR Baffle

Figure 3: H2 HAM9: SR2 Scraper Baffle, SR2 AR Baffle, Hartmann Scraper Baffle, Hartmann Beam Dump

Figure 4: H2 HAM10: SR3 HR Baffle, SR3 AR Baffle, SRM HR Baffle

# Related Documentation

SLC and Viewports Installation Plan (LIGO- LIGO-E1000099-v1)

Advanced LIGO Safety: Processes and Guidelines (LIGO-M070360)

LIGO Project System Safety Plan (LIGO-M950046)

LIGO Hanford Observatory Contamination Control Plan (LIGO-M990034)

Chamber Entry/Exit Checklist (LIGO-E000065)

LIGO Hanford Observatory Laser Safety Plan (LIGO-M020131)

LLO Safety Procedure documents (http://www.ligo-la.caltech.edu/contents/internalmain.htm)

# Hazard Analysis

Each hazard and mitigation approach or measure is listed in the severity table in the next section.

## Eye Hazard

The infrared autocollimator beam may have a power level exceeding 1 W; looking directly into the beam may cause retinal damage.

## Lifting and Bending Strain

Each piece of the baffle weighs no more than 35 lbs.  Back strain may occur from improperly lifting and bending to place a heavy baffle onto the HAM ISI table. This may be mitigated by using proper bending and lifting techniques while installing the baffles.

## Vacuum Spatial Awareness

As there will need to be assembly inside the vacuum chamber, personnel should be mindful of where they stand and move as to not damage nearby objects and bump their heads, knees, etc. Damage from accidental bumps can be mitigated from being spatially aware of the working area and by spotting one another.

## Pinching/Cutting of Hands

The installer could hurt their hand or fingers by improper use of the torque wrench used to tighten the dog-clamp bolts, but this can be mitigated with proper attention to how parts are handled. The team must inspect all parts before handling to identify locations of potential hazards (sharp edges and the like).

## Vacuum Contamination

The vacuum system will be opened during this installation process and has the potential to be contaminated. All work must be done in positive pressure clean rooms and all personnel must be garbed in appropriate Class A garb. Standard Class A procedures must be practiced at all times.

# Signal Recycling Cavity Baffles Hazard Analysis Severity Table

| Hazard | Cause | Effect | Unmitigated Severity | Unmitigated Probability Level | Unmitigated Risk Index | Comment | Mitigation | Mitigation Severity | Mitigated Probability Level | Mitigated Risk Index |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Eye damage | Looking directly into IR autocollimator beam | Injury to Personnel | Critical | occasional | 2C | May cause serious retinal damage | Wear appropriate safety glasses/goggles; laser trained personnel required | marginal | remote | 3D |
| Lifting and bending strain | heavy lifting and bending | Injury to personnel; damage to equipment | Marginal | occasional | 3C | Individually, the parts weigh no more than 30 lbs | Use appropriate lifting techniques and precautions | minor | improbable | 4E |
| Head Bumping in vacuum tight spaces | Unawareness of surroundings | Injury to personnel; damage to equipment | Marginal | occasional | 3C |  | At least two people must be in vacuum for lifting purposes and spotting as well | minor | improbable | 4E |
| Finger/Hand Pinching and cutting | Hands caught in between parts when installing | Injury to personnel; damage/ contamination to equipment | Marginal | remote | 3D |  | Use appropriate tool precautions | minor | remote | 4D |
| Vacuum Contamination | Exposed Vacuum Chamber; removal of covers/ wraps | damage to environment | marginal | occasional | 3C |  | All parts handled in clean rooms outside of vacuum; all personnel dressed in Class A approved garb | minor | remote | 4D |

|  |  |  | PROBABILITY |  |  |
| --- | --- | --- | --- | --- | --- |
| SEVERITY OF | E | D | C | B | A |
| CONSEQUENCE | Improbable | Remote | Occasional | Probable | Frequent |
| 1 |  |  |  |  |  |
| Catastrophic |  |  |  |  |  |
| 2 |  |  |  |  |  |
| Critical |  |  |  |  |  |
| 3 |  |  |  |  |  |
| Marginal |  |  |  |  |  |
| 4 |  |  |  |  |  |
| Negligible |  |  |  |  |  |
| Hazard Risk Index |  |  | Risk Code Criteria |  |
| 1A, 1B, 1C, 2A, 2B, 3A |  | Unacceptable |  |  |
| 1D, 2C, 2D, 3B, 3C |  | Undesirable (Directorate decision required) |
| 1E, 2E, 3D, 3E, 4A, 4B |  | Acceptable with review by Directorate |
| 4C, 4D, 4E |  | Acceptable without review |  |

# Text boxes

SR2 Scraper Baffle

SR2

SR3 HR Baffle

Hartmann Beam Dump (typical)

Hartmann Scraper Baffle

SR2 AR Baffle

SR3

SR3 AR Baffle

SRM

SRM HR Baffle

Hartmann Beam Dump (typical)

Hartmann Scraper Baffle

SR2

SR2 Scraper Baffle

SR2 AR Baffle

SR2

SR3 AR Baffle

SRM HR Baffle

SR3

SR3 HR Baffle