## Slide 1: Results from TOBAs Cross correlation analysis to search for a Stochastic Gravitational Wave Background
University of Tokyo
Ayaka Shoda
M. Ando, K. Okada, K. Ishidoshiro, W. Kokuyama, Y. Aso, K. Tsubono

## Slide 2: Prototype TOBA
20cm
20-cm small torsion bar
Suspended by the flux pinning effect of the superconductor
Rotation monitor: laser Michelson interferometer
Actuator: coil-magnet actuator

## Slide 3: Prototype TOBA
Superconductor
Test mass
Laser source
Interferometer

## Slide 4: Previous Result
For the detection of a stochastic gravitational-wave background, simultaneous observation is necessary.
Upper limit on a stochastic GW background

## Slide 5: Simultaneous Observation
Tokyo
Kyoto
~370km
Kyoto
Tokyo
DATE: 21:30 – 7:30, Oct. 29, 2011
Sampling frequency: 500 Hz, the direction of the test mass: north-south

## Slide 6: Data Quality
Equivalent Strain Noise Spectra
Tokyo
Kyoto
Seismic
Magnetic coupling

## Slide 7: Data Quality
10
9
8
7
6
5
4
3
2
1
×10-6
Spectrogram
Tokyo
Kyoto
Glitches
→The data should be selected

## Slide 8: Cross Correlation Analysis
Concept
difficult to predict the waveform of a stochastic GW background
Search the coherent signal
on the data of the two detectors.
Correlation Value
: The signal of i-th detector
: The optimal filter (Weighting function)

## Slide 9: Cross Correlation Analysis
Data selection
Calculate the cross correlation value
Detection test
Set the upper limit
If not detected
Divide the time series data into 200sec long segments
Delete 10% of the segments whose noise level is worst
Choose the analyzed frequency band as 0.035 – 0.84 Hz
Inject mock signals into the real data and calculate the detection efficiency

## Slide 10: Result
Detection threshold
for false alarm rate 5%
NO SIGNAL
Histogram and Cross correlation value

## Slide 11: Result –upper limit
NEW!!
4 times better
Extend explored frequency band
95 % confidence upper limit

## Slide 12: Summary
Established the pipeline of the cross correlation analysis with TOBAs
The stochastic GW background signal is not detected.
Update the upper limit on a stochastic GW background at 0.035~0.840 Hz:

## Slide 13: Backup slides

## Slide 14: Data Selection
Divide time series data into several segments
Remove the segments in which RMS is big
Calculate cross correlation with the survived segments
Tokyo
Kyoto
segment
Time

## Slide 15: Cross Correlation Value
Optimal Filter
：a filter which maximizes the signal-to-noise ratio
Pi ( f ): PSD of i-th detector
Overlap reduction function
: a function which represents the difference of response to the GWs between two detectors
In the case of TOBAs,
same as the interferometer’s one
In this case,

## Slide 16: Optimal filter
The frequency band where the optimal filter is the biggest is chosen as the analyzed frequency band.
Optimal filter = big when the sensitivity to a stochastic GW background is good

## Slide 17: Upper Limit
Mock signal
How big a stochastic GW background can we detect if it would come to this data set?
Make a mock signal of a stochastic GW background
Inject the signal into the observational data
Perform same analysis as explained above
95% confidence upper limit
Repeat 1-3 to compute the rate at which we detect the mock signal.
Detection efficiency
Receiver operating characteristic
Detection efficiency
0.95
The amplitude of injected signals

## Slide 18: Parameter Tuning
There are some parameters whose optimal values are depend on the data quality
The length of the segments
The amount of the segments removed by data selection
The bandwidth of the analyzed frequency band
Determined by the time shifted data.
→200 sec
→10 %
→0.8 Hz
The values which make the upper limit calculated with time shifted data best is used.

## Slide 19: Summary of Analysis

## Slide 20: Data selection
whitening
The analyzed frequency band is excluded from RMS calculation
The indicator of the noise level = Whitened RMS
Avoid making the result intentionally better

## Slide 21: Cross correlation anlysis
signal
GW signal
noise
Cross correlation value
Noise is reduced
Cross correlation value
Fourier transformation

## Slide 22: Detection Criteria
<Y>/Tseg
Probability distribution of <Y>/Tseg
a
za
By the Neuman-Peason criterion,
Note: we do not know the sign of the two signal.
Signal is present
Signal is absent
a
a: false alarm rate
∝Histogram of <Y>/Tseg calculated with time shifted data

## Slide 23: Signal detection
How to decide :
<Y>/Tseg
za
Calculate with diversely time shifted data
Histogram of calculated ＝Histogram of when the signal is absent.
a: false alarm rate
b: false dismissal rate
No
GW signal
with
GW signal

## Slide 24: Future plan
This cross correlation analysis
1 year observation
Big TOBA