## Slide 1: Status of Ground-Based Gravitational-wave Interferometers
July 11, 2012
Daniel Sigg
LIGO Hanford Observatory
Astrod 5, Bangalore, India

## Slide 2: Abstract
We present the status of ground based gravitational wave detectors. All observatories are currently in the process of installing second generation instruments with the intend to introduce the era of detection. The regular observations of sources will require a worldwide network of detectors for reliably localizing the sky position. The LIGO project and the implications of LIGO-Indigo will be discussed in detail.

## Slide 3: Gravitational Waves
10-9 Hz
10-4 Hz
100 Hz
103 Hz
Relic radiation
Cosmic Strings
Supermassive BH Binaries
BH and NS Binaries
Binaries coalescences
Extreme Mass Ratio
Inspirals
Supernovae
Spinning NS
?
?
?
?
?
?
10-16 Hz
Inflation Probe
Pulsar timing
Space detectors
Ground interferometers
?

## Slide 4: Gravitational Wave Signal and Fundamental Noise Sources
Quantum Noise
Shot Noise
Radiation Pressure Noise
Laser Noise
Frequency Noise
Intensity Noise
Thermal Noise
Test masses
Suspensions
Coatings
Vibrational Noise
Ground motion
Acoustic

## Slide 5: Sensitivity Sixth Science Run

## Slide 6: Results from Initial Detectors: Some highlights from LIGO and Virgo
Several ~year long science data runs by LIGO and Virgo Since 2007 all data analyzed jointly
Limits on GW emission from known msec pulsars
  Crab pulsar emitting less than 2% of available spin-down energy in gravitational waves
Limits on compact binary (NS-NS, NS-BH, BH-BH) coalescence rates in our local neighborhood (~20 Mpc)
Limits on stochastic background in 100 Hz range
  Limit beats the limit derived from Big Bang nucleosynthesis
Virgo

## Slide 7: Advanced LIGO Sensitivity
Standard quantum limit
Initial LIGO
Radiation pressure noise
Shot noise

## Slide 8: The Advanced LIGO Detector
Laser
Laser:
200W - 1064nm
Input mode cleaner:
stabilizes frequency
and cleans laser mode
Arm cavities:
Fabry-Perrot cavities store light to effectively increase length
Homodyne Readout
Signal recycling mirror: amplifies readout signal
Input
Test
Mass
End
Test
Mass
4 km
4 km
800kW
800kW
Power recycling mirror: reflects light back coming from the beam splitter, increasing power in the arm cavities

## Slide 9: Advanced LIGO PSL
Designed and contributed by Albert Einstein Institute
Higher power: 10W -> 180W
Better stability
  10x improvement in intensity and frequency stability

## Slide 10: Advanced LIGO Seismic Isolation
Two-stage six-degree-of-freedom active isolation
  Low noise sensors, low noise actuators,
  Digital control system to blend outputs of multiple sensors, tailor loop for maximum performance

## Slide 11: Advanced LIGO Suspensions
UK designed and contributed test mass suspensions
Silicate bonds create quasi-monolithic pendulums using ultra-low loss fused silica fibers to suspend interferometer optics
  Pendulum Q ~105 -> ~108
Electrostatic actuators for alignment and length control

## Slide 12: Advanced LIGO Mirrors
Larger size
  11 kg -> 40 kg
Smaller figure error
  0.7 nm -> 0.35 nm
Lower absorption
  2 ppm -> 0.5 ppm
Lower coating thermal noise

## Slide 13: Current Progress
Install
PSL/ IO table
Install
IMC
Install
Rec’ld vertex MICH
Full interferometer
L1
Full Interferometer
Squeeze Test
H1
July 2014
Install
PSL/ IO table
Install
IMC
Install
Rec’ld vertex MICH
Install
H2
Single arm cavity
DE-Install
Store H2 for India
You Are Here

## Slide 14: Global Network
LIGO
GEO
Virgo
LIGO-India
KAGRA

## Slide 15: VIRGO
Virgo
  European collaboration, located near Pisa
  Single 3 km interferometer, similar to LIGO in design and specification
  Advanced seismic isolation system (“Super-attenuator”)
Advanced Virgo
  Similar in scope and schedule to Advanced LIGO
Joint observations with LIGO since May 2007

## Slide 16: GEO
GEO Collaboration
  GEO as a whole is a member of the LIGO Scientific Collaboration
  GEO making a capital contribution to Advanced LIGO
GEO600
  Near Hannover
  600 m arms
  Signal recycling
  Fused silica suspensions
GEO-HF
  Up-grade underway
  Pioneer advanced optical techniques

## Slide 17: KAGRA
Project approved July 2010
  Lead institution: Institute for Cosmic Ray Research
  Other participants include University of Tokyo, National Astronomical Observatory of Japan, KEK, …
Key Design Parameters
  Underground
  Sapphire test masses cooled to <20K
  150W Nd:YAG laser
  Five stage low frequency (soft) suspension
  Promises sensitivity similar to Advanced LIGO

## Slide 18: LIGO-India Concept
A direct partnership between LIGO Laboratory and IndIGO collaboration to build an Indian interferometer
  LIGO Lab (with its UK, German and Australian partners) provides components for one Advanced LIGO interferometer from the Advanced LIGO project
  India provides the infrastructure (site, roads, building, vacuum system), “shipping & handling,” staff, installation & commissioning, operating costs
LIGO-India would be operated as part of LIGO network to maximize scientific impact
Awaiting formal approval by the Governments

## Slide 19: Why a Global Network?
Source Localization
  Sky position is determined by triangulation from the arrival times
Polarization
  Requires a three dimensional array
Worldwide coincidence greatly increases confidence
Sky position and polarization measurement are required to extract maximum science!

## Slide 20: LIGO-Virgo Network

## Slide 21: India-LIGO-Virgo Network

## Slide 22: Final Thoughts
We are on the threshold of a new era of gravitational wave astrophysics
First generation detectors have broken new ground in optical sensitivity
  Initial detectors have proven technique
Second generation detectors are being installed
  Will expand the “Science” (astrophysics) by factor of 1000
In the next decade, emphasis will be on the network
  Groundwork has been laid for operation as a worldwide network
  India could play a key role