## Slide 1: Modal Damping of a Quad Pendulum for Advanced Gravitational Wave Detectors
Brett Shapiro
Nergis Mavalvala
Kamal Youcef-Toumi
ACC 2012 – Montreal
June 27
Massachusetts Institute of Technology
Notes: My name is Brett Shapiro and I am going to speak to you about the sizing of actuators for a quadruple pendulum used in advanced gravitational waves

## Slide 2: Abstract
Motivation: Observe gravitational waves from astrophysical sources (supernovae, pulsars, black hole mergers, etc) using the LIGO observatories.
Problem: Multi-DOF isolation systems enhance ground motion at high Q resonances. Damped using active feedback. This control introduces additional noise. Optimal control required achieve adequate trade-off.
Solution: Modal damping to simplify and decouple optimization of each mode’s damping. Also permits real-time tuning.

## Slide 3: Outline
LIGO and gravitational waves
Seismic (vibration) isolation
Competing damping control goals
Method of modal damping
Optimization of modal damping
Results

## Slide 4: Gravitational Waves
Pulsar
Supernova
Merging Black Holes
Supernovae
  Asymmetry required
Coalescing Binaries
  Black Holes or Neutron Stars
  Mergers
Pulsars
    Asymmetry required
Stochastic Background
(Big bang, etc.)
Wave of strain amplitude h

## Slide 5: The Laser Interferometer Gravitational-wave Observatory (LIGO)
Livingston, LA
Hanford, WA
3, 4 km interferometers at 2 sites in the US
Michelson interferometers with Fabry-Pérot arms
Optical path enclosed in vacuum
Sensitive to strains around 10-22 -> 10-19mrms
LIGO Budget ≈ $60 Million per year from NSF.
Operated by MIT and Caltech.
Funded by
FI
Test Masses
:
fused silica
,
34
cm diam x
20
cm thick
,
40
kg
SRM
ITM
ETM
Input
Mode
Cleaner
Output
Mode
Cleaner
PRM
BS
4 km
T = 3%
Laser
Φ
m
PD
GW readout
FI
ITM
ETM
125 W
5.7 kW
815 kW
CP
Not to scale
Advanced LIGO configuration
Under construction until ≈2015
Upgrade to Initial LIGO

## Slide 6: If we put LIGO in Cambridge, MA
LIGO spans 16 km2. Cambridge, MA covers 16.65 km2 (wikipedia http://en.wikipedia.org/wiki/Cambridge,_Massachusetts).
Kenmore Square
MIT
Harvard
MGH
Porter Square

## Slide 7
LIGO Scientific Collaboration
Australian Consortium for Interferometric Gravitational Astronomy
The Univ. of Adelaide
Andrews University
The Australian National Univ.
The University of Birmingham
California Inst. of Technology
Cardiff University
Carleton College
Charles Sturt Univ.
Columbia University
CSU Fullerton
Embry Riddle Aeronautical Univ.
Eötvös Loránd University
University of Florida
German/British Collaboration for the Detection of Gravitational Waves
University of Glasgow
Goddard Space Flight Center
Leibniz Universität Hannover
Hobart & William Smith Colleges
Inst. of Applied Physics of the Russian Academy of Sciences
Polish Academy of Sciences
India Inter-University Centre for Astronomy and Astrophysics
Louisiana State University
Louisiana Tech University
Loyola University New Orleans
University of Maryland
Max Planck Institute for Gravitational Physics
University of Michigan
University of Minnesota
The University of Mississippi
Massachusetts Inst. of Technology
Monash University
Montana State University
Moscow State University
National Astronomical Observatory of Japan
Northwestern University
University of Oregon
Pennsylvania State University
Rochester Inst. of Technology
Rutherford Appleton Lab
University of Rochester
San Jose State University
Univ. of Sannio at Benevento, and Univ. of Salerno
University of Sheffield
University of Southampton
Southeastern Louisiana Univ.
Southern Univ. and A&M College
Stanford University
University of Strathclyde
Syracuse University
Univ. of Texas at Austin
Univ. of Texas at Brownsville
Trinity University
Tsinghua University
Universitat de les Illes Balears
Univ. of Massachusetts Amherst
University of Western Australia
Univ. of Wisconsin-Milwaukee
Washington State University
University of Washington

## Slide 8: Projected Sensitivity for Advanced LIGO

## Slide 9: Suspensions and Seismic Isolation
active isolation platform (2 stages of isolation)
hydraulic external pre-isolator (HEPI) (one stage of isolation)
quadruple pendulum (four stages of isolation) with monolithic silica final stage
Advanced LIGO test mass isolation
Ref: LIGO-G1000469-v1; Kissel PhD thesis

## Slide 10
quadruple pendulum (four stages of isolation)
active isolation platform (2 stages of isolation)
Installing prototype quad pendulum with glass optic on metal wires, Jan 2009 at MIT.

## Slide 11: Quadruple Pendulum
Main (test) Chain
Reaction Chain
Control
Damping –stage 1
Cavity length - all stages
Sensors/Actuators
BOSEMs at stage 1 & 2
AOSEMs at stage 3
Opt. levs. and interf. sigs. at stage 2
Electrostatic drive (ESD) at stage 4
Purpose
Test mass (stage 4) isolation.
the test mass consists of a 40 kg high reflective mirror
Stage 1
Stage 2
Stage 3
Stage 4
IR laser

## Slide 12: Multi-stage Isolation Performance
Each stage provides 1/f2 isolation
1/f2
1/f4
1/f6
1/f8

## Slide 13: Two Competing Goals
Damp modes
Limit sensor noise amplification beyond 10 Hz
Along laser beam axis

## Slide 14: Modal Damping with State Estimation
Cartesian
Coordinates
(coupled
dynamics)
Modal
Coordinates
(decoupled
dynamics)
Estimator
Pendulum
= pendulum
eigenvector matrix
= Cartesian coordinates
= sensor sig.
= estimated modal coord.
= Cartesian damping forces
= modal damping forces
mode damping filter
mode damping gain

## Slide 15: Modal Feedback Design
,
,
,

## Slide 16: Damped Response to Impulse from Gnd.
Modes | 1 | 2 | 3 | 4
Freq (Hz) | 0.443 | 0.996 | 2.001 | 3.416
 | 0.040 | 0.018 | 0.009 | 0.001
Assuming perfect state estimation
10 second damping requirement
Impulse Response Simulation

## Slide 17: Estimator Design
Weight cost of estimation error
Weight cost of using noisy sensor
?
Linear Quadratic Regulator (LQR) design

## Slide 18: Choosing Q and R: Not Unique
R is still to be determined

## Slide 19: Solving the R matrix for MIMO Modal Damping
DOFs i are: x, y, z, yaw, pitch, roll
x
z
Try a bunch of R matrices and see what works best
Measure ‘best’ with an auxiliary cost function.

## Slide 20: Modal Estimation Cost
(x is the laser axis)

## Slide 21: Optimal Noise Amplification
Noise requirement
simulation

## Slide 22: Conclusions
Modal damping provides an intuitive way to optimize a highly coupled, many DOF system, with strict noise performance.
Real-time or adaptive tuning possible by adjusting gains on each mode.
Future work to involve implementation on a true Advanced LIGO interferometer.

## Slide 23: Backups
LIGO spans 16 km2. Cambridge, MA covers 16.65 km2 (wikipedia http://en.wikipedia.org/wiki/Cambridge,_Massachusetts).
Kenmore Square
MIT
Harvard
MGH
Porter Square

## Slide 24: Five Pendulum Designs
FI
Test Masses
:
fused silica
,
34
cm diam x
20
cm thick
,
40
kg
SRM
ITM
ETM
Output
Mode
Cleaner
PRM
BS
4 km
T = 3%
Laser
Φ
Input
Mode
Cleaner
m
PD
GW readout
FI
ITM
ETM
125 W
5.7 kW
815 kW
CP
Ref: G1100434

## Slide 25: Backups: Optical Sensor ElectroMagnet (OSEM)
Birmingham OSEM (BOSEM)
Advanced LIGO OSEM (AOSEM)
- modified iLIGO OSEM
BOSEM Schematic
Magnet Types (M0900034)
BOSEM – 10 X 10 mm, NdFeB , SmCo
10 X 5 mm, NdFeB, SmCo
AOSEM – 2 X 3 mm, SmCo
    2 X 6 mm, SmCo
    2 X 0.5 mm, SmCo

## Slide 26: Backups: Quadruple Suspension ESD
Main (test) Chain
Reaction Chain
The electrostatic drive (ESD) acts directly on the test ITM and ETM test masses.
± 400 V (ΔV 800 V)
  ≈ 100 μN
Each quadrant has an independent control channel
Common bias channel over all quadrants
UL
UR
LL
LR

## Slide 27: Backups: Quadruple Suspension
MIT monolithic quad in BSC
June 2010