Thermal Noise Reduction in Future Gravitational Wave Interferometers
Nicolas Smith-Lefebvre
LIGO Caltech
April APS 2013

---
Punch line first

---
Astrophysical benefits beyond Advanced LIGO

---
Advanced LIGO Noise

---
Thermal Noise, a physics lesson

---
Fluctuation-Dissipation Theorem
- The FDT tells us that thermal fluctuations are closely related to friction
- Q is the mechanical quality factor (inverse of fractional energy lost after one oscillation)

---
FDT explains...
- Johnson-Nyquist noise in electronic systems
- Brownian motion of particles in fluids
- Blackbody radiation
- Quantum noise...

---
T and Q are not independent
- Silica gets worse at low temperatures
- Thermoelastic (Zener) damping
Silica loss v T
Silicon loss v T
R. Nawrodt et al arXiv:1003.2893
A. Schroeter et al arXiv:0709.4359

---
Cryogenics in Gravitational Wave Interferometers: the cooling problem
a few Watts absorbed
3MW

---
Cooling methods
Conduction
Radiation

---
Cooling power as a function of fiber diameter and temperature

---
Cooling power as a function of fiber diameter and temperature
More conduction

---
Cooling power as a function of fiber diameter and temperature
More radiation
More conduction

---
Thermal Noise as a function of fiber diameter and temperature

---
Thermal Noise as a function of fiber diameter and temperature
Stiffer fiber

---
Thermal Noise as a function of fiber diameter and temperature
More thermal fluctuations
Stiffer fiber

---
Cooling vs Noise trade-off

---
Primary sources of thermal noise

---
Primary sources of thermal noise
Suspension Thermal Noise

---
Primary sources of thermal noise
Coating Thermal Noise

---
The Silicon Bullet
- Very low intrinsic loss at 124K, where radiative cooling is still feasible
  - Zero crossing of thermal expansion coefficient, so no Zener damping
- Large thermal conductivity (10W/cmK), low thermal distortion, lots of circulating power in the arms
  - Fused Silica is limited to <1MW, (1000 times worse conductivity)
- Requires move to 1550nm laser, squeezed light research maturing rapidly (12dB at high-f)

---
Cryogenic Silicon Suspensions

---
Losses in Silicon Samples @Jena/Glasgow/Moscow
- Losses in silicon samples still limited by surface quality or other dirty physics
- More tests required to hit the true loss limit
Silicon Wafer @ Moscow
Prokhorov, Mitrofanov
Silicon Cantilever @ Jena/Glasgow
Nawrodt et al. arXiv:1003.2893

---
Cryogenic Reference Cavities @Caltech
- Provides experience for many relevant technologies
- Ultra-stable DC frequency reference
- Potentially interesting system for studying macroscopic quantum mechanics

---
High emissivity coating experiment @MIT
5cm

---
Prototype Suspension Test @Caltech
- Early planning
- Shopping for a cryostat
~20cm
250g
5cm diameter
77K shield
~20cm

---
Reducing coating thermal noise
- Traditional materials used for optical coatings have relatively low Q
  - Amorphous Silica/Tantala
  - Q ~ few 104
- High Q optical coatings has been a major research subject for many years
- Recent results on new crystalline materials show order of magnitude higher Q
  - Very exciting!

---
AlGaAs Coatings
arXiv:1302.6489
- Shown to have Q>105
- Thermal noise upper limit measured, consistent with measured Q
- Grown on GaAs substrate, lifted and bonded onto optic (any material)

---
AlGaAs Thermal Noise Estimate
Cole et al.
arXiv:1302.6489

---
AlGaP Coatings
- Also high Q, though no thermal noise measurement yet
- Has the same lattice spacing as Silicon, so can be grown directly on the mirror
Angie Lin, Stanford

---
Possible Sensitivity of Future LIGO

---
Possible Sensitivity of Future LIGO
Cold Silicon

---
Possible Sensitivity of Future LIGO
Cold Silicon
Crystal Coatings