| ECR Title: TMS Telescope Primary Mirror Mounting and Clamps | DCC No: E1300611-v1 |
| --- | --- |
|  | Date: 7-18-13 |
| Requester: Ken Mailand | Impacted Subsystem(s): AOS TMS |  |
| Description of Proposed Change(s): TMS Telescope Production set ( 6 units) To change the Primary Mirror Top Clamp D1002732 from v2 to v3. |
| Reason for Change(s): This will accommodate the thinner Production Primary Mirror, allowing the clamp to properly engage and secure the mirror with a set clamping force. |
| Estimated Cost: $250. |
| Schedule Impact Estimate: Unknown, need response to comments below |
| Nature of Change (check all that apply): Safety Correct Hardware Correct Documentation | Improve Hardware Improve/Clarify Documentation Change Interface Change Requirement |
| Importance: Desirable for ease of use, maintenance, safety Desirable for improved performance, reliability Essential for performance, reliability Essential for function Essential for safety | Urgency: No urgency Desirable by date/event: ____________ Essential by date/event: ____________ Immediately (ASAP) |
| Impacted Hardware (select all that apply): Repair/Modify. List part & SNs: ______________________ Scrap & Replace. List part & SNs:_____________________ Installed units? List IFO, part & SNs: _________________ Future units to be built | Impacted Documentation (list all dwgs, design reports, test reports, specifications, etc.): D1102361 |
| Disposition of the proposed change(s): The disposition of this proposed engineering change request is to be completed by Systems Engineering and indicated in the “Notes and Changes” metadata field in the DCC entry for this ECR. The typical dispositions are as follows: · Additional Information Required: in which case the additional information requested is defined. The ECR requester then re-submits the ECR with the new information using the same DCC number for the ECR but with the next version number. · Rejected: in which case the reason(s) for the rejection are to be given · Approved · Approved with Caveat(s): in which case the caveat(s) are listed · TRB: the ECR is referred to an ad-hoc Technical Review Board for further evaluation and recommendation. It is the System Engineer’s (or designee’s) responsibility to organize the TRB. The System Engineer (or designee) then makes a technical decision based on the TRB’s recommendation. Links to the TRB’s documentation (charge, memos, final report, etc.) are to be added to the “Related Documents” field for this ECR. · CCB: a change request for approval of additional funds or schedule impact is to be submitted to the Configuration Control Board. Links to the CCB’s documentation (CR, etc.) are to be added to the “Related Documents” field for this ECR. Concurrence by Project Management: Acknowledgement/acceptance/approval of the disposition is to be indicated by the electronic “signature” feature in the DCC entry for this ECR, by one the following personnel: · Systems Scientist · Systems Engineer · Deputy Systems Engineer |

Re. TMS Telescope Primary Mirror Mounting and Clamps (LBSC4)

Reference: D1102361 items  #18, 8, 15 ,17 & 6

In this Telescope the optics were installed (mirrors) and the telescope aligned.

Following alignment it was found that the Primary Mirror was not clamped in place securely.

The clamp system was from the first article, and not the production set, which uses a thinner Primary Mirror and clamps to suit.

The Primary Mirror is orientated in a vertical plane, and has 3 face clamps, on standoff's at the 12, 4, and 8 o'clock positions.

The back face of the mirror was meant to contact with three pads on the back plate and are in line and opposite the face clamps.

The clamps did not make contact with the Mirror face, and force it against the back plate pads for a positive location before alignment.

The mirror has a set screw in the 12 o'clock clamp that contacts the barrel forcing

the mirror to a three place radial contact preventing x-y movement.

The mirror now has a non uniform gap between the back face and pads.

Ref. T1300636-v1

There are ways to address the above issue:

1)To leave it alone 'as is' since it is now aligned.

pro. _No time or effort expended

con. _The mirror can move when the telescope or frame is moved or flexed in moving, or thru temperature cycling.

2) To carefully slide shims under the wedge shaped gap at the back between the mirror and back plate (3 places) then add the new front clamp.

pro. _Minimum effort and time

con. _The possibility of moving the mirror a small amount in clamping.

3) Installing the production clamp and re-seating the mirror.

pro. _This Mirror will be securely placed.

con. _This will require a realignment, may impact on schedule

NOTE:

The above Mirror issue is with One assembled TMS Telescope for LLO BSC4-X

Reference Other Installations:

LLO-Y 	We can use the D1003732 -v3 clamp in initial assembly.

LHO-X	Modified the Standoff achieving the same result in clamping.

LHO-Y	Installed (WBSC6-Y) First Article Thick Mirror, and Clamp to Match.