## Slide 1: Progress on Cryogenics for aLIGO upgrades
Brett Shapiro
Stanford University
LIGO

## Slide 2: Summary
Cryo test mass problem statement
LIGO III quad pendulum modeling – summer student work
  SUS conceptual design modeling
  Heat shield beam tube length
Stanford experiments
Future Work
LIGO

## Slide 3: Cyro Test Mass Problem Statement
* For LIGO III, reduce suspension and coating thermal noise by cooling the lower quad to 124 K (-149.15 C)
  Si test masses (blue team in T1200031)
  Get to 124 K in a timely manner
  Then maintain 124 K
Include a warm-up scheme (don’t forget!)
Do not increase the test mass lossiness
  Emissive coatings, heat links, thick sus fibers, etc
Do not compromise passive seismic isolation
  Cables, hoses, links, etc
The same seismic isolation platforms (ISIs, HEPIs)
  Limit the amount of extra weight on the ISI
  Leave the rest of the BSC warm

## Slide 4: Possible LIGO III Cryogenic Upgrade
120 K
295 K
Heat shield
77 K
ISI stage 2
Vacuum flange
Flexible liquid nitrogen hose
(77 K = -196 C)
clamp
1560 nm laser rather than 1064 nm
See also G1200246-v1
≈ 3 W at 120 K
10 m
T1300556

## Slide 5: Quad pendulum modeling
LIGO III Conceptual Design
of blue team approach
in T1200031
LIGO

## Slide 6: Possible LIGO III Mechanical Upgrades
10 kg
20 kg
Main
chain
Reaction
chain
143 kg
Main
chain
Reaction
chain
Advanced LIGO quad pendulum
Preliminary LIGO III quad pendulum
G1300966
2.14 m
1.626 m
40 kg
20 kg
40 kg
20 kg
Fused silica, 295 K
Silicon, 120 K
? kg
? kg
? kg

## Slide 7: Optimizing the mass distribution
m: mass of stage
L: wire length
k: vertical stiffness
x: longitudinal displacement
v: vertical displacement
MATLAB model

## Slide 8: Optimizing the mass distribution
m: mass of stage
L: wire length
k: vertical stiffness
x: longitudinal displacement
v: vertical displacement
Fixed weight limit ≈ 270 kg
Target test mass m4 ≈ 143 kg
Best m1, m2, m3?
Meet or beat
aLIGO at 10 Hz
MATLAB model

## Slide 9: Model search for best mass values
Best values: m3=33.68 kg, m2=42.65 kg -> m1 = 51.67 kg
For 143 kg test mass, 270 kg payload, and 0.535 m wire lengths
See T1300786

## Slide 10: Longitudinal Isolation Asymptote
See T1300786
Asymptote:

## Slide 11: Optimal Longitudinal Isolation
Given constrained test mass and payload:
Unique optimal solution of isolation asymptote:
See T1300786

## Slide 12: Optimal Longitudinal Isolation
Given constrained test mass and payload:
Unique optimal solution of isolation asymptote:
See T1300786

## Slide 13: Optimal Longitudinal Isolation
Given constrained test mass and payload:
Unique optimal solution of isolation asymptote:
See T1300786

## Slide 14: Optimal Longitudinal Isolation
Given constrained test mass and payload:
Unique optimal solution of isolation asymptote:
See T1300786

## Slide 15: Optimal Longitudinal Isolation
Given constrained test mass and payload:
Unique optimal solution of isolation asymptote:
See T1300786

## Slide 16: Optimal Longitudinal Isolation
Given constrained test mass and payload:
Unique optimal solution of isolation asymptote:
Iterate a few times to solve both simultaneously
See T1300786

## Slide 17: PUM and Test Mass Bounce Mode
m3
m4
…
L4
See T1300786

## Slide 18: PUM and Test Mass Bounce Mode
m3
m4
…
L4
Vertical bounce frequency (Hz):
* U. Gysin, S. Rast, P. Ruff, E. Meyer, D. W. Lee, P. Vettiger, C. Gerber. “Temperature dependence of the force sensitivity of silicon cantilevers”,
2004, Physical Review B, Volume 69, Number 4, http://prb.aps.org/abstract/PRB/v69/i4/e045403
See T1300786

## Slide 19: PUM and Test Mass Bounce Mode
m3
m4
…
L4
Vertical bounce frequency (Hz):
* U. Gysin, S. Rast, P. Ruff, E. Meyer, D. W. Lee, P. Vettiger, C. Gerber. “Temperature dependence of the force sensitivity of silicon cantilevers”,
2004, Physical Review B, Volume 69, Number 4, http://prb.aps.org/abstract/PRB/v69/i4/e045403
For longitudinal optimal solution with m3 = 33.74 kg, m4 =143 kg
For aLIGO, fbounce = 9.27 Hz
See T1300786

## Slide 20: PUM and Test Mass Bounce Mode
m3
m4
…
L4
Vertical bounce frequency (Hz):
* U. Gysin, S. Rast, P. Ruff, E. Meyer, D. W. Lee, P. Vettiger, C. Gerber. “Temperature dependence of the force sensitivity of silicon cantilevers”,
2004, Physical Review B, Volume 69, Number 4, http://prb.aps.org/abstract/PRB/v69/i4/e045403
For longitudinal optimal solution with m3 = 33.74 kg, m4 =143 kg
For aLIGO, fbounce = 9.27 Hz
No solution that meets both aLIGO performance and our goals for payload and test mass weight.
See T1300786

## Slide 21: 3 Quad Conceptual Designs
T1300786
Higher payload
Lighter
Test mass
Ideal masses with PUM springs

## Slide 22: Quad pendulum modeling
Heat shield beam tube length
LIGO

## Slide 23: Beam Tube Heat Shield Length
ε
Beam tube
Blackbody disc model
Heat Shield
rj = 0.28m
ri = 0.6225m
Test Mass
L (m)
What is the optimal heat shield length in the beam tube?
Tj = 120 K
Ti = 295 K
T = 77 K
Ε = 1
Ε = 0.1
See T1300556

## Slide 24: Heat shield length in beam tube
Beam tube shield length L (m)
Black body power from beam tube arriving at test mass
≈1/3 drop for every factor of 2 L
See T1300556
Test mass emissivity = 0.1

## Slide 25: Stanford Cryo Test Mass Experiments
LIGO

## Slide 26: Goal of Stanford Cryo Experiments
Stanford prototypes
Model
LIGO III design
understand
modify
extrapolate
Fastest method of cooling a LIGO III test mass to 124 K, -150 C

## Slide 27: Experimental Setup
Test dewar
Heat shield

## Slide 28
1 kg Si test mass
Flexible cold link
Temperature sensor clamp
Test dewar
Nitrogen plumbing

## Slide 29
Liquid nitrogen dewar
Test dewar
Pumps

## Slide 30
Nitrogen vent

## Slide 34
Much faster cool down

## Slide 35: Future work
More cooling experiments
  Iterate liquid nitrogen cooling design
  Apply emissive coatings
Modeling to understand cooling results
Modeling to extrapolate results to LIGO III
More complicated experiments
  Hang test mass on blade spring
  Move LN2 system onto vacuum seismic table with minimal seismic impact
LIGO

## Slide 36: Backups

## Slide 37: Optimal Fiber Length
Optimal length for fiber stress of 1.4 Gpa.

## Slide 38: Comparing Quad Models

## Slide 39: Longitudinal Stiffness
* Stiffness is the tension in the wire divided by the wire length

## Slide 40: How to get a LN2 Hose to ST2
Stage 0
Stage 1
Stage 2
Stage A
LN2 hose
Actuators
Sensors
Extra stage, A, in parallel with stage 1 carries hose. Stage A is actuated to follow stage 2 so the hose has does not short seismic isolation.

## Slide 43
LN2 Puddled around shield at bottom

## Slide 44
N2 ice around shield at bottom. This happens when you try to remove the LN2 by turning on the roughing pumps.