## Slide 1
Gravitational Wave Detection
With Initial and Advanced LIGO
Gregory Harry
American University
US Naval Observatory
July 10, 2014
LIGO-G1400749

## Slide 2: Gravitational Waves
Gravitational waves are a prediction of Einstein’s theory of gravity
Similar to electromagnetic waves (light) from Maxwell’s equations
Two major differences
Spin two (tensor) shape
Much smaller amplitude
  Strain
  Kilometer baseline, subnuclear length changes

## Slide 3: Indirect Evidence for GW
Known binary neutron star binaries will merge within 100 million years
Hulse and Taylor observation
  Change in orbit of neutron star binary
BICEP2 result
  If it holds up, gravitational waves from Bing Bang

## Slide 4: Direct Gravitational Wave Sources
Short Duration Long Duration
Modeled
Unmodeled
Compact Body Inspirals
Periodic Sources
Bursts
Stochastic Background

## Slide 5: LIGO Interferometers
US has two sites
  Livingston, Louisiana (LLO) and Hanford, Washington (LHO)
4 kilometer-long beam tubes
  Entire 8 km length in vacuum
  Low seismic noise environment
Modern gravitational wave detectors use interferometers
Sense tiny motion of mirrors
L shape for tensor waves

## Slide 6: Initial LIGO
Science data 2002 – 2010
  Over full year coincident
Bandwidth 40 – 3000 Hz
Exceeded sensitivity goal
3 detectors. 24 km/12 km
20 W Nd:YAG laser
10 kg silica optics
Steel wire suspensions

## Slide 7: Initial LIGO Astrophysics: Burst and Inspiral Sources
Gama ray bursts (GRBs) may be compact body inspirals
Short GRBs 050311 and 070201
  Locations in galaxies M81 and M31
  Inspiral excluded at >98%
M31, GRB 070201
GW100916
  Consistent with compact body inspiral
  Blind injection done to test analysis process

## Slide 8: Initial LIGO Astrophysics: Pulsars and Stochastic
Pulsars can give continuous GW from asymmetric rotation
Crab pulsar
Ellipticity limit in 116 pulsars
  Lowest upper limit
Stochastic GW from primordial background
  Nucleosynthesis limit
Limits on point sources

## Slide 9: Advanced LIGO
Goal: 10X sensitivity
  10 – 5000 Hz
  200 Mpc NS inspiral range
  Inspirals possible ~ 1/month
  One day with Adv LIGO = a few years with initial LIGO
Project began 2008
  Installation started 2010
  Building three interferometers
  Installation finishing this year
Image courtesy of Beverly Berger
Cluster map by Richard Powell
Initial LIGO

## Slide 10: Advanced LIGO Installation

## Slide 11: Advanced LIGO Sensitivity
Limited by Earth motion, thermodynamics, and quantum mechanics
Better
seismic
isolation
Higher
power
laser
Better
test masses

## Slide 12: Advanced LIGO Seismic Isolation and Suspension
Quadruple suspension
  Based on GEO600 triples
  Seismic noise reduction above pendulum
  Final stage silica fibers to reduce thermal noise
Seismic isolation
  Hydraulic preisolator external to vacuum
  In vacuum, two stage, 6 DOF active mass/spring system

## Slide 13: Advanced LIGO Mirrors and Coatings
Fused silica optics
  40 kilograms
  Very low absorption
  Monolithic connection to suspension
Optical coatings
  34 centimeter diameter
  5-6 cm beam spot
  Very low absorption
  Low thermal noise

## Slide 14: Advanced LIGO Laser and Interferometry
Laser
  Nd:YAG 1064 nm
  Three stage NPRO
  180 Watts
  Shot noise limited
Interferometer
  Power recycling increases arm power to 800 kW
  Signal recycling to tune sensitivity curve
Coating Thermal

## Slide 15: Status and Science Plans
90% complete by budget
Remaining activities
  Finish installation at LHO
  Testing at both LLO and LHO
  Computer procurement
Goal: Direct detection century after Einstein’s 1916 GW paper
Date | Length | Sensitivity
Late 2015 | 3 months | 40-80 Mpc
2016/2017 | 6 months | 80-120 Mpc
2017/2018 | 9 months | 120-170 Mpc
2019 | Full year | 200 Mpc
See Arxiv/gr-qc/1304.0670, 1003.2480

## Slide 16: Multimessenger Astronomy
Low latency data analysis happening as data comes in → Generate triggers
Increase confidence in GW detection
More precise sky location, better understanding

## Slide 17: Livingston is Locked and Accepted
Livingston interferometer has locked for more than 2 hours (135 minutes)
  June 30, 2014
  Now commissioning
  When Hanford locks for > 2 hours, late 2015, construction phase ends
BREAKING NEWS
LLO LOCKS FOR 2 HOURS

## Slide 18: Worldwide Network
KAGRA: Japan
Adv Virgo:
Italy
GEO HF:
Germany
Adv LIGO:
Hanford
Adv LIGO:
Livingston

## Slide 19: LIGO India
Third Advanced LIGO detector in India
Site selection committee set up
Interferometer hardware stored
Join network 2022
Training and collaboration now

## Slide 20: Conclusion
Initial LIGO complete
  Validated technology
  Contributed to astrophysics but no detections
Advanced LIGO
  Installation in US nearly complete
  Lower noise technology→10X sensitivity
  Science runs begin 2015, detections likely
LIGO India
  Expect approval soon
  Improve sky positioning of sources