## Slide 1
Cryogenic Systems for Future LIGO Detectors - G1400940
Brett Shapiro, Brian Lantz, Tim MacDonald, Dakota Madden-Fong
Quadruple Suspension Redesign
LIGO III Cryogenic System
The figures below show a recent measurement of the magnitude of vibration induced by flowing fluids. The experiment uses water for its ease of use and similarity to LN2 in terms of density and viscosity. So far the measured vibration is low enough it is difficult to distinguish from noise. More work is required.
Cooling with Cu cables or Liquid Nitrogen (LN2) Pipes?
Integrated System Test Beginning at Stanford
Vacuum wall
LN2 feedthrough
GN2 feedthrough
chiller
ISI Stage 2
ISI Stage 1
LN2 return
LN2 supply
Cold link
motor
Stainless steel legs
Heat shield
T1400553
1 kg silicon
test mass
Cold link
Maraging steel
blade spring
LN2 pipe around shield
 | Heat Transfer | Added weight | Seismic shorting | System Complexity | Vacuum leaks
Cu cables |  |  |  |  | 
LN2 pipes |  |  |  |  | 
Show stopper
Main Chain
Reaction Chain
52 kg
143 kg
silicon
42 kg
34kg
silicon
20 kg
10 kg
2.1 m
Advanced LIGO
LIGO III
1.6 m
Main Chain
Reaction Chain
22 kg
40 kg
silica
ETM ITM
53 kg 60 kg
26 kg 20 kg
One of 3 conceptual designs for a LIGO III quad suspension discussed in T1300786. The test mass is silicon rather than fused silica, with an increase in weight. Silicon is useful at cryogenic temperatures for its low loss and high thermal conductivity. The remaining stages are optimized in terms of mass and wire length. This particular design assumes the test mass hangs from silicon springs at the penultimate mass. However, T1300786 also considers designs without these springs, at the expense of some increase in noise.
LN2 has more cooling power, and can be pumped where needed, but it is unknown how much noise its flow will generate. The LN2 is pre-cooled so it does not boil.
This poster explores the details of a cryogenic system for the ITM and ETM suspensions in 3rd generation LIGO observatories. Cold silicon test masses improve thermal noise and thermal lensing issues. The poster follows the Blue Team description in the Instrument Science White Paper T1200199.
The figure on the left illustrates an overview of what such a system may look like for one of the test mass suspensions. The figure on the right is a planned test at the Stanford facility integrating as many of these components as possible.
?
Good
Fair
Risky
Stage 2
Stage 1
Cu Water pipes with Viton damping
Vibration test plate on viton balls
HS1 Geophone
The measured vibration for reasonable flow rates is difficult to distinguish from the experiment noise floor. This noise floor, projected onto BSC-ISI stage 2 Rz motion (the ‘quietest’ ISI DOF), is more than the seismic noise.
Silicon fibers
The goal of this test is to show we can build a low vibration cryogenic environment.
≈ 124 K
295 K
Heat shield at
80 K maintains 124 K through radiative coupling
Active Seismic Isolation Table
ISI stage 2
Vacuum flange
Flexible LN2 tubing
or Cu cables
clamp
1560 nm MW laser
≈ 3 W absorption at 124 K
≤ 10 m
≈140 kg Si test mass
…
…
chiller
Not shown:
A movable cold link achieves the initial test mass cool down in ≈ 1 day.