## Slide 1: Interferometry and Optics in Advanced LIGO
ASPE Boston 2014-11-13
David Shoemaker
For the LIGO Scientific Collaboration

## Slide 2: LIGO Laboratory: two Observatories and Caltech, MIT campuses
Caltech
MIT
Mission: Develop gravitational-wave detectors; Operate them as astrophysical observatories
Jointly managed by Caltech and MIT
Requires instrument science at the frontiers of physics fundamental limits
This talk covers 10-21 of a very neat story!
LIGO Livingston
Notes: LIGO is actually two observatories.
Describe parameters
Emphasize that the arms are in ultra high vacuum. 8 km of steel 1.2 m dia beam tubes at each site
Separate observatories allow for coincidence detection – since the detectors see uncorrelated noise, only a true gravitational wave would appear on all the interferometers with the correct amplitude.
Emphasize that the LIGO Observatories were designed and are operated by Caltech and MIT

## Slide 3: Gravitational waves
Gravitational waves are propagating dynamic fluctuations in the curvature of space-time (‘ripples’ in space-time)
Emissions from rapidly accelerating non-spherical mass distributions
  Practically, need massive objects moving at speeds approaching the speed of light
  According to GR, GWs propagate at the speed of light
  Quadrupolar radiation; two polarizations: h+ and hx
  Physically, GWs are strains
  GWs carry direct information about the dynamics of matter
  Space is stiff… h is 10-21 for a ~monthly signal rate
Credit: T. Strohmayer and D. Berry

## Slide 4: Interferometric Gravitational-wave Detectors
Enhanced Michelson interferometers
Passing GWs modulate the distance between the end test mass and the beam splitter
The interferometer acts as a transducer, turning GWs into photocurrent proportional to the strain amplitude
Arms are short compared to GW wavelengths, so longer arms make bigger signals  multi-km installations
Arm length limited by taxpayer noise….
Laser 
Photo
diode
4km
4km

## Slide 5: The real instrument is far more complex…
Reality axis

## Slide 6: Design drivers
Long arms and extreme interferometry lead to many design impacts
World’s biggest UHV vacuum system, straighter than earth’s curvature
Optics size – 1064 nm over 4km means beam spots of ~12 cm, 34cm optics
Readout requirements of one part in 1010 of a fringe requires 200W CW Nd:YAG lasers, stabilized in frequency, intensity, and pointing; boosted to ~1 MW with optical resonant cavities
Pointing and control requirements – hold 4km cavities on resonance to 10-15 m; point optics with microradian RMS motion; 5 coupled cavities, 21 coupled DOF
Suppress seismic and anthropogenic noise input; another 18×5 + 12×5 MIMO DOF

## Slide 7: Test Masses
Half-nm flatness over 300mm diameter
0.2 ppm absorption at 1064nm
Coating specs for 1064 and 532 nm
Mechanical requirements: bulk and coating thermal noise, high resonant frequency
Requires the state of the art in substrates, polishing, coating
Both the physical test mass – a free point in space-time – and a crucial optical element
Test Masses:
34cm  x 20cm
40 kg
40 kg
BS:
37cm  x 6cm
ITM
T = 1.4%
Round-trip optical loss: 75 ppm max
Compensation plates:
34cm  x 10cm

## Slide 8: Test mass Optics figure
In-house metrology on 300 mm diameter shows 0.66 nm RMS
  Note spiral from planetary system; about 0.2 nm pk-pk
In-situ measurements of as-built 4km cavity show results are better than requirements!

## Slide 9: Seismic Isolation: Multi-Stage Solution (talk by Matichard)
Objectives:
  Render seismic noise a negligible limitation to GW searches
  Reduce actuation forces on test masses
Both suspension and seismic isolation systems contribute to attenuation
Choose an active isolation approach, 3 stages of 6 degrees-of-freedom :
  1) Hydraulic External Pre-Isolation
  2) Two Active Stages of Internal Seismic Isolation
Low noise sensors (position, velocity, acceleration) are combined, passed through a servo amplifier, and delivered to the optimal actuator as a function of frequency to hold platform and 1-ton payload still in inertial space
At 10Hz: 10-12 m/rHz and -80 dB transmissibility
~2m

## Slide 10: Test Mass Quadruple Pendulum suspension
Optics Table Interface
(Seismic Isolation System)
Damping Controls
Electrostatic
Actuation
Hierarchical Global
Controls
Quadruple pendulum suspensions for the test masses; second ‘reaction’ mass to give quiet point from which to push
Create quasi-monolithic pendulums using fused silica fibers to suspend 40 kg test mass
  VERY Low thermal noise! Q = 109
Another element in hierarchical control system
Final elements
All Fused silica

## Slide 11: Advanced LIGO commissioning just starting – already more sensitive than any previous detector
Sufficient in principle to detect the GW signal from a binary star system 120,000,000 light years distant
Frequency (Hz)
Accomplished in 4 months what it took
~ 4 years to do in Initial LIGO

## Slide 12: The Last Page
The next generation of gravitational-wave detectors will have the sensitivity to make frequent detections
The Advanced LIGO detectors are coming along well, planned to observe in 2015
The world-wide community is growing, and is working together toward the goal of gravitational-wave astronomy
www.advancedligo.mit.edu
Goal: Direct Detection 100 years after Einstein’s 1916 paper on GR