|  | REQUEST FOR WAIVER OR DEVIATION SCAN AND EMAIL COMPLETED FORM TO QUALITY@LIGO.CALTECH.EDU NOTE: DO NOT SUBMIT DISCREPANT MATERIAL UNTIL AUTHORIZED BY LIGO |
| --- | --- |
| PART NO. D0900461 | REV. v5 | PART NAME L1 SR3 Suspension | P.O. NO. NA | P.O. QTY: NA DISCREPANT QTY: 1 (the L1 instance) |
| SUPPLIER: NA, internal assembly process CONTACT: Janeen Romie | TEL #: 225.686.3109 EMAIL: janeen@ligo-la.caltech.edu | DATE: 1/14/2013 |
| DESCRIPTION OF REQUEST (PLEASE GIVE COMPLETE TECHNICAL DESCRIPTION OF DEVIATION, REFERENCING DRAWING ZONE AS APPROPRIATE) The magnet/dumbbell assembly on the lower right of the penultimate mass of SR3 has fallen off. We would like to re-glue it in-situ. However, due to the assembled state of the suspension, a heat lamp is not a good idea, due to the various materials nearby. We would like a waiver for this tiny bond, .0044 in ^2. Thoughts? |
| ROOT CAUSE Schedule pressure; delays close-up of the LHAM5 vacuum chamber. Would require extensive disassembly. | CORRECTIVE ACTION No elevated temperature bake. Note that the UHV qualification of the adhesive used (EP30) was done for room temperature (non-elevated) cure. |
| SIGNATURE Janeen Romie (1/14/2013 email) | TITLE Suspensions Lead Engineer | IMPLEMENTATION DATE: ASAP |
| ACTION TAKEN / DISPOSITION INSTRUCTION (FOR LIGO USE ONLY) Approved by Dennis Coyne (Systems Engineer) on 1/14/2013 | DATE RECEIVED 1/14/2013 |
|  | PROGRAM aLIGO Project |
|  | QUALITY ASSURANCE NA | DATE |
|  | DESIGN ENGINEER NA | DATE |
|  | OTHER | DATE |

LIGO-Q1500003-v1