How to measure Open Loop Gain
(and UGF)
A Tutorial

---
Transfer Functions
- Linear systems can be characterized in the frequency domain by the amplitude and phase response to sinusoidal excitations, represented as a complex function of frequency.
- Can be measured with “swept sine” method
T(f)

---
Features of linear systems
G(f)+H(f)
G(f)
+
=
H(f)
G(f)*H(f)
G(f)
H(f)
=

---
Bode Diagram
A common graphical representation of transfer functions
|T(f)|
arg(T(f))

---
Coherence
- Important note: measurement signal to noise ratio is characterized by the coherence function
- Coherence ~ 1 means small uncertainty in data points
- Good Reference: “Random Data” Bendat and Piersol (Appendix)

---
Negative Feedback System
- A linear system where signals propagate through loops
- Each piece is linear
T(f)
+
-
K(f)
H(f)

---
Open Loop Gain
Collapse all TFs around the loop to a single TF
+
-
G(f)

---
The response of the loop to excitations
B
A
X
+
+
-
G(f)

---
Extracting the Open Loop Gain
- The ratio of the two measurements gives the open loop gain.
- Most network analyzers can perform the ratio in a single measurement. (One excitation port, two measurement ports)
- Important that coherence of both measurements is high. (Either by longer measurement or larger excitation amplitude)

---
The Unity Gain Frequency
- Defined as |G(f_U)| = 1
- The UGF characterizes the time scale for the loop to stabilize against external excitations
|G(f)|
f_U
arg(G(f))