## Slide 1: VOPO Optical Layout
LIGO MIT Lab
Matichard, Fabrice
Fernandez Galiana, Alvaro

## Slide 2: Optical Layout
2 different layouts:
  O3 Squeezer model with filter cavity + RFPD in Vacuum
  O2 Squeezer model (early squeezing)

## Slide 3: Squeezer Model
Solid Works Optical Layout
Mirror:
  Mass: 159.176 g
  Quantity: 11 / 19
Lens:
  Mass: 121.375 g
  Quantity: 7 / 10

## Slide 4: Squeezer Model
Solid Works Optical Layout
Beam Dump:
  Mass: 202.27 g
  Quantity: 2 / 5
QPD:
  Mass: 142.98 g
  Quantity: 2 / 3

## Slide 5: Squeezer Model
Solid Works Optical Layout
Polarizers:
  Mass: 159.176 g
  Quantity: 2+2 / 2+2
Wave Plate:
  Mass: 300 g
  Quantity: 1 / 2
NOTE: At this point the polarizers have been modeled as mirrors. A more realistic model has to be done to the two kinds of polarizers that will be used.

## Slide 6: Squeezer Model
Solid Works Optical Layout
Fibers In:
  Mass: 195.175 g
  Quantity: 2 / 2
RFPD in Vacuum
  Mass: 270.41 g
  Quantity: 0 / 2
NOTE: At this point the
fiber In have been modeled
as mirrors with pico motors. A
more realistic model has to be done to
the two kinds of polarizers that will be used.
NOTE: At this point the
model used is for a 4” beam
height while the real one will be at 2.5”

## Slide 7: Squeezer Model
Solid Works Optical Layout
Faraday Rotator:
  Mass:
    Base: 170.43 g
    Rotator: X g
  Quantity: 1 / 1
NOTE: At this point the
Faraday Rotator has been
modeled as just its base and
with a rough design that will
be improved once the Faraday
rotator model will be obtained.
Base (6061-T6 Al)
EOT Faraday Rotator

## Slide 8: O2 Squeezer Model
O2 Solid Works Optical Layout

## Slide 9: O2 Squeezer Model
O2 Solid Works Optical Layout
Beam Dump (2)
Mirror (11)
Lens (2)
QPD (2)
Polarizer (2+2)
Faraday Rotator
Wave Plate
Fiber In (2)

## Slide 10: O2 Squeezer Model
Mass Budget
  Without Balancing Masses
NOTE: The blades design is made for a 37.5 kg suspended mass. With that design, that means 17.28 kg of balanced mass
Model used in FEA

## Slide 11: O3 Squeezer Model
O3 Solid Works Optical Layout

## Slide 12: O3 Squeezer Model
O3 Solid Works Optical Layout
Beam Dump (5)
Mirror (19)
Lens (7)
QPD (3)
Polarizer (2+2)
Faraday Rotator
Wave Plate (2)
Fiber In (2)
RFPD (2)

## Slide 13: O3 Squeezer Model
O3 Solid Works Optical Layout
  “Conflict” areas
NOTE: One of the biggest fitting
issues involves the 5 beam dumps.
With the configuration shown in the
actual SW model they could not be placed.
So they will have for sure to be redesigned

## Slide 14: O3 Squeezer Model
Mass Budget
  Without Balancing Masses
NOTE: The blades design is made for a 37.5 kg suspended mass. With this design, that means 14.17 kg of balanced mass
Model used in FEA

## Slide 15: O3 Squeezer Model
Conclusions:
  Layout is “feasible” (Detailed layout is needed to confirm it)
  Model has to be refined with the proper dimensions
  Part masses have to be checked with the existing real pieces
  Beam Dumps will have to be redesigned (lack of space)
  Blade design may have to be reconsidered (17.28kg / 14.17 kg of balancing mass)