## Slide 1: Interferometer configurations for Gravitational Wave Detectors
Koji Arai (新井宏二) – LIGO Laboratory / Caltech
GW mini-school: Beijing Normal University 2016/9/15~18
LIGO-G1601926-v1
引力波

## Slide 2: Optical configurations

## Slide 3: Laser interferometry
GW detection
= High sensitive detection of displacement
Laser interferometry is an indispensable technology (lambda ~ 1um)
We use optical cavities in many places
What is an optical cavity?

## Slide 4: Gaussian beam
Propagation of EM waves
  Plane wave Spherical
  wave
  Gaussian beam:
  A solution to paraxial approximated wave equation
  Amplitude distribution of the beam is Gaussian
Equiphase
Planes
Coherent
Light source
Plane-wave like
Spherical-
wave like
waist
divergence
angle
Rayleigh range

## Slide 5: Fringes
Two beams overlap at the BS
Differential change of the arm length
=> fringe condition changed
Dark Fringe
Bright Fringe
dx
Power
Power

## Slide 6: Fringes
Contrast
Dark Fringe
Contrast
Light intensity at the output with a mirror swept
Contrast Defect with mirror tilting

## Slide 7: Simplified interferometer GW detector
Differential motion => Michelson interferometer

## Slide 8: Introduction ~ Interferometer?
Interferometry
  Utilize characteristic of a Michelson interferometer as a length comparator
Michelson
Interferometer
Advanced LIGO
Dual-Recycled Fabry-Perot Michelson Interferometer
In reality...
Fabry-Perot cavity
No worries: It’s just a combination of MI and FPs

## Slide 9: Plain wave (single mode) model

## Slide 10: Michelson interferometer
Light intensity at the output port
  Difference of the electric fields from the arms
  Output intensity is sensitive
  to the differential phase

## Slide 11: Michelson interferometer
Frequency response of the Michelson to GWs
Jean-Yves Vinet,et al
Phys. Rev. D 38, 433 (1988)
Frequency response
of the Michelson interferometer
Ω: optical angular frequency, λOPT laser wavelength
ω: angular frequency of GW, λGW wavelength of GW

## Slide 12: Michelson interferometer
Frequency response of the Michelson to GWs
DC Response
longer -> larger
Cut off freq
longer -> lower
Notch freq
f = n c / (2 L)
  Michelson arm length optimized for 1kHz GW -> 75km, too long!

## Slide 13: Michelson shot noise limit
Quantum noises: Shot noise
  Photon shot noise associated with photodetection
  Michelson interferometer
  Michelson response (@DC)
at the limit of d𝜙->0
  iDC : DC Photocurrent
  η : PD Quantum Efficiency
  ν : Optical Frequency
Shot-noise limit of the Michelson phase sensitivity
  1.3x10-20 1/sqrtHz
  @1W, 1064nm, 4km
Michelson
Strain Sensitivity
  (5x10-17 m/sqrtHz)

## Slide 14: Supplemental slide
Shot noise derivation

## Slide 15: Fabry-Perot optical resonator
Storing light in an optical cavity
  Input vs circulating: constructive Prompt reflection vs leakage: destructive => The circulating field grows up
  N times more power Equivalent to have N times longer arm
Finesse
Folding Number
99%
99.999%

## Slide 16: Fabry-Perot optical resonator
Storing light in an optical cavity

## Slide 17: Fabry-Perot optical resonator
Storing light in an optical cavity
  Field equations
Very fast phase response

## Slide 18: Pound-Drever-Hall technique (PDH)
Signal extraction scheme for the cavities
  Phase modulation -> RF optical sidebands
  Reflected beam -> detected / demodulated
Laser
Electro-Optic
Modulator
Faraday
Isolator
or
Pick-off mirror
dL or f
V

## Slide 19: Fabry-Perot optical resonator
Storing light in an optical cavity
Finesse
DC Response
amplification
Cutoff freq “Cavity pole”
  1. FP increases stored power in the arm
  2. FP increases accumulation time of the signal
  => Above the roll-off, increasing F does not improve the response

## Slide 20: Fabry-Perot Michelson Interferometer
Differential nature of the Michelson + Longer photon storage time of Fabry-Perot cavities = Fabry-Perot Michelson Interferometer
Basic form of the modern interferometer GW detector

## Slide 21: Optical Recycling Technique
Power recycling
  Place a mirror in front of the interferometer to form a cavity with the Michelson (compound mirror) “Power Recycling Mirror”
  The internal light power is increased = equivalent to the increase of the input laser power
compound mirror

## Slide 22: Optical Recycling Technique
Power-recycled Fabry-Perot Michelson Interferometer
  Internal light power in the arms is increased
From the laser side /
common arm length change
It looks like a three mirror caivty
= high finesse cavity
For the differential motion (=GW)
It looks like just an arm cavity

## Slide 23: Optical Recycling Technique
Common mode
= high finesse three mirror cavity
Differential mode (=GW)
= low (or high) finesse three mirror cavity
Dual-recycled Fabry-Perot Michelson Interferometer
  Another mirror is added at the dark port “Signal Recycling Mirror”
  Dual recycling allows us to set different storage times for common and differential modes

## Slide 24: To tuned or not to tune
Bandwidth of the detector can be changed
  by changing the resonant phase of the signal recycling cavity (SRC)
Optimize the curve depending on the noise shape
Dynamic signal tracking
Signals: resonant in SRC
(Resonant Sideband Extraction)
Signals: anti-resonant in SRC
(Signal Recycling)

## Slide 25: Summary
Optical phase measurement => Interferometry
Michelson interferometer: requires too long arm
Fabry-Perot arm: longer light storage time
Optical recycling technique: allows us to set different storage time for the incident light and the GW signals
  Power recycling: maximize the stored light power
  Resonant sideband extraction: optimize the signal bandwidth