## Slide 1
Veronica Leccese, Dr. Dooley Research Group
LITTLE PRE-MODE CLEANER
&
TILT-FREE SEISMOMETER

## Slide 2
Outline
Laser beam and its instability
Solution: PMC
Little PMC building
Future work
Little Pre-Mode Cleaner (PMC)
Tilt-free seismometer
Seismic noise in LIGO: solutions
Tilt-to-translation coupling and tilt-free sismometer
Tilt injection: current driver
Future work

## Slide 3
LITTLE PRE-MODE CLEANER

## Slide 4
Gaussian beam is a beam of monochromatic electromagnetic radiation whose transverse magnetic and electric field amplitude profiles are given by the Gaussian function; this also implies a Gaussian intensity profile.
Laser emission: Gaussian beam
Gaussian beams and the higher-order Gaussian modes are solutions to the wave equation for an electromagnetic field in free space or in a homogeneous dielectric medium:

## Slide 5
is the radius at the plane z
is the radius of curvature of the
beam’s wavefront
is Gouy phase shift
The electric field of the fundamental transverse Gaussian mode ( TEM00) is:
where
is the Rayleigh length

## Slide 6
TEM00 describes the intended output of most lasers, as such a beam can be focused into the most concentrated spot
Problem:
the electric field of the laser beam cannot be described only by the one of TEM00 because of the presence of higher-trasversal modes.
Wikipedia

## Slide 7
Instability of the laser beam
Spatial instability, known as beam jitter, is due to the mixing of higher order modes with the fundamental mode (TEM00).
Amplitude and phase fluctuations are created by beam jitter whenever the beam interacts with a spatially sensitive element such as an optical cavity
Frequency instability
NOISE SOURCES

## Slide 8
Solution: Pre-Mode Cleaner (PMC)
It’s a triangular ring cavity

## Slide 9
Only the fundamental mode is resonant – hence ‘Mode cleaner’ - and the higher order modes, having different cavity eigen frequencies, are attenuated or suppressed.
Transmission =
where
is the difference in frequency between any higher order mode TEMmn and the fundamental mode TEM00
is the finesse of the cavity

## Slide 10
Building a Little PMC
What do we need?
A spacer
Two clamps and an endcup
Two flat mirrors and a curved mirror
Piezoelectric transducer (PZT)
A base
DCC E1400332-v1

## Slide 11
Jig

## Slide 13
Set up for testing the Little PMC
z

## Slide 14
Mode matching
How much is the waist of the beam?

## Slide 15
Measuring the beam size

## Slide 17
3.3±0.5 | 0.90±0.05
5.8±0.5 | 0.53±0.04
9.6±0.5 | 0.049±0.003
13.3±0.5 | 0.56±0.04
18.5±0.5 | 1.18±0.06
23±0.5 | 1.83±0.06
34±0.5 | 3.58±0.08
3.3±0.5 | 0.90±0.05
5.8±0.5 | 0.53±0.04
9.6±0.5 | 0.049±0.003
13.3±0.5 | 0.56±0.04
18.5±0.5 | 1.18±0.06
23±0.5 | 1.83±0.06
34±0.5 | 3.58±0.08
from the lens

## Slide 18
Choise of lenses
where
and

## Slide 19
Future work
Gluing the PZT to the mirror and the mirror on the endcup
Driver for the PZT
Lock the PMC
Characterize the PMC (i.e. measure the mode matching and the transmission)
Use the cavity in optic experiments (e.g. squeezed light)

## Slide 20
TILT-FREE SEISMOMETER

## Slide 21
Seismic noise in LIGO: solutions
Seismic noise due to vibration of the laboratory is a low frequency limit for the interferometer in LIGO
Active isolation
Passive isolation
Multiple stages platforms separated by spring assembly for the optics and suspension of the optics themselves

## Slide 22
Active isolation problem: tilt-to-translation coupling
At low frequency (< 40 mHz) the seismometer signals are too contaminated by ground tilt to be used for active control

## Slide 23
Two different approches
Measuring tilt
Independently measure ground tilt and subtract it
Filtering tilt
Mechanically filter tilt
Suspended structure

## Slide 24
Tilt-free seismometer

## Slide 25
Above the tilt resonant frequency: ‘tilt-free’
Below the pendulum resonant frequency: the suspended platform motion follows ground translation
Between the tilt and pendulum frequencies: good translation sensitivity of the suspended seismometer
F. Matichard, DCC P1400060

## Slide 27
Tilt injection: current driver for the coil

## Slide 29
Future work
Test the circuit with the coil
Solder components to breadboard
Measurement of the tilt to displacement transfer function

## Slide 30
Acknowledgments
Dr. Kate Dooley
Dr. Marco Cavaglià
Dr. Antonio Perreca
Dr. Lucien Cremaldi
Dr. Giancarlo Cella
Mohammad Afrough
Camillo Cocchieri
INFN, NSF and LIGO
Thank you for your attention!