## Slide 1: FUTURE LASER INTERFEROMETER GRAVITATIONAL WAVE OBSERVATORIES & VACUUM REQUIREMENTS
Chandra Romel, LIGO Hanford Caltech
AVS 66th International Symposium & Exhibition
Columbus, OH
20-25 October, 2019
LIGO-G1901913
Image Credit: Aurore Simmonet/SSU

## Slide 2
- Existing Gravitational Wave Observatories
- Vacuum Requirements
- 3G Gravitational Wave Observatories
- Technologies for 3G Large Vacuum
- Path Forward
Topics

## Slide 3
Gravity & Curved Space-time

## Slide 4: Gravitational Waves
Credit: LIGO/Tim Pyle

## Slide 5
Typical Interferometer

## Slide 6
LIGO’s Crown Jewels

## Slide 8: Global GW Detector Network

## Slide 9
A “Small” Problem
A wave’s strength is measured by the strain induced in the detector,
We can calculate expected strain at Earth;
If we make our interferometer arms 4,000 meters long,
!!
A ten-thousandth the size of an atomic nucleus

## Slide 10
The Enemies: NOISE

## Slide 11
Vacuum Requirements
Brownian noise due to gas impact
    Exacerbated by small gaps
      P(H2) < 10-8 Torr
Contamination of optics
    Mirror absorption budget: < 0.1 ppm change
    over operating life
    Hydrocarbons: < 1 monolayer/10 years
    Particles: < one 10 µm particle on any mirror
Light scattering phase noise from residual gas
    A function of molecular polarizability and
    thermal speed
    Primary goals for beam tubes:
      P(H2) < 10-9 Torr
      P(H2O) < 10-10 Torr

## Slide 12
Vacuum Equipment
Chambers, pumps, instruments-
“Vacuum Equipment”
  Houses detector apparatus
  Isolation (valves), access (doors)
  Electrical, mechanical, optical penetrations/interfaces
  Pumping & instrumentation
  Somewhat “conventional”
  F:A ~ 10-2 ls-1cm-2
Beam tubes
  Just a long hole in the air;
      Never to be vented
  Highly “unconventional”
    10 million liters (per site)
    300 million cm2 (per site)
    200 l/s char. conductance
  F:A ~ 10-5 ls-1cm-2
LIGO is Really Two Vacuum Systems (at each site)

## Slide 13
LIGO Vacuum Equipment, LHO Corner Station

## Slide 14: Pumping for Non-Condensibles
Maglev turbos for initial evacuation only
Ion pumps assisted by NEGs in normal operation
NO rotating or vibrating machinery allowed during interferometer operation

## Slide 15: A+ Upgrade
1.7x distance ~ 5x volume

## Slide 16: Sensitivity
Courtesy of E. Hall, LIGO MIT

## Slide 17: Future Gravitational Wave Detectors

## Slide 18: Einstein Telescope www.et-gw.eu

## Slide 19: Cosmic Explorer www.cosmicexplorer.org

## Slide 20: What is Cosmic Explorer?
40 km L-shaped facility on the Earth’s surface
2030s: room-temperature glass detector
2040s: cryogenic silicon detector
Collaborating institutions in the US:
Caltech: R. Adhikari, Y. Chen1; Cal State Fullerton: G. Lovelace1, J. Read, J. Smith; Penn State: B. Sathyaprakash1; Syracuse: S. Ballmer1, D. Brown; MIT: M. Evans1,2, S. Vitale
Three-year horizon study funded by the NSF, 2018–2021
1PI
2Lead PI

## Slide 21: CE Vacuum Requirements

## Slide 22: Blue Sky Large Vacuum Workshop
Goal: examine vacuum design concepts & technologies to aid detailed design & engineering studies of CE and ET
Held at LIGO Livingston on January 29-31, 2019
38 attendees, organized by H.F. Dylla, R. Weiss, M.E. Zucker
Sponsored by NSF & Caltech/MIT LIGO Lab
Proceedings available @ https://dcc.ligo.org/LIGO-P1900072/public

## Slide 23: Working Groups
Conventional single-wall vacuum systems
  - Cost reduction options of single wall beamtube technology and material options
Non-conventional vacuum technology
  - Cost reduction options including nested vacuum tubes with thin, bakeable UHV shell inside robust outer wall
Novel surface treatment for conventional and UHV materials
  - Surface modifications and coatings to meet UHV and optical requirements
Vacuum pumping for conventional and nested systems
  - Pumping schemes and scenarios for obtaining UHV for both conventional single wall and nested differential pressures

## Slide 24: WG1: Single Wall Beamtube
Material evaluation
  304L SS well understood
  Al offers low H2 outgassing and relatively low cost; dissimilar metal welding a challenge –~4000 bellows w/40 mm stroke for 120C bake
  Mild steel lower cost alternative offering low H2 outgassing through Ruhrstahl-Hausen processing1
Fabrication Techniques
  Spiral vs longitudinal welding
  Seamless and Al extrusion
  Explosion bonding vs hot isostatic pressing
  vs adhesive bonded transition
Surface & Bakeout
  Reflective surface bad; smooth surface good
  100C bakeout via iterative traveling ‘hot tent’ and ppb ultra dry viscous air flow – no isolation valves needed
  1Chongdo Park, et. al., J. Vac. Sci. Technol. A 34(2), 021601-1 2016
LIGO Beamtube
9000 m3 volume/site
30000 m2 area/site
50 km of spiral welds
~10-9 torr
budget ~ $40M (1997)
$2500/m
$50/lb
  Figure courtesy of C. Baffes, FNAL
Co-chairs: C. Baffes (FNAL) and D. Henkel (Rimkus Consulting Group, Inc.)

## Slide 25: WG2: Nested Beamtube
Nested design conceived by R. Weiss
Concentric tubes
  Thin, bakeable inner shell ½-1.5 mm thick Al with vibration dampening
  Robust outer tube holds rough to HV; mild steel or FRP
  Sealed or shared volumes
  Annulus or soft sealing valves/shutters
Co-chairs: J. Noonan (ANL) and D. Manos (William and Mary)

## Slide 26: WG3: Novel Surface Treatments
1 μm TiN coating on SS to minimize water adsorption1
Vacuum degassing at foundry reduces H2 in mild steel2
Magnetite (Fe3O4) on mild steel to prevent corrosion
Electrochemical conversion for low-reflection surface (blue/black surface)
Diamond-like carbon (DLC) coating
Amorphous silicon (a-Si)
UV light sources and ozone considered
Dry purge cleaning and “cycle purge” method
NIST will perform outgassing measurements using SRG technique of mild steel and TiN, DLC coated chambers
Co-chairs: J. Fedchak (NIST) and J. Feicht (LIGO)
  1Y. Saito, et. al., Vacuum 53, 353 (1999)
  2C. Park, et. al., JVST A34, 021601 (2016)

## Slide 27: WG4: Pumping
40 km sectored into 10 km segments for independent pump down
10 km segments reduced to 2 km sections for installation intervals and bake out
Automated venting for nested system to avoid buckling
Rough to 10-2 Torr  turbo to 10-5 Torr  cryopumps or ZAO NEG+IP to trap H20 during bake
Ne-He cryo cycles to condense N2, O2, Ar
Ti sublimation pumping for distributed getter pumping
Pump interval ~ 250 m during bake and 1000 l/s per 1 km during operation
Pressure gauges every 100-250 m to localize leaks
Co-chairs: Y. Li (Cornell) and P. Chiggiato (CERN)
Data courtesy of SAES

## Slide 28: Path Forward
Carry out single wall and nested beamtube concepts to next level of detailed design, engineering, and cost studies
Consider mild steel alloys and Al in addition to SS, detailing surface treatment, coatings, and material transitions
Study best options for outer vessel material in nested system
Quantify TiN, DLC, a-Si, Fe3O4 coating effectiveness for H20 adsorption, scale and particulate, welding interference, and optical characterization
Collaborate with NIST, Jlab, and CERN on outgassing studies
Follow-up workshop is planned for April 2020 at CERN:
  Research agenda layout for short-term R&D to quantify cost-benefit of material choices and surface treatments identified

## Slide 29: Acknowledgements
Thank you to the US National Science Foundation
award PHY-1846124
Thank you to all attendees of the Large Vacuum Workshop. Special thanks to F. Dylla, R. Weiss, M. Zucker for organizing, and to co-chairs for leading working groups and composing reports.

## Slide 30
THANK YOU