## Slide 1: Non-Linear Noise Subtraction for Low Frequency
Final Presentation for LIGO SURF 2021 August 19, 2021
Student: Yuka Lin
Mentor: Dr. Gabriele Vajente

## Slide 2: Outline
Motivation
NonSENS Algorithm
Results
Questions

## Slide 3: Motivation

## Slide 4: Core-Collapse Supernovae
when a massive star reaches the end of its lifespan and experiences rapid collapse
in an event such as a galactic supernova, a fraction of the GW memory might be able to be detected above the noise floor
  GW “memory” is permanent deformation of spacetime in the LOW FREQUENCY range of the signal
GW memory emission of CCSN’s can peak below ~10 Hz
  has the center frequency around 2Hz but it has tails that survive up to 40Hz and that can be above the current LIGO noise for a galactic SN

## Slide 5: NonSENS Algorithm
Non-Stationary Estimation of Noise Subtraction
Original application of the algorithm used for subtraction in frequency ranges over 10 Hz
Now we want to modify the algorithm to perform similar noise reductions under 10 Hz
Project Goal: reduce the noise in the range where the GW memory is relevant for a CCSN
https://alog.ligo-wa.caltech.edu/aLOG/index.php?callRep=57423

## Slide 6: NonSENS Algorithm

## Slide 7: NonSENS Algorithm
= Gravitational Waves signal
= “fast” noise witness
= “slow” modulation noise witness
= non-linear noise coupling
= linear noise coupling
Non-linear
Linear
Was created to reduce the noise that are coupled non-linearly and non-stationary in a strain signal
  Noise “couples” or leak into main signal; limits sensitivity of detectors
  Noise coupling – physical process of adding some noise sources to the GW output

## Slide 8: What is the non-Linear subtraction?
In the linear and stationary subtraction, the noise that is witnessed by some auxiliary channel will couple to the strain
In the non-stationary case, the coupling is modulated (In other words, the effects of the noise in the strain contains non-stationary characteristics)
Where:

## Slide 9: Auxiliary Channels
ast noise witnesses contains content in the higher frequency band (1-10 Hz)
, slow modulation witness contains content in the lower frequency band (below 1 Hz)
Auxiliary channel – time series data recorded by the detector; monitors detector behavior and environment

## Slide 10: Subtraction
The modulated signals are coupled with the non-stationary transfer function
Then:
Purpose of algorithm is to find the best parameters that will reduce the maximum amount of noise from the target strain as possible; the algorithm then will perform a prediction of the most optimal subtraction possible

## Slide 11: Results

## Slide 12: Results:
Step 1) Linear Coherence:
https://ldas-jobs.ligo.caltech.edu/~gabriele.vajente/bruco_lf_2021_06_22/
Coherence
Frequency [Hz]
Linear coherence describes the correlation between the two signals in the frequency domain.

## Slide 13: Results:
Step 2) Picking fast noise witness channels that perform the best linear subtraction
Subsystems:
ASC - Alignment Sensing and Control
SUS – Suspension
Mirror Identifiers:
SRM – Signal Recycling Mirrors
ZM2 – 2nd Squeezer Mirror
M1, M3 – Suspension levels
Signal Identifiers:
DSOFT – differential control arms (soft)
DHARD – different control arms (hard)
X_TR – transmission to X arm
Some naming convention for channels:

## Slide 14: Results:
Step 3) Try non-stationary subtraction by adding “slow” modulation channels.

## Slide 15: Results:
Time Domain Subtraction Plot:
*algorithm doesn’t always converge; no guarantee you will get an optimal solution
PSD between Target Channel H1: CAL-DELTAL_EXTERNAL_DQ and Subtracted Signals (Linear and Nonlinear Subtraction)
ASD(Hz^(-1/2))
Ratio
Frequency [Hz]

## Slide 16: Is this Result good?
Original plan was to run algorithm through all of the O3 data
  Takes a lot of time/computation
  Goal is to do more subtraction in order to be able to be effective for study at lower frequency range
  more possible channels relevant to the noise sources in the low frequency range should be assessed – mainly only the SUS and ASC channels were found in this project
Continuation of project 

## Slide 17: Acknowledgements
A special thanks to:
  Dr. Gabriele Vajente (mentor)
  LIGO Summer Undergraduate Research Fellowship
  Research Experiences for Undergraduates (REU) Program of the National Science Foundation

## Slide 18
Thank you for listening!
Any Questions?
Contact: liny10@my.erau.edu

## Slide 19: Linear/Nonlinear System
Homogeneity
Additivity
Shift Invariance
Linear and Time Invariant System
System – process in which an output signal is produced as a result of the response to an input signal

## Slide 20: Linear and Time Invariant System
Properties:
Additivity
Homogeneity
Shift Invariance

## Slide 21: “Target” Strain Channel (Supplemental)
The target channel is the channel that we want to subtract the noise from
For this project, utilize: CAL-DELTAL_EXTERNAL_DQ
  produces the calibrated strain signals that are corrected below 10 Hz
  Advantage: the only channel currently that contains calibrated strain below 10 Hz.
  Disadvantage: less accuracy than the GDS-CALIB_STRAIN channel, which was the target channel that was originally used for subtracting noise between 10 and 30 Hz

## Slide 22: (supplemental) Results:
Contribution plot:

## Slide 23: (supplemental) Results:
Optimized parameter is the minimum value that is calculated by the cost function
Algorithm doesn’t always converge
Cost Function:

## Slide 24: (Supplemental) Modulated Signals