## Slide 1
LIGO: Using Quantum-Enhanced Interferometry to Observe the Most Energetic Events in the Universe
David Reitze
LIGO Laboratory
California Institute of Technology
Image Credit: Aurore Simmonet/LIGO-Virgo/Sonoma State Univ.
LIGO-G2201708-v2
NASA Quantum Sensing Workshop, Newport News, VA, Sept 29, 2022
Notes: Thanks for the opportunity to speak about the recent GW discoveries and the role that large scientific collaborations played.

## Slide 2
Overview
Gravitational Waves and Precision Interferometry for Gravitational-wave Detection…
… Enabling the Recent Gravitational-wave Astrophysics Revolution
In-depth Precision Interferometry: Understanding Noises
Quantum-engineered ‘Squeezed’ Light for LIGO: Beyond Shot Noise and Fundamental Radiation Pressure
New Horizons in Sub-quantum-limited Sensing with LIGO
Next Generation GW Observatories

## Slide 3
Einstein’s General Theory of Relativity (1915)  ‘Ripples in Space-time’ (1918)
Any accelerating massive object generates gravitational waves…
... but the amplitude of those waves is exceedingly tiny.
Gravitational Waves
L
Two merging black holes
Matter/Energy
Space/Time
~ 10-43 !!
Physically, amplitude DL/L ~ 10-21
Gravitational waves:
- are produced with detectable amplitudes by the most violent astrophysical events in the universe
- travel at the speed of light
- travel unimpeded through matter
- carry direct information about the relativistic motion of bulk matter
- propagate with amplitudes that fall off as 1/distance; they are ‘standard sirens’
Notes: GR in one slide. Start w/ field equations “space = time’ then move to GWs. Might point out that Einstein flipped flopped on GWs. Also point out that he thought them an esoteric consequence with no physical relevance. Play video. Talk about physical effect. Show coupling constant and strain

## Slide 4: Precision Gravitational-wave Interferometry
GW interferometers use enhanced Michelson interferometry
  With suspended (‘freely falling’) mirrors
Passing GWs stretch and compress the distance between the end test mass and the beam splitter
The interferometer acts as a transducer, turning GWs into photocurrent
  A coherent detector!
Amplitude
Time
Output
LIGO Hanford Observatory,
Washington
LIGO Livingston Observatory
Louisiana
Notes: At end of slide “Let’s examine some history”

## Slide 5: Gravitational-wave Astrophysics
Gravitational waves reveal information about the most violent and highest energy events in the Universe
Credit: Chandra X-ray Observatory
Credit: Casey Reed, Penn State
Merging Binary Systems
The Stochastic Gravitational
Wave Background
Spinning Neutron Stars
Exploding Stars
Credit: Bohn, Hébert, Throwe, SXS
Black hole – black hole
Black hole – neutron star
Neutron star – neutron star
White dwarf binaries
Credit: Planck Collaboration
Asymmetric core collapse supernovae
Neutron stars possessing ellipticity
Incoherent sum of unresolved astrophysical ‘point’ sources
Primordial GWs from the Big Bang
And possibly dark matter, dark energy, and yet to be discovered objects!

## Slide 6
2001
2007
2001
2001
2019
~ 2028-2030

## Slide 7: The Gravitational-Wave Universe Revealed to Date
The First Detection:
Binary Black Hole Merger
Sept 14, 2015
Multi-messenger Astronomy
Binary Neutron Star Merger
Aug 17, 2017
Gravitational Waves
Gamma Rays
Optical (Hubble Telescope)

## Slide 8: Recent LIGO-Virgo-KAGRA Science Highlights I
qw
2016
2020
Calendar Time
?
?
?
?

## Slide 9
Gravitational waves from astrophysical sources can be directly measured!
Astrophysics: Binary black hole (BBH) systems exist.
Astrophysics: Binary neutron stars (BNS) are progenitors of short gamma ray bursts.
Astrophysics: BNS mergers produce kilonovae, which produce heavy elements.
Astrophysics: Black hole – neutron star binary systems exist.
Astrophysics: Compact objects exist in the 2 – 3 M⦿ mass range. We don’t know what they are…
Astrophysics: Black holes with masses in the (pulsational) pair instability gap between ~60 – 135 M⦿ exist.
General Relativity: Astrophysical black holes are Kerr black holes as predicted by GR.
General Relativity: The speed of gravitational waves equals the speed of light.
General Relativity: GR is valid in the high curvature, high field regime.
Cosmology: The Hubble constant can be measured using EM-bright GW ‘sirens’.
Cosmology: The Hubble constant can be measured using dark GW ‘sirens’.
What Ground-Based Gravitational Wave Observations Have Already Taught
Us About High Energy Astrophysics, General Relativity, and Cosmology
GW150914
GW170817/
GRB170817A
SSS17A

## Slide 10: Advanced LIGO Interferometer in More Depth
Pre-stabilized Laser
70W , 1064 nm
Active Seismic Isolation
40 kg ‘Test Mass’ Mirror
Input Optics
Output Mode Cleaner
Auxiliary Laser
140 W
100 W
3.0 kW
400 kW
4 km long Arm Cavity
Signal
Recycling
Cavity
Power Recycling
Cavity
4 km long Arm Cavity
Notes: Go through the slide from laser forward. NOTE THAT THE GW SIGNAL IS READ OUT BY INTRODUCING A ~10 pm ARMLENGTH OFFSET. THE STATIC DC FIELD IS MODULATED BY THE DIFFERENTIAL ARM LENGTH INDUCED BY THE PASSING GW.

## Slide 11: Advanced LIGO Sensitivity

## Slide 12
Displacement noises (DLarm) shake the mirrors
  seismic perturbations
  quantum noise: photon pressure
  thermal noise (suspensions, mirror
  substrates, mirror coatings)
Sensing noises (Dtphoton) alter the arrival time of the light at the output photodetector
    quantum noise: photon arrival times
    presence of residual gas
(There are also hundreds of sources of technical noise that must be understood and eliminated)
Measurement Noises

## Slide 13
Quantum noise (high freq.):
photon arrival times 1/ Laser
Quantum noise (low freq.):
photon pressure Laser
Displacement noises (DLarm) shake mirrors
  seismic perturbations
  quantum noise: photon pressure
  thermal noise (suspensions, mirror
  substrates, mirror coatings)
Sensing noises (Dtphoton) alter the arrival time of the light
    quantum noise: photon arrival times
    presence of residual gas
(There are also hundreds of sources of technical noise that must be understood and eliminated)
Total noise
Measurement Noises

## Slide 14: Coupled Quantum “Optical Readout” Noise
M = 40 kg
P = 103 W
Quantum Noise in Interferometers

## Slide 15: Coupled Quantum “Optical Readout” Noise
M = 40 kg
P = 103 W
Quantum Noise in Interferometers

## Slide 16: Coupled Quantum “Optical Readout” Noise
M = 40 kg
P = 105 W
Quantum Noise in Interferometers

## Slide 17: Coupled Quantum “Optical Readout” Noise
M = 40 kg
P = 107 W
M = 40 kg
P = 107 W
Quantum Noise in Interferometers

## Slide 18: Coupled Quantum “Optical Readout” Noise
M = 40 kg
Quantum Noise in Interferometers

## Slide 19: Coupled Quantum “Optical Readout” Noise
M = 400 kg
Quantum Noise in Interferometers

## Slide 20: Suppressing Quantum Noise
Amplitude squeezing
Phase
squeezing
Coherent State
ϕ
│E │
Vacuum State
Squeezed
vacuum
Electromagnetic fields are quantized:
Quantum fluctuations exist in the vacuum state:

## Slide 21: Controlling Quantum Noise in Interferometers
Photodiode
Main Laser
x1
x2
Photodiode
Faraday
Isolator
Squeezed Vacuum
Source
Main Laser
PLL
x1
x2
Vacuum noise naturally enters through the asymmetric (dark) port of the interferometer
Asymmetric port
Symmetric port
J. Aasi, et al. (LIGO Scientific Collaboration), Nature Phot. 7, 613-619 (2013).
Squeezed vacuum can be injected to
suppress shot noise

## Slide 22: Shot Noise Suppression in the LIGO Interferometers
Frequency Independent Squeezing:
Experimental implementation at LIGO
Shot Noise
2 dB squeezing
Binary Neutron Star Range
34% increase in
rate of detected
binary neutron stars

## Slide 23: Beyond the Standard Quantum Limit: Radiation Pressure Suppression
Ponderomotive Squeezing: the interferometer introduces correlations between the position/ momentum uncertainty of the mirrors and the photon number/phase uncertainty
By varying the squeezed quadrature field (phase) and subtracting off the classical noise, the QPR noise can be reduced below the SQL
Yu, et al., “Quantum correlations between light and the kilogram-mass mirrors of LIGO” Natiure 583, 43-54 (2020).
Squeeze
angle f

## Slide 24: Frequency Dependent Squeezing
wqe
Oelker, et al., “Audio-band Frequency-dependent Squeezing”, Phys. Rev. Lett. 116, 041102 (2016).
L. McCuller, et al., “Frequency-Dependent Squeezing for Advanced LIGO”, Phys. Rev. Lett. 124, 171102 (2020).
Y. Zhao, et al., “Improving the stability of frequency-dependent squeezing with bichromatic control of filter cavity length, alignment, and incident beam pointing”, Phys. Rev. D 105, 082003 (2022).
Squeezed Light Response to Filter Cavity
Demonstration on a 16 m suspended cavity
at the MIT LIGO Advanced System Test Interferometer
Demonstration on a 300 m suspended cavity
at the Virgo European Gravitational-Wave Observatory

## Slide 25: What’s Next for LIGO
Implementation frequency-dependent squeezing in the next LIGO-Virgo-KAGRA O4 Observing Run
Improvements in the test mass mirror coatings to reduce thermal noise to be deployed for the O5 Observing Run in 2025
300 m
Filter Cavity
Filter Cavity
End Station
Major Facility
Improvements

## Slide 26
Next Generation GW Observatory Projects in Europe and the US are gaining significant momentum
  Einstein Telescope (ET) in Europe
  Cosmic Explorer (CE) in the US
ET and CE will observe compact GW events to the edge of the star-forming universe as a global network
Gravitational Wave Observatories in the 2030s & 2040s:
Global Scale Detector Networks
US: Cosmic Explorer
Europe: Einstein Telescope
US: Cosmic Explorer
40 km arm lengths
10 km arm lengths

## Slide 27
ET Design: underground, triangular, 3 detectors consisting of two interferometers (high frequency + low frequency ‘xylophone’)
  Cryogenic test masses, longer wavelengths for LF operation
  Underground infrastructure designed for future upgrades
Possible sites:
  Euregio Meuse-Rhine
  Sardinia, Italy
  (possibly) Saxony, Germany
Current envisioned timeframe:
  Construction to begin in 2026
  Science operations to begin in 2035
Status:
  ET is a fully recognized European Project on European Strategy Forum for Research Infrastructures (ESFRI) Roadmap  a key step in getting the project funding lined up.
  ET Project Organization and relevant Boards have been established
  ET Pathfinder facility in Maastricht, Netherlands under construction
  Site evaluation well underway
Einstein Telescope

## Slide 28
Detector Design: one 40 km and one 20 km L-shaped surface observatories
  Detector technology based on scaling up existing LIGO interferometer technology
Possible sites:
  No specific sites identified, however a trade study has identified candidate sites in NW and SW United States
Current envisioned timeframe:
  Construction to begin in 2029
  Science operations to begin in ~ 2037
Status:
  CE Horizon Study released in October 2022
  Currently developing proposal to enter NSF ‘Conceptual Design’ phase  this is a key step to secure construction funding
  R&D on development new lower cost ultrahigh vacuum systems underway
Cosmic Explorer
CE Design
Concept

## Slide 29
The first three Advanced Detector observing runs have been a smashing success!
Upgrades are progressing toward O4 run to begin in December 2022.
Detailed plans for detector upgrades for O5 are in hand; O5 run plan coming into focus.
Planning for O6, O7, … which will carry us into the next decade are underway.
Later in the 2030s: Einstein Telescope and Cosmic Explorer will probe the compact GW sources to the nearly edge of the Universe
Conclusions
Acknowledgments:

## Slide 30
Force  Displacement
Transfer Function
Model vs. Measured
Concept:
Harmonic
Oscillator
Implementation:
Upper ‘ear’
Lower ‘ear’
Collaboration w/ U. Glasgow
4 Stage Transfer Function
Seismic Isolation

## Slide 31
Force  Displacement
Transfer Function
Model vs. Measured
Concept:
Harmonic
Oscillator
Implementation:
Upper ‘ear’
Lower ‘ear’
Collaboration w/ U. Glasgow
4 Stage Transfer Function
Seismic Isolation

## Slide 32: Beyond the Standard Quantum Limit: Quantum Radiation Pressure Suppression
Diff. displacement spectral density:
Ponderomotive coupling:
Squeeze factor:
frequency-dependent interaction between ponderomotive and injected squeezing
{
{
1) Yu, et al., “Quantum correlations between light and the kilogram-mass mirrors of LIGO” Natiure 583, 43-54 (2020).
2) A. Buonanno, A. & Y. Chen, “Quantum noise in second generation, signal-recycled laser interferometric gravitational-wave detectors” Phys. Rev. D 64, 042006 (2001).
3) H. J. Kimble, et al., "Conversion of
conventional gravitational-wave interferometers into quantum nondemolition interferometers by modifying their input and/or output optics", Phys. Rev. D 65, 022002 (2001).

## Slide 33: Squeezing & Anti-squeezing
Coherent State
ϕ
│E │
Amplitude squeezing
Phase Anti-squeezing
Phase
Squeezing
Amplitude Anti-squeezing

## Slide 34
Advanced LIGO Test Mass Coatings
  Ion-beam sputtered (IBS) amorphous (almost) ¼ wave dielectric stack
    TiO2:Ta2O5 (nh = 2.07) & SiO2 (nL = 1.45)
Statistical Mechanics: kT of energy per mechanical mode, viscous damping
Slide inspiration:
Marty Fejer, Stanford
Compare: Bulk Silica f ~ 10-6-10-8
Y. Levin Phys. Rev. D 57 659 (1998); Harry, G.M., et al.m Class. Quantum Gravity 19 (5), 897.
beam radius
coating thickness
coating
elastic loss
Young’s modulus, coating
Measurement
Band
Loss Angle:
High Q (GOOD)
nh
nL
nL
nL
nL
nL
nL
nh
nh
nh
nh
nh
Low Q (BAD)
Coating Thermal Noise