## Slide 1: Update on LIGO instruments OpenLVKEM town hall, 13 April 2023
P. Fritschel, LIGO Lab, M.I.T.
LIGO-G2300838-v1

## Slide 2: LIGO Interferometer Status
3000 km (10 ms)
H1
Frequency Dependent Squeezing operational
Much effort on achieving stability at high power (thermal compensation, alignment control, parametric instabilities)
Continued investigations of technical noises
H1 & L1
Significant periods of undisturbed running, useful for testing.
L1
Frequency Dependent Squeezing operational
Laser power increase
Mid-frequency noise is elevated compared to a year ago (10%) – cause unknown

## Slide 3: Summary of LIGO Improvement Goals
 | Hanford, H1 |  | Livingston, L1 | 
400 kW circulating arm power | ✓(440 kW) |  | 300 kW | 
Squeezed light efficacy 4.5 dB | ✓ | 4.5 dB | ✓ | 5.8 dB
300 m filter cavity for frequency-dependent squeezing | Automation in progress |  | Automation in progress | 
Low frequency technical noise reduction (f < 100 Hz) | ✓ work continues |  | ✓ work continues | 
Binary Neutron Star inspiral detection range: 160-190 Mpc | 145 Mpc |  | 150 Mpc | 

## Slide 4: BNS range over 24 hrs (earlier this week) still in commissioning mode

## Slide 5: Frequency Dependent Squeezing: H1 and L1
Hanford
Livingston