## Slide 1: University of Washington Seattle Eöt-Wash Group Overview
GWANW 2023
Michael Ross

## Slide 2: CENPA – Center for Experimental Nuclear Physics and Astrophysics

## Slide 3: Eöt-Wash Group
Jens Gundlach (Professor)
Erik Shaw (Postdoc)
Shoshana Apple
(Grad student)
Michael Ross
(Postdoc)
Conner Gettings
(Postdoc)
Yasin Chowdhury
(Undergrad. RA)
Peter Wu
(Undergrad. RA)

## Slide 4: Torsion Balance Experiments
Testing gravity since the 1980s
We use torsion balances to:
  Test gravity’s short-range behavior
  Verify the equivalence principle (EP)
  Search for ultra-light dark matter
  Measure gravitational constant, G
Recent Results:
  Test of short-range gravity at separations of 52 μm: arxiv.org/abs/2002.11761
  Search for atto-eV ( mass dark matter: https://arxiv.org/abs/2109.08822
On-going/Soon to be released:
  Upgraded EP test
  Test of EP for Cooper pairs (

## Slide 5: Rotation Sensors
Developed beam-balance based rotation sensors (rotational seismometers)
Proof-mass suspended from 10-15 μm thick Be-Cu flexures forms rotational spring-mass system
Three versions:
  Beam Rotation Sensors (BRS): 1-m long beam, used to sense ground rotation for seismic isolation systems, 6 deployed at LIGO (LHO: 2, LLO: 4)
  compact Beam Rotation Sensor (cBRS): 30-cm wide cross, installed on Stanford ETF ISI
  Cylindrical Rotation Sensor (CRS): In development, 30-cm diam. cylinder, HoQI readouts, to be installed on ISI
BRS
cBRS
CRS

## Slide 6: Newtonian Calibrator
“New” way to calibrate LIGO
Injects forces on the test mass with gravity instead of photon pressure
Aluminum rotor with tungsten slugs inserted into it injects at two times and three times the rotation rate
Successfully injected forces during LIGO’s third observing run
Initial Results yielded ~1% absolute calibration: https://arxiv.org/abs/2107.00141
New design expected to reach ~0.1% uncertainty: P2200021

## Slide 7: Thanks