## Slide 1: Environmental noise lessons from LIGO for CE site selection

## Slide 3
Imagine looking down on an array of objects, with a gravitational wave coming in from above (out of the page)

## Slide 20
Rai Weiss

## Slide 21: The two things we had to do to detect gravitational waves
Quiet the motion of the test masses so that they are moving less than about 1e-19 m, so that the motion produced by gravitational waves is not swamped by other motion
Measure the tiny relative motion between test masses

## Slide 22: 1) Quiet the motion of the mirrors to about 1e-19 m at certain frequencies

## Slide 24: 2) Measure the tiny distances: interferometers are the best at measuring small differences in distance

## Slide 26
Frequency band | Dominant Noise Source | How it can hurt GW detectors | Coupling
1/day | Earth tides | Changes distance between buildings | Stronger actuators are noisier. Higher velocity between buildings can make main laser light “mimic” GWs (scattered light noise.
Around 0.1 Hz | Ocean waves: microseismic peak | Same as above and also some relative motion within buildings. | Same as above: scattered light noise is one of the worst non-fundamental noise sources.
0.1 – 10 Hz and above | Wind | Shakes buildings, tilts ground | More motion gets through isolation, moving optics, and scattered light noise, also direct Newtonian coupling to TMs
1-30 Hz | Anthropogenic noise Trains, trucks, cars, OHVs, construction equipment, wind farms, dams | Motion within a building | Moving test masses and other optics, and scattered light noise, also direct Newtonian coupling to TMs
30 Hz to 7000 Hz | On site sources, HVAC, motors, people | Same as above | Same as above
Seismic

## Slide 27
Frequency band | Dominant Noise Source | How it can hurt GW detectors | Coupling
1–1000 Hz and up | Electric currents | magnetic coupling moves optics and other components | Actuation permanent magnets and magnetized components
1-1000 Hz and up but increasing with frequency | Electric currents | Induced currents add noise, mainly to analog signals | Electronic components and cables
Magnetic

## Slide 29
2 km

## Slide 34
6 km

## Slide 36
10 km

## Slide 37
1-3 Hz band

## Slide 41
20 km
20 km

## Slide 42
50 km

## Slide 43
60 km

## Slide 47
2 km

## Slide 49
Suggested day-scale instrumented site evaluation
Will not deal with earth tides, microseismic peak, wind driven seismicity that vary on week scales and greater
Focus on local sources that are present daily but may not be captured by seismic maps and other external sources.
Use imperfect but nimble setups so that we can measure at multiple sites, and alter our plans in order to investigate a signal.
Focus on seismic and magnetic signals, which are the worst environmental noise for LIGO

## Slide 53
This workshop’s activities
Identify truck transients from roads around the site
Determine if the Ashe-Slatt, Ashe-Marion transmission lines are the main sources of magnetic fields and transients
Try out a nimble system where we collect data and evaluate it “in the van”
We will use a WebDAQ acquisition system that allows us to monitor spectra real-time
We will use jupyter notebooks to display the data in different ways “in the van”